CS1000

Fault Code Scanner

Mercedes-Benz

Instructions

Model Years 1988-98

| Analog/Digital Fault Code Module 1988-98 | OB15-11 |
| --- | --- |
| Transmission Fault Code Module 1990-98 | OB15-12 |

©Baum Tools Unlimited Inc. December 1, 1998

Table of Contents

SCANNER FEATURES	7

Keypad	7

Screen Symbols	7

Indicator lights	8

SECTION 1	Using the CS1000 Code Scanner	9

Diagnostic Cable	9

General Usage Notes	9

Connection Table	10

Connector Layout of Vehicle Diagnostic Connector	10

8-pole Diagnostic Connector	10

16-pole Diagnostic Connector	11

38-Pin Diagnostic Connector	12

9-Pole Diagnostic Connector (1980-94)	13

Operating the CS1000 - Mercedes Benz	14

Setting Up	14

Ignition ON or Engine at idle	14

System Selection	15

About Current, Stored and Registered Faults	15

Check Engine Light Diagnosis	16

Read Fault Codes	16

Identification/Rectification of Faults	16

Clearing Fault Codes	17

Return to System Select Function	17

MERCEDES BENZ SYSTEM TYPE AND MODEL APPLICATIONS

OB15-11 Software Cartridge	18

ANALOG FAULT CODES

ELECTRONIC DIESEL IDLE SPEED CONTROL (ELR)

201.126	1989  . . . . . . . . . . . . . . . . . . . . . . . . . . 19

ELECTRONIC DIESEL SYSTEM (EDS)

124.128	1990-91 . . . . . . . . . . . . . . . . . . . . . . . . 20

126.134   126.135	1990-91 . . . . . . . . . . . . . . . . . . . . . . . . 20

124.128	1992-93 . . . . . . . . . . . . . . . . . . . . . . . . 21

140.134	1992-93 . . . . . . . . . . . . . . . . . . . . . . . . 21

CONTINUOUS FUEL INJECTION SYSTEM (CFI)

124.026  124.030  124.050  124.090	1988-89 (California version only)	22

126.024  126.025	1988-89 (California version only)	22

201.028 (1988-93)   201.029	1988-89 (California version only)	22

107.048	1988-91 (California version only)	22

126.035  126.039  126.045	1988-91 (California version only)	22

124.026  124.030  124.090  124.230  124.290	1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 23

126.024  126.025	1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 23

201.029	1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 23

124.051  129.061	1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 25

129.066	1990-92 . . . . . . . . . . . . . . . . . . . . . . . . 25

CONTINUOUS FUEL INJECTION SYSTEM (MAS CONTROLLER)

124.026  124.030  124.090 124.230  124.290	1990-92 . . . . . . . . . . . . . . . . . . . . . . . . 27

129.066	1990-92 . . . . . . . . . . . . . . . . . . . . . . . . 27

201.029	1990-92 . . . . . . . . . . . . . . . . . . . . . . . . 27

LH SEQUENTIAL MULTIPORT FUEL INJECTION SYSTEM (LH-SFI)

| 140.032 140.057 140.076 | 1992-93 | . . . . . . . . . . . . . . . . . . . . . . . . 28 |
| --- | --- | --- |
| 124.034 124.036 | 1992-93 | . . . . . . . . . . . . . . . . . . . . . . . . 28 |
| 129.067 | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 28 |
| 140.042 140.043 140.051 | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 28 |
| HFM SEQUENTIAL MULTIPORT FUEL INJECTION SYSTEM 104 111 | 1993-97 | . . . . . . . . . . . . . . . . . . . . . . . . 30 |
| BASE MODULE (BM) 124.034 124.036 | 1992-93 | . . . . . . . . . . . . . . . . . . . . . . . . 33 |
| 129.067 | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 33 |
| 140.032 140.042 140.043 140.051 140.057 140.076 | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 33 |

DIAGNOSTIC MODULE (DM)

| 124.034 | 124.036 |  |  | 1992-93 | . . . . . . . . . . . . . . . . . . . . . . . . 34 |
| --- | --- | --- | --- | --- | --- |
| 129.067 |  |  |  | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 34 |
| 140.032 | 140.042 | 140.043 | 140.051 | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 34 |
| 140.057 | 140.076 |  |  | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 36 |
| 124.028 | 124.032 | 124.052 | 124.092 | 1994-95 | . . . . . . . . . . . . . . . . . . . . . . . . 39 |

| DISTRIBUTOR IGNITION (DI) LH-SFI |  |
| --- | --- |
| 140.032 |  | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 41 |
| 124.051 |  | 1990-93 | . . . . . . . . . . . . . . . . . . . . . . . . 43 |
| 129.061 | 129.066 |  |  | 1990-95 | . . . . . . . . . . . . . . . . . . . . . . . . 43 |
| 124.034 | 124.036 |  |  | 1992-93 | . . . . . . . . . . . . . . . . . . . . . . . . 44 |
| 129.067 | 129.076 |  |  | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 44 |
| 140.042 | 140.043 | 140.051 140.057 140.070 | 140.076 | 1992-95 | . . . . . . . . . . . . . . . . . . . . . . . . 44 |

CRUISE CONTROL/IDLE SPEED CONTROL (CC/ISC) w/o ASR

124   129   140   202	1992-97 . . . . . . . . . . . . . . . . . . . . . . . . 46

ELECTRONIC ACCELERATOR / CRUISE CONTROL / IDLE SPEED CONTROL (EA/CC/ISC) w/ASR

| 124 129 140 202 ELECTRONIC AUTOMATIC TRANSMISSION CONTROL (ETC) | 1992-97 . . . . . . . . . . . . . . . . . . . . . . . . 47 |
| --- | --- |
| 129 w/CFI | 1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 49 |
| 129 140 w/HFM-SFI | 1993-97 . . . . . . . . . . . . . . . . . . . . . . . . 50 |
| AUTOMATIC-ENGAGED FOUR-WHEEL DRIVE (4MATIC) 124.230 124.290 | 1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 51 |
| ADAPTIVE DAMPING SYSTEM (ADS) 129.061 129.066 | 1991-93 . . . . . . . . . . . . . . . . . . . . . . . . 52 |
| 129.063 129.067 129.076 | 1991-95 . . . . . . . . . . . . . . . . . . . . . . . . 53 |
| 140.032 140.042 140.051 140.057 140.070 140.076 140.134 | 1991-94 . . . . . . . . . . . . . . . . . . . . . . . . 54 |
| AUTOMATIC LOCKING DIFFERENTIAL (ASD) 124.128 | 1991-95 . . . . . . . . . . . . . . . . . . . . . . . . 55 |
| 126.134 126.135 | 1991 . . . . . . . . . . . . . . . . . . . . . . . . . . 55 |
| 129.061 | 1991-95 . . . . . . . . . . . . . . . . . . . . . . . . 55 |
| 140.134 | 1991-95 . . . . . . . . . . . . . . . . . . . . . . . . 55 |
| 201.028 | 1991-93 . . . . . . . . . . . . . . . . . . . . . . . . 55 |
| ANTI-LOCK BRAKE SYSTEM (ABS & ABS w/ASR) 140.032 140.042 140.043 140.134 | 1992-93 . . . . . . . . . . . . . . . . . . . . . . . . 56 |
| 124.034 124.036 | 1992-93 . . . . . . . . . . . . . . . . . . . . . . . . 57 |
| 140.032 140.042 140.051 140.057 140.070 140.076 | 1992-93 . . . . . . . . . . . . . . . . . . . . . . . . 57 |
| 202 210 | 1994-95 . . . . . . . . . . . . . . . . . . . . . . . . 59 |
| 124.034 | 1994-95 . . . . . . . . . . . . . . . . . . . . . . . . 60 |
| 129 | 1994-95 . . . . . . . . . . . . . . . . . . . . . . . . 60 |
| 140 | 1994-95 . . . . . . . . . . . . . . . . . . . . . . . . 60 |

| 1. |  | ELECTRONIC TRACTION SYSTEMS (ASR, ETS) |
| --- | --- | --- |
| 129 | 140 202 | 1995 . . . . . . . . . . . . . . . . . . . . . . . . . . 61 |
| 210 |  | 1995-96 . . . . . . . . . . . . . . . . . . . . . . . . 61 |
| SPEED SENSITIVE POWER STEERING (SPS) |
| 140.032 140.042 140.051 140.057 140.070 140.076 140.134 | 1992-93 . . . . . . . . . . . . . . . . . . . . . . . . 63 |
| 140 | 1994 . . . . . . . . . . . . . . . . . . . . . . . . . . 64 |
| CABRIOLET SOFT TOP (CST7 124.066 | 1993-95 . . . . . . . . . . . . . . . . . . . . . . . . 65 |
| ROLL BAR (RB) 124.066 | 1993-95 . . . . . . . . . . . . . . . . . . . . . . . . 66 |
| 129.061 129.066 129.067 129.076 | 1990-12/93 . . . . . . . . . . . . . . . . . . . . . 67 |
| ROADSTER SOFT TOP (RST) 129.061 129.066 129.067 129.076 | 1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 68 |
| 129 | 1/94-6/96 . . . . . . . . . . . . . . . . . . . . . . . 70 |
| INFRARED REMOTE CONTROL FOR CENTRAL LOCKING (IRCL) 129.061 129.066 129.067 129.076 | 1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 71 |
| 140 | 1990-96 . . . . . . . . . . . . . . . . . . . . . . . . 72 |
| 129 | 1993-96 . . . . . . . . . . . . . . . . . . . . . . . . 73 |
| PNEUMATIC SYSTEMS EQUIPMENT (PSE) 129 140 202 | 1992-94 . . . . . . . . . . . . . . . . . . . . . . . . 74 |
| ANTI-THEFT ALARM SYSTEM(ATA) 129.061 129.066 129.067 129.076 | 1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 75 |
| 140.032 140.042 140.051 140.057 140.070 140.076 140.134 | 1990-93 . . . . . . . . . . . . . . . . . . . . . . . . 75 |
| 129 140 202 | 1994-96 . . . . . . . . . . . . . . . . . . . . . . . . 75 |
| CELLULAR TELEPHONE (CT) 129.061 129.066 129.067 129.076 | 1992-95 . . . . . . . . . . . . . . . . . . . . . . . . 76 |
| 140.032 140.042 140.051 140.057 140.070 140.076 140.134 | 1992-95 . . . . . . . . . . . . . . . . . . . . . . . . 76 |
| CONVENIENCE FEATURES (CF) 140 | 1992-96 . . . . . . . . . . . . . . . . . . . . . . . . 77 |
| TEMPMATIC A/C 201.028 201.029 201.034 201.126 201.128 | 1988-93 . . . . . . . . . . . . . . . . . . . . . . . . 79 |
| A/C 124.034 124.036 | 1992-95 . . . . . . . . . . . . . . . . . . . . . . . . 81 |
| 124.026 124.030 124.050 124.090 124.051 124.230 124.290 | 1988-95 . . . . . . . . . . . . . . . . . . . . . . . . 82 |
| 126.024 126.025 126.035 126.039 126.045 126.134 126.135 | 1988-91 . . . . . . . . . . . . . . . . . . . . . . . . 82 |
| A/C SELF DIAGNOSTIC SYSTEMS TAU 2.1 | . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 83 |
| 129 Chassis | 1990-95 . . . . . . . . . . . . . . . . . . . . . . . . 86 |
| 129 Chassis | 1996-98 . . . . . . . . . . . . . . . . . . . . . . . . 89 |
| 140 Chassis | 1992-95 . . . . . . . . . . . . . . . . . . . . . . . . 92 |
| 140 Chassis | 1996-97 . . . . . . . . . . . . . . . . . . . . . . . . 98 |
| 202 Chassis | 1995 . . . . . . . . . . . . . . . . . . . . . . . . . 101 |
| 202 Chassis | 1996-98 . . . . . . . . . . . . . . . . . . . . . . . 107 |
| 210 Chassis | 1996-98 . . . . . . . . . . . . . . . . . . . . . . . 110 |
| SUPPLEMENTAL RESTRAINT SYSTEM (SRS) 107 126 140 201 | 1988-93 . . . . . . . . . . . . . . . . . . . . . . . 113 |
| 124 129 | 1990-93 . . . . . . . . . . . . . . . . . . . . . . . 114 |

DIGITAL FAULT CODE SYSTEMS F2 - F12	115

F2 SUPPLEMENTAL RESTRAINT SYSTEM (SRS) BAE, ZAE SYSTEM

129   140   124	1994-1995 . . . . . . . . . . . . . . . . . . . . . 116

202   210	Beginning of manufacture -1995	116

F3 SUPPLEMENTAL RESTRAINT SYSTEM (SRS) WITH SIDE AIRBAGS

129 (R)  140 (S)  202 (C)  210 (E)	1996 - 98	117

F4 - F5 LH SEQUENTIAL MULTIPORT FUEL INJECTION SYSTEM (LH-SFI)

104   119   120	1991-1993 . . . . . . . . . . . . . . . . . . . . . 118

F6 - F7 HFM SEQUENTIAL MULTIPORT FUEL INJECTION SYSTEM (HFM-SFI)

111 (4 cylinder, 2.2/2.3L engine)	1994-1997	122

104 (6 cylinder, 2.8/3.2L engine)	1994-1997	122

F6 - F7 PMS FUEL INJECTION SYSTEM

111 (4 cylinders, 1.8/2.0L engine)	1994-1997	127

F8, F9 & F10 DIAGNOSTIC MODULE (DM)

104   119   120	1991-1996 . . . . . . . . . . . . . . . . . . . . . 131

F11 - F12 ME SEQUENTIAL MULTIPORT FUEL INJECTION SYSTEM (ME-SFI)	134

TRANSMISSION MODULE OB15-12 INSTRUCTIONS	141

ANALOG FAULT CODES

| 124.230 124.290 w/CFI | 1990-93 . . . . . . . . . . . . . . . . . . . . 144 |
| --- | --- |
| 129 w/CFI | 1990-93 . . . . . . . . . . . . . . . . . . . . 145 |
| 129 140 w/LH-SFI | 1990-93 . . . . . . . . . . . . . . . . . . . . 146 |

| DIGITAL FAULT CODES |  |
| --- | --- |
| 129 140 163 170 202 208 | 210 w/ME-SFI | 1995-98 . . . . . . . . . . . . . . . . . . . . 147 |
| 129 140 w/LH-SFI or HFM-SFI |  | 1993-96 . . . . . . . . . . . . . . . . . . . . 150 |

MERCEDES TECHNICAL ACRONYMS	151

MERCEDES MODEL IDENTIFIER	154

DISCLAIMER: ALL INFORMATION CONTAINED IN THIS DOCUMENT IS CORRECT TO THE BEST OF OUR KNOWLEDGE. ERRORS MAY OCCUR THEREFORE BAUM TOOLS UNLIMITED INC. MAKES NO WARRANTEE, GUARANTEE OR ASSURANCE THAT DAMAGE MAY NOT OCCUR FROM THE USE OF THIS INFORMATION. THE USER TAKES ALL RESPONSIBILITY FOR ITS USE.

LIMITATION OF WARRANTIES AND LIABILITY: THE PRODUCT IS PROVIDED ON AN "AS IS" BASIS, WITHOUT ANY OTHER WARRANTIES OR CONDITIONS, EXPRESS OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, WARRANTIES OF MERCHANTABLE QUALITY, MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE, OR THOSE ARISING BY LAW, STATUTE, USAGE OF TRADE, OR COURSE OF DEALING. THE ENTIRE RISK AS TO THE RESULTS AND PERFORMANCE OF THE PRODUCT IS ASSUMED BY YOU. NEITHER WE NOR OUR DEALERS OR SUPPLIERS SHALL HAVE ANY LIABILITY TO YOU OR ANY OTHER PERSON OR ENTITY FOR ANY INDIRECT, INCIDENTAL, SPECIAL, OR CONSEQUENTIAL DAMAGES WHATSOEVER, INCLUDING, BUT NOT LIMITED TO, LOSS OF REVENUE OR PROFIT, LOST OR DAMAGED DATA OR OTHER COMMERCIAL OR ECONOMIC LOSS, EVEN IF WE HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES, OR THEY ARE FORESEEABLE. WE ARE ALSO NOT RESPONSIBLE FOR CLAIMS BY A THIRD PARTY. OUR MAXIMUM AGGREGATE LIABILITY TO YOU AND THAT OF OUR DEALERS AND SUPPLIERS SHALL NOT EXCEED THE AMOUNT PAID BY YOU FOR THE PRODUCT. THE LIMITATIONS IN THIS SECTION SHALL APPLY WHETHER OR NOT THE ALLEGED BREACH OR DEFAULT IS A BREACH OF A FUNDAMENTAL CONDITION OR TERM OR A FUNDAMENTAL BREACH. SOME STATES/COUNTRIES DO NOT ALLOW THE EXCLUSION OR LIMITATION OF LIABILITY FOR CONSEQUENTIAL OR INCIDENTAL DAMAGES, SO THE ABOVE LIMITATION MAY NOT APPLY TO YOU.

Mercedes Benz is a registered trademark of Daimler Benz AG.

Copyright © 1998 BAUM TOOLS UNLIMITED INC.

All rights reserved. Any reproduction in whole or in part is strictly prohibited.

SCANNER FEATURES

Keypad

SYSTEM	Select vehicle control system for code reading and erasing.

READ	Read fault codes.

NEXT	2. View next fault code. (If more than one fault code present)

CLEAR	Clear fault codes.

Screen Symbols

F	Control systems select.

	

:::::::::::: ::::::::: ::::::::::::



Scanner is Reading or Clearing fault code

U	Indicate fault code list number to use.

cccc

I	Indicate fault code.

0000

Four 0s flashing together.

Connection fault or vehicle not equipped with this system

» Check that the Ignition key is on or the Engine is running.

» Check power requirement to scanner (10.5 to 14.5 Volts)

» Check the in-line fuse on the Yellow probe wire.

» Check for correct connection to the Vehicle Diagnostic Connector.

» Check for short circuit in the Vehicle Diagnostic Connector.

» Check that this memory cartridge is available for this vehicle system.

» Check that vehicle system requested for test is fitted to this vehicle.

Indicator lights

Power indicator (Red LED light)

Data link indicator (Green LED light). Receive data from the control unit.

Data link indicator (Yellow LED light). Transfer data to the control unit.

SECTION 1	Using the CS1000 Code Scanner

Diagnostic Cable

General Usage Notes

+	The OB15 Code Scanner can display available fault codes from Mercedes Benz vehicles fitted with 8-pole, 16-pole and 38-pole Diagnostic Connectors. The Red wire from the scanner is for powering up the unit and is taken either from the power source socket on the Diagnostic Connector, if available, or from the vehicle  battery, using the extension cable supplied. The Black earth wire from the scanner is grounded to the earth socket on the Diagnostic Connector. The Yellow wire from the scanner is used to read the codes from the Diagnostic Connector.

+	The P/N 15-C2 diagnostic cable must be used with the P/N 15-C2-1 diagnostic cable for the 38-pole vehicle diagnostic connector.

Connection Table

Test Lead of Cable	Connection source

Red	Power -To power supply socket or vehicle battery Black	Ground - To socket 1

Yellow	To diagnostic test socket

Power supply (B+) socket on the vehicle Diagnostic Connectors

8-pole connector	Use with the battery extension cable to the vehicle battery 16-pole connector	Socket 16 (circuit 15 - ignition ON)*

Not present in some models. Use battery +.

38-pole connector	Socket  3 (circuit 30 - Battery+)

*Must be performed with the ignition ON to power up the scanner.

Ground (-) socket on the vehicle Diagnostic Connectors

8-pole connector socket 1 16-pole connector socket 1 38-pole connector   socket 1

Connector Layout of Vehicle Diagnostic Connector

8-pole Diagnostic Connector

Models 201, 124, 126

Ground

Not used

CIS-E	Continuous fuel injection system (CFI)

ELR EDS

ASD 4MATIC

Diesel injection system - Electronic idle speed control system Electronic diesel system

Automatic locking differential

Automatic-engaged four wheel drive (124 only)

SRS	Supplemental Restraint System

A/C	Air Conditioning

Not used

16-pole Diagnostic Connector

Models 124, 129

| 1 |  | Ground |
| --- | --- | --- |
| 2 | OBD | Push-button for On Board Diagnostic (California only) |
| 3 | CIS-E DM | Continuous Fuel injection system (CFI) Diagnostic Module - LED (California only) |
| 4 | EDS | Electronic diesel system |
| 5 | ASD 4MATIC | Automatic locking differential Automatic-engaged four wheel drive |
| 6 | SRS / AB | Supplemental Restraint System / Air Bag |
| 7 | A/C RB | Air Conditioning (Model 124) Roll Bar (Model 129) |
| 8 | DI HFM-SFI PEC | Distributor ignition HFM Sequential multi-port Fuel Injection/Ignition system Pressurized engine control |
| 9 | ADS RB | Adaptive Damping System Roll Bar (Model 124) |
| 10 | RST | Roadster Soft Top (Model 129) TN-signal (Gasoline) |
| 11 | ATA | Anti Theft Alarm system |
| 12 | IRCL | Infrared Remote Central Locking |
| 13 | ETC | Electronic automatic Transmission Control |
| 14 | EA CC / ISC ESCM | Electronic Accelerator (Model 124) Cruise Control / Idle Speed Control (Model 124) Engine System Control Module (MAS), (Model 129) |
| 15 |  | Not used |
| 16 |  | Voltage, Ignition ON (Circuit 15) (Not equipped on all models.) |

38-Pin Diagnostic Connector

Models 124.034/036, 129.058/063/067/076, 140, 170, 202,

208, 210

The Mercedes Diagnostic “Mushroom” #140-1463 available from Baum Tools Unltd. is recommended to allow easy  access to the diagnostic connector. Call 800-848-6657 or 941- 927-1414 for more information.

| Pin | System | Description |
| --- | --- | --- |
| 1 | Ground (Terminal 31) | W12 (Chassis Ground), W15 (Electronics Ground) |
| 2 | Voltage, terminal 87 | Ignition Switch 12volts + |
| 3 | Voltage, terminal 30 | Battery 12volts + |
| 4 | EDS | Electronic Diesel System |
|  | IFI | In-line Fuel Injection |
|  | DFI | Electronic Distributor-type Fuel Injection (Diesel) |
|  | HFM-SFI | Hot-Film Engine Management Sequential Multiport Fuel Injection/ignition |
|  | LH-SFI | LH Sequential Multiport Fuel Injection System Engines 104, 119 Engine 120 Right Bank |
|  | ME-SFI | Motor Electronics with Sequential Multiport Fuel Injection/ignition System Engine 119 Engine 120, Right Bank |
| 5 | LH-SFI | LH Sequential Multiport Fuel Injection, Engine 120 Left Bank |
|  | ME-SFI | Motor Electronics with Sequential Multiport Fuel Injection/ignition System Engine 120 Left Bank |
| 6 | ABS | Anti-lock Brake System |
|  | ETS | Electronic Traction System |
|  | ASR | Acceleration Slip Regulation |
|  | ESP | Electronic Stability Program |
| 7 | EA | Electronic Accelerator+ |
|  | ISC | Idle Speed Control |
|  | CC | Cruise Control/idle Speed Control |
| 8 | BM | Base Module |
|  | BAS | Brake Assist |
| 9 | ASD | Automatic Locking Differential, Models 124, 129, 140 |
| 10 | EATC | Electronic Automatic Transmission Control (5-speed AT) (722.6) |
|  | ETC | Electronic Transmission Control (722.6) |
| 11 | ADS | Adaptive Damping System |

| 12 | SPS | Speed-sensitive Power Steering |
| --- | --- | --- |
| 13 | TD | Speed Signal (Time Division) (Di) (Diesel) Models 202, 210 |
|  | TNA | Signal (Gasoline) on LH-SFI |
|  | TN | Speed Signal (DI/KSS) (Gasoline) on HFM-SFI, ME-SFI |
| 14 | Lambda on/off ratio | LH-SFI Engine 119, LH-SFI Engine 120 LH-SFI, Right Bank |
| 15 | Lambda on/off ratio | LH-SFI Engine 120 Left Bank |
|  | IC | Instrument Cluster |
| 16 | HEAT | Automatic Heater |
|  | TA/C | Air Conditioning (Tempmatic) |
|  | AA/C | Air Conditioning (Automatic) |
| 17 | DI | Distributor Ignition, Engines 104, 119, Engine 120, Right |
|  | TD | Speed Signal (Time Division) (Di) (Diesel) Model 140 |
|  | TN | Speed Signal (DI/KSS) (Gasoline) on LH-SFI / model 202 HFM-SFI |
| 18 | DI | Distributor Ignition, Engine 120, Left |
| 19 | DM | Diagnostic Module |
| 20 | PSE | Pneumatic System Equipment, Model 140 |
|  | MFCM | Multi-function Control Module, Model 210 |
| 21 | CF | Convenience Feature, Model 140 |
|  | RST | Roadster Soft Top, Model 129 |
| 22 | RB | Roll Bar, Model 129 |
| 23 | ATA | Anti-theft Alarm |
| 24-25 | - |  |
| 26 | ASD | Automatic Locking Differential, Model 202 |
| 27 | - |  |
| 28 | PTS | Parktronic System, Model 140 |
| 29 | - |  |
| 30 | AB | Airbag/emergency Tensioning Retractor |
| 31 | RCL | Remote Central Locking |
| 32-33 | - |  |
| 34 | CNS | Communication and Navigation System |
| 35 | - |  |
| 36 | STH | Stationary Heater |
| 36 | ZUH | Heater Booster |
| 37-38 | - |  |

9-Pole Diagnostic Connector (1980-94)

The 9-pole Diagnostic Connector is used on earlier model vehicles. It can display on-off ratio fault codes (1986 and later), RPM and Lambda sensor values. Various on-off ratio Meters are available that provide access to this type of diagnostic connector. Call Baum Tools at 800-848-6657 or 941-927-1414 for more information on these meters.

Operating the CS1000 - Mercedes Benz

OB15-11 Memory Cartridge - Mercedes Benz Analog & Digital Fault Codes

Setting Up

ATTENTION: DO NOT INSERT CARTRIDGE WITH POWER SUPPLIED TO THE CS1000.

PROPER USE OF THE MERCEDES DIAGNOSTIC SYSTEM

�	Identify vehicle Model and Month/Year of production

�	Confirm specific drivability complaint. If MIL is on, when did it come on and under what conditions?

Insert the OB15-11 memory cartridge into the base of the scanner. Make sure the arrow on the cartridge is facing up as it is inserted. Gently push the cartridge into the CS1000 until the cartridge seats completely.

fii Refer to Diagnostic Cable introduction page 9 and connection table page 10 of this manual to determine vehicle cable requirements. Connect the cable specified to the scanner and to the vehicle Diagnostic Connector.

+	Connect the 25-pin cable connector head firmly to the scanner 25-pin connection port.

+	Connect the Red test lead from the scanner to the power supply socket (B+) on the Diagnostic Connector, where available, or to the vehicle's battery via the extension cable and battery clamp supplied.

+	Connect the Black test lead from the scanner to the ground socket on the Diagnostic Connector. Now the scanner powered up and the power indicator light should be fully illuminated. The screen will display E	1.

Note:

Power indicator light (LED) must light up. If it does not, refer to the list below for detailed test.

Refer to the connection table of this manual; check the Red and Black test lead with the socket number on the Diagnostic Connector, Is there an incorrect or weak connection?

Check the power requirement on the Diagnostic Connector. (Must be performed with the ignition ON when connected with 16-pole diagnostic connector at socket 16)

Connect the Yellow test lead to the system diagnostic socket that you use to extract codes.

Refer to this manual or Mercedes Benz maintenance manual for location of the Diagnostic sockets for the type of Diagnostic Connector fitted to the vehicle and the system capabilities available for code access on the applicable Diagnostic sockets.

Turn Ignition ON (KOEO) or Engine at idle (KOER)

System Selection

| F | 1 |
| --- | --- |
| F | 2 |
| F | 3 |
| F | 4 |
| F | 5 |
| F | 6 |
| F | 7 |

All analog impulse fault code systems. If unsure, start with this system.

Digital type SRS (1 or 2 airbag) system as follows:

1. W202 © class).	2. W129 / W140  1993 - 1996

Digital type SRS (4 airbags)

1. W210 (E class).	2. W129 / W140  1996  1998

Digital type LH-SFI for the Current fault codes. 1991-1993 Digital type LH-SFI for the Stored fault codes. 1991-1993

Digital type HFM-SFI for the Current fault codes. 1993-1997

Digital type PMS for the Current fault codes. 1993-1996 Digital type HFM-SFI for the Stored fault codes. 1993-1997

Digital type PMS for the Stored fault codes. 1993-1996

| F | 8 |
| --- | --- |
| F | 9 |
| F | 10 |

Digital type DM for the Current fault codes. 1991-1996 Digital type DM for the Stored fault codes. 1991-1996 Digital type DM for the Registered fault codes. 1991-1996

F	11	Digital type ME-SFI for the Current fault codes. 1996-1998

F	12	Digital type ME-SFI for the Stored fault codes. 1996-1998 Press the SYSTEM key to scroll to display from F 1 to F 2 system etc....

SYSTEM

ANALOG TEST PROCEDURES

Ignition in the KOEO position (Key On Engine Off)

Choose system F1

Place test probe (yellow) in pin-out for specific analog test.

DIGITAL TEST PROCEDURE

Ignition in the KOEO position (Key On Engine Off)

Choose system F2 thru F12

Place test probe (yellow) in pin-out for specific analog test.

If any system does not respond, test it using the Analog Test Procedure.

*Some early LH Injection and Diagnostic Module systems may not respond to the digital test.

Read Fault Codes

Press the READ key to begin to read the fault codes for the system selected. The scanner will scan all of the fault codes and keep them in memory.

READ

Press the NEXT key to scroll through the fault codes C	xx . The display will cycle to the first code after the last code is displayed. When there are no faults in the system, C	0 will be displayed on the screen.

NEXT

There are 5 digital numbers for fault code for the ME-SFI control system, the fault code will automatically display 1 digital number first then 4 digital numbers later. For example, the fault code  1234 will display C    0 then 1 2 3 4 .  C    0 stands for   (Power-train system)

5678 will display C    1 then 5 6 7 8 .  C    1 stands for   (Chassis system) 0110 will display C    2 then 0 1 1 0 .  C    2 stands for   (Body system)

4321 will display C    3 then 4 3 2 1 .  C    3 stands for   (Unspecified system)

Identification/Rectification of Faults

Identify fault code and related circuit using this manual or using the factory diagnostic manuals available from Baum Tools Technical Publications 415-566-9229.

Carry out required repair before clearing fault codes.

About Current, Stored and Registered Faults

Current Faults - These faults are detected while the car is running at idle or speed. They represent components currently failing. These codes cannot be erased, and are only meaningful with the ignition on and the engine running. Codes found in this system with the KOEO have no meaning. Components not present on the vehicle may be flagged as failing by the cars internal diagnostics due to the generic nature of the cars software. This is particularly true in C-Class (202) cars.

Stored or Permanent Faults - These faults are recorded in the permanent memory of the cars system controller and are the main cause of MIL illumination. These codes can be erased.

Registered Faults - These faults are recorded in the temporary memory of the of the cars system controller. This temporary memory records the number of times a component fails. When a certain number of failures has occurred the fault is moved to permanent storage and the Check Engine Light (MIL) will be illuminated. On cars equipped with Fault Registers the Check Engine Light may stay on after the Stored or Permanent Fault has been erased if another occurrence of the fault has happened since the Permanent Fault was stored. To extinguish the light erase the Stored and Registered faults. These codes can be erased.

Check Engine Light Diagnosis

Mercedes S(140), SL(129), E(210) and C(202) class have multiple systems which can turn on an Check Engine Light. All related systems must be tested for codes and repaired before the light will extinguish.

| 129 LH | LH (pin 4 & 5) EA/CC/ISC (pin 7), BM (pin 8), DI (pin 17 & 18) and DM (pin 19) |
| --- | --- |
| 140 LH | LH (pin 4) EA/CC/ISC (pin 7), BM (pin 8), DI (pin 17) and DM (pin 19) |
| 124 HFM | HFM (pin 8) EA/CC/ISC (pin 14), and DM (pin 3) |
| 140 HFM | HFM (pin 4) EA/CC/ISC (pin 7), BM (pin 8), DI (pin 17) and DM (pin 19) |
| 202 HFM | HFM (pin 4) EA/CC/ISC (pin 7) (except C220) and DM (pin 19) |
| 210 HFM | HFM (pin 4) EA/CC/ISC (pin 7), BM (pin 8), DI (pin 17) and DM (pin 19) |

Clearing Fault Codes

After repairs have been carried out reread the codes. After rereading the codes press the CLEAR key to erase all of the fault codes from the control unit memory. When there are no faults in the system, either C	1 (Impulse or analog systems) or C  2 (digital systems) will be displayed on the screen.

CLEAR

Return to System Select Function

Press the SYSTEM key to scroll through the system selections.

SYSTEM

Mercedes Benz System Type and Model Applications OB15-11 Software Cartridge

The Code Scanner will read and clear the fault codes for the following System applications and Year models. Refer to the table of contents section 3 or to system  malfunction tables of this manual to determine vehicle model and year.

ANALOG/DIGITAL MODULE OB15-11

| SYSTEM | DESCRIPTION | ANALOG | DIGITAL |
| --- | --- | --- | --- |
| A/C | Air Conditioning / Heating | 1988-93 |  |
| ABS | Anti-lock Brake System | 1992-95 | 1992-97 |
| ADS | Automatic Damping System (Suspension) | 1991-93 |  |
| ASD | Automatic Locking Differential | 1991-93 |  |
| ASR | Acceleration Slip Regulation | 1992-95 | 1992-97 |
| ATA | Anti-theft Alarm System | 1990-95 |  |
| BM | Base Module (Master ECU Controller) | 1992-95 |  |
| CC | Cruise Control (Tempomat) | 1992-95 |  |
| CF | Convenience Feature | 1992-95 |  |
| CFI | Continuous Fuel Injection (CIS-E) | 1988-92 |  |
| CST | Cabriolet Soft Top | 1993-95 |  |
| DI | Distributor Ignition System | 1990-93 |  |
| DM (USA) | Diagnostic Module (Emissions) | 1990-93 | 1991-98 |
| EA | Electronic Accelerator | 1992-95 |  |
| EDS | Electronic Diesel System | 1990-93 |  |
| ELR | Diesel Electronic Idle Speed Control | 1989 |  |
| HFM-SFI | Hot Film Engine Management | 1993-95 | 1994-97 |
| IRCL | Infrared Remote Central Locking | 1990-95 |  |
| ISC | Idle Speed Control | 1992-95 |  |
| KE | Continuous Injection System (CIS-E) | 1987-92 |  |
| LH-SFI | LH Sequential Fuel Management | 1990-93 | 1991-93 |
| MAS | Engine System Control Module (Mas) | 1990-93 |  |
| ME-SFI | Motor Electronic Injection |  | 1996-98 |
| PMS |  | 1993-95 | 1994-97 |
| PSE | Pneumatic System Equipment | 1992-95 |  |
| RB | Roll Bar Control | 1990-95 |  |
| RST | Roadster Soft Top | 1992-95 |  |
| SPS | Speed-sensitive Power Steering | 1992-95 |  |
| SRS | Supplemental Restraint System (Airbag) | 1988-93 | 1993-98 |

TRANSMISSION MODULE OB15-12

| 4MATIC | 4 Wheel Drive Transmission Control | 1990-93 | 1993-95 |
| --- | --- | --- | --- |
| ETC/EGS | Electronic Transmission Control | 1990-93 | 1993-97 |

ErEC.lHOMIC IDrE 2bEED COM.lHOr (ErH)

| Model | Model Year |
| --- | --- |
| 201.126 | 1989 |

Connect wires of Scanner as follows:

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Speed sensor signal |
| 3 | Coolant temperature sensor signal |
| 4 | ELR control unit or Idle speed control (ISC) system |

| Model | Model Year |
| --- | --- |
| 124.128 | 1990-91 |
| 126.134 126.135 | 1990-91 |

Connect wires of Scanner as follows:

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Fuel rack position sensor (L7) |
| 3 | Air flow sensor (B2/1) |
| 4 | EDS control unit (N39), atmospheric pressure sensor |
| 5 | EGR valve vacuum transducer (Y31/1) or malfunction in EGR control circuit |
| 6 | EDS control unit (N39), internal voltage supply |
| 7 | Starter ring gear speed sensor (L3) |
| 8 | Coolant temperature sensor (B11/4) |
| 9 | Intake air temperature sensor (B2/1a) |
| 10 | Voltage supply insufficient |
| 11 | Electronic idle speed control actuator or exhaust gas recirculation (EGR) valve vacuum transducer |
| 12 | Not used |
| 13 | Electronic diesel system control unit (n39), faulty (internal fault memory) |
| 14 | Electronic diesel system pressure sensor (B5/1), defective |
| 15 | Intake manifold air pressure control valve vacuum transducer (Y31/2), wastage vacuum transducer (Y31/3), or malfunction Intake manifold air pressure circuit |

| Model | Model Year |
| --- | --- |
| 124.128 | 1992-93 |
| 140.134 | 1992-93 |

Connect wires of Scanner as follows (124)

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Battery (+) |

Connect wires of Scanner as follows (140)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Fuel rack position sensor (L7) |
| 3 | Air flow sensor signal (B2/1) |
| 4 | Electronic diesel system (EDS) control unit (N39) or atmospheric pressure sensor |
| 5 | Exhaust gas recirculation valve vacuum transducer (Y31/1) or fault in exhaust gas recirculation (EGR) control circuit |
| 6 | Electronic diesel system (EDS) control unit (N39), internal voltage supply |
| 7 | Starter ring gear speed sensor (L3) |
| 8 | Engine coolant temperature sensor (B11/4) |
| 9 | Intake air temperature sensor (B2/1a) |
| 10 | Voltage supply insufficient |
| 11 | Electronic idle speed control actuator (Y22) or exhaust gas recirculation (EGR) valve vacuum transducer (Y31/1) or Boost pressure cut-out switchover valve |
| 12 | Not used |
| 13 | Electronic diesel system control unit (N39), faulty (internal fault memory) |
| 14 | Electronic diesel system pressure sensor (B5/1), defective |
| 15 | Boost pressure control/ pressure control flap vacuum transducer (Y31/5) , or defect in Boost pressure control circuit. |

| Model | Model Year |
| --- | --- |
| 107.048 | 1988-91 (California version only) |
| 124.026 124.030 124.050 124.090 | 1988-89 (California version only) |
| 126.024 126.025 | 1988-89 (California version only) |
| 126.035 126.039 126.045 | 1988-91 (California version only) |
| 201.028 (1988-93) 201.029 | 1988-89 (California version only) |

Connect wires of Scanner as follows:

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 3 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Throttle position switch - wide open throttle fault |
| 3 | Engine coolant temperature sensor |
| 4 | Air flow sensor position indicator |
| 5 | Oxygen sensor |
| 6 | Not used |
| 7 | TD-signal (rpm) |
| 8 | Altitude correction capsule |
| 9 | Electronic hydraulic actuator (EHA) |
| 10 | Throttle position switch - closed throttle position fault (idle) |
| 12 | Exhaust gas recirculation temperature sensor |

| Models | Model Years |
| --- | --- |
| 124.026 124.030 124.090 124.230 124.290 | 1990-93 |
| 126.024 126.025 | 1990-93 |
| 201.029 | 1990-93 |

Connect Wires of Scanner as Follows:

| Scanner | Data Link Connector 8 & 16-pin |
| --- | --- |
| Yellow | Socket 3 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Throttle position switch - wide open throttle (WOT), signal faulty |
| 3 | Engine coolant temperature signal read by CFI control module |
| 4 | Potentiometer voltage illogical |
| 5 | Oxygen sensor signal illogical |
| 6 | Not used |
| 7 | TNA signal(rpm) read by CFI control module |
| 8 | Altitude pressure signal from ignition control module illogical |
| 9 | Current to EHA is illogical |
| 10 | Throttle position switch - closed throttle position fault (idle) |
| 11 | Air injection system |
| 12 | Absolute pressure values from EZL ignition control module are illogical |
| 13 | Intake air temperature reading is illogical |
| 14 | Vehicle speed signal read by CFI control module is illogical |
| 15 | Not used |
| 16 | Exhaust gas recirculation |
| 17 | Oxygen sensor is shorted to positive or ground |
| 18 | Current to idle control valve is illogical |
| 19 | Not used |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 20 | Not used |
| 21 | Not used |
| 22 | Oxygen sensor heating current illogical |
| 23 | Short circuit to positive in purge switchover valve circuit |
| 24 | Not used |
| 25 | Short circuit to positive in start valve circuit |
| 26 | Short circuit to positive in upshift delay solenoid valve circuit |
| 27 | Data exchange between CFI control module and ignition control module interrupted |
| 28 | Intermittent contact in engine coolant temperature sensor circuit |
| 29 | CFI and ignition control module reading different engine coolant temperature |
| 30 | Not used |
| 31 | Intermittent contact in engine coolant temperature sensor circuit |
| 32 | Not used |
| 33 | Not used |
| 34 | Engine coolant temperature read from ignition control module illogical |

\;OU+!UnOn2 1:n&1 IUl&C+!OU it]\2+&W (\;1:IJ

| Models | Model Years |
| --- | --- |
| 124.051 129.061 | 1990-93 |
| 129.066 | 1990-92 |

Connect wires of Scanner as follows:

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 3 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Throttle position switch - wide open throttle fault (WOT), signal faulty |
| 3 | Engine coolant temperature in CFI control module illogical |
| 4 | Air flow sensor position indicator potentiometer current illogical |
| 5 | Oxygen sensor signal illogical |
| 6 | Not used |
| 7 | TNA- signal (rpm) at CFI control module illogical |
| 8 | Altitude correction signal from ignition control module |
| 9 | Current to EHA is illogical |
| 10 | Throttle position switch - closed throttle position fault (idle) |
| 11 | Air injection system, open or short circuit |
| 12 | Absolute pressure values from ignition control module illogical |
| 13 | Intake air temperature illogical |
| 14 | Speed signal at CFI control module illogical |
| 15 | Not used |
| 16 | Exhaust gas recirculation switchover valve, open or short circuit |
| 17 | Oxygen sensor signal wire shorted to positive or ground |
| 18 | Current to idle control valve is illogical |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 19 | Not used |
| 20 | Not used |
| 21 | Not used |
| 22 | Oxygen sensor heater voltage illogical |
| 23 | Short to positive in purge switchover valve circuit |
| 24 | Not used |
| 25 | Short circuit to positive in start valve circuit |
| 26 | Short circuit to positive in upshift delay solenoid valve circuit |
| 27 | Data exchange between CFI control module and ignition control module |
| 28 | Intermittent contact in engine coolant temperature sensor circuit |
| 29 | CFI and ignition control module reading different engine coolant temperature |
| 30 | Not used |
| 31 | Intermittent contact in engine coolant temperature sensor circuit |
| 32 | Not used |
| 33 | Not used |
| 34 | Engine coolant temperature read from ignition control module illogical |

CouJ!unon2 l:n&I lul&CJ!ou 2A2J&W (INY2 COMJ.HOrrEH)

| Models | Model Years |
| --- | --- |
| 124.026 | 124.030 | 124.090 124.230 | 124.290 | 129.066 | 201.029 | 1990-92 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 14 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Fuel pump relay (circuit 87) not functioning |
| 3 | TN/TD signal (RPM) interrupted |
| 4 | Output for oxygen sensor heater control defective |
| 5 | Output for air injection pump control defective |
| 6 | Output for kickdown switch control defective |
| 7 | Not used |
| 8 | Engine coolant temperature sensor signal out of range |
| 9 | Circuit 50 failure |
| 10 | Output failure of the start valve |
| 11 | A/C compressor engagement signal missing (87Z) |
| 12 | Output for A/C compressor control defective |
| 13 | Excessive A/C compressor clutch slippage |
| 14 | Vehicle speed signal illogical |
| 15 | Short circuit detected in fuel primp circuit |

Itt �&dn&U+!SI INnI+!bOL+ 1:n&I IU!&C+!OU �.A2+&W {Itt-�1:IJ

| Models | Model Years |
| --- | --- |
| 140.032 | 140.057 | 140.076 | 1992-93 |
| 124.034 | 124.036 | 1992-93 |
| 129.067 | 1992-95 |
| 140.042 | 140.043 | 140.051 | 1992-95 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Engine coolant temperature sensor circuit 1, open or short circuit. |
| 3 | Engine coolant temperature sensor circuit 2, open or short circuit. |
| 4 | Voltage at mass air sensor with hot wire circuit. Open or short circuit. |
| 5 | Not used |
| 6 | Not used |
| 7 | TNA-signal (rpm signal ) incorrect or open or short circuit. |
| 8 | Camshaft position sensor signal. Open or short circuit. |
| 9 | Starter signal (circuit 50) missing, open or short circuit. |
| 10 | Closed throttle position recognition from electronic accelerator control unit, short circuit. |
| 11 | Secondary air injection system, open or short circuit. |
| 12 | Burn-off control for mass air sensor with hot-wire, open or short circuit. |
| 13 | Intake air temperature sensor, open or short circuit. |
| 14 | Not used |
| 15 | Not used |
| 16 | Exhaust gas recirculation (EGR) switchover valve, open or short circuit. |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 17 | CAN data: Electronic accelerator control module - no data transmission |
| 18 | CAN data: Ignition control module - no data transmission from DI module |
| 19 | Left LH-SFI control module no data transmission to right LH-SFI control module |
| 20 | LH-SFI control module - no data transmission |
| 21 | Oxygen sensor open circuit. |
| 22 | Oxygen sensor heater, open or short circuit. |
| 23 | Purge switchover valve, open or short circuit. |
| 24 | Left adjustable camshaft timing solenoid (Y49/1), open or short circuit |
| 25 | Adjustable camshaft timing solenoid, open or short circuit. |
| 27 | Injectors, open or short circuit. |
| 29 | I GR Start relay module (K29/1), open or short circuit |

tt�ll\ �&dn&U+!91 ll\n1+!bOL+ �n&1 IUl&C+!OU �A2+&W

| Engines | Model Year |
| --- | --- |
| 104 111 | 1993-97 |

Connect wires of Scanner as follows (124)

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 8 |
| Black | Socket 1 |
| Red | Socket 16 |

Connect wires of Scanner as follows (202  129  140)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Engine Coolant temperature sensor |
| 3 | Intake air temperature sensor |
| 4 | Hot film mass air flow sensor |
| 5 | CTP switch |
| 6 | Not used |
| 7 | Not used |
| 8 | Idle speed control (ISC) system at upper or lower control stop or CC or EA indicates "limp home" mode. |
| 9 | O2S 1 (before TWC) - voltage too high, circuit open or voltage implausible |
| 10 | O2S 2 (after TWC)voltage too high, circuit open or voltage implausible |
| 11 | O2S 1 heater (before TWC) - Current too high/low or short circuit. |
| 12 | O2S 2 heater (after TWC) - Current too high/low or short circuit. |
| 13 | O2S (Lambda) control system operating at rich or lean limit |
| 14 | Injector, cylinder 1 |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 15 | Injector, cylinder 2 |
| 16 | Injector, cylinder 3 |
| 17 | Injector, cylinder 4 |
| 18 | Injector, cylinder 5 |
| 19 | Injector, cylinder 6 |
| 20 | Self-adaptation at idle speed or upper/lower partial load at rich or lean limit |
| 21 | Ignition output 3 or ignition coil for cylinder 1 and 6 |
| 22 | Ignition output 1 or ignition coil for cylinder 2 and 5 (Engine 111, cylinder 1 and 4) |
| 23 | Ignition output 2 or ignition coil for cylinder 3 and 4 (Engine 111, cylinder 2 and 3) |
| 24 | CKP sensor or magnet for position sensor not recognized |
| 25 | CMP sensor not recognized or implausible |
| 26 | Not used |
| 27 | TN-signal (rpm signal ) - open or short to ground |
| 28 | VSS - open circuit |
| 29 | Not used |
| 30 | Fuel pump relay module - open or short circuit |
| 31 | Not used |
| 32 | Knock sensors 1 and /or 2 |
| 33 | Maximum retard setting on at least one cylinder has been reached or the ignition angle deviation between the individual cylinders is greater than 6 degrees crankshaft angle |
| 34 | Knock control-output switch in engine control module faulty Momentary fault in self-adaptation closed throttle speed/partial load |
| 35 | Model 124,129 and 140 AIR pump switchover valve and/or electromagnetic AIR pump clutch. Model 202 AIR pump switchover valve and/or AIR relay module |
| 36 | Purge control valve - open/short to ground or B+ |
| 37 | Upshift delay switchover valve |
| 38 | Adjustable camshaft timing solenoid - open/short to ground or B+ |
| 39 | Exhaust gas recirculation switchover valve - open/short to ground or B+ |
| 40 | Transmission overload protection switch - open/short to ground or B+ or open or closed or implausible |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 41 | CAN communication from engine control module faulty |
| 42 | CAN communication from ASR, EA/CC/ISC module or diagnostic module (OBD II) faulty |
| 43 | Starter signal (circuit 50) not present |
| 44 | Not used |
| 45 | Fuel safety shut-off of electronic accelerator or cruise control active |
| 46 | Resonance intake manifold switchover valve - open/short to ground or B+ |
| 48 | O2S 2 (after TWC) heating circuit relay module - open/short to ground or B+ |
| 49 | Voltage supply at engine control module implausible/low volts |
| 50 | Engine control module faulty or not coded. |

| Models | Model Years |
| --- | --- |
| 124.034 124.036 | 1992-93 |
| 129.067 | 1992-95 |
| 140.032 140.042 140.043 140.051 140.057 140.076 | 1992-95 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 8 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2, 3, 4 | Not used |
| 5 | Maximum permissible temperature in module box exceeded |
| 6 | Electromagnetic a/c compressor clutch blocked |
| 7 | Poly v-belt slipping |
| 8 | Voltage supply for LH-SFI control module interrupted |
| 9 | Voltage supply for LH-SFI control module interrupted |
| 10 | Voltage supply for LH-SFI control module interrupted Voltage supply for fuel injectors interrupted |
| 11 | Voltage supply for accessory equipment control module interrupted |
| 12 | Voltage supply for ABS control module, ABS/ASR control module or ASD control module interrupted |
| 13, 14 | Not used |
| 15 | Voltage supply for kickdown valve interrupted |
| 16 | Voltage supply for electromagnetic a/c compressor clutch interrupted |
| 17 | Voltage supply for module box blower motor interrupted |

| Models | Model Years |
| --- | --- |
| 124.034 124.036 | 1992-1993 |
| 119.067 | 1992-1995 |
| 140.032 140.042 140.043 140.051 | 1992-1995 |

Connect wires of Scanner as follows

| Scanner | Data link connector 38- pin |
| --- | --- |
| Yellow | Socket 19 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Oxygen sensor faulty |
| 3 | Lambda control faulty |
| 4 | Air injection system faulty |
| 5 | Exhaust gas recirculation faulty |
| 6 | Idle speed control faulty |
| 7 | Ignition system faulty |
| 8 | Engine coolant temperature sensor. Circuit open or circuit short |
| 9 | Intake air temperature sensor. Circuit open or circuit short |
| 10 | Voltage at mass air sensor too high/low |
| 11 | TNA-signal (rpm signal ) faulty |
| 12 | Oxygen sensor greater, circuit open or circuit short |
| 13 | Camshaft position sensor signal from ignition control module faulty |
| 14 | Intake manifold pressure too low when starting |
| 15 | Wide open throttle position information faulty |
| 16 | Closed throttle position information faulty |
| 17 | Data exchange fault between individual control module |
| 18 | Adjustable camshaft timing solenoid circuit open or circuit short |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 19 | Injector open or short circuit or emission control system adaptation at limit |
| 20 | Vehicle speed signal missing |
| 21 | Purge switchover valve, circuit open or circuit short |
| 22 | Camshaft position sensor signal faulty |
| 23 | Intake manifold pressure with engine running too low |
| 24 | Starter ring gear segments faulty |
| 25 | Knock sensors faulty |
| 26 | Upshift delay switchover valve, circuit open or circuit short |
| 27 | Engine coolant temperature sensor deviation between sensor circuit 1and sensor circuit 2. |
| 28 | Engine coolant temperature sensor (engine coolant temperature change monitor) |

| Models | Model Years |
| --- | --- |
| 140.057 140.076 | 1992-1995 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 19 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Right oxygen sensor faulty |
| 3 | Lambda control of right LH-SFI control module faulty |
| 4 | Air injection at right cylinder bank faulty |
| 5 | Exhaust gas recirculation of right LH-SFI control module faulty |
| 6 | Idle speed control faulty |
| 7 | Ignition system for right cylinder faulty |
| 8 | Right engine coolant temperature sensor, circuit open or circuit short |
| 9 | Right intake air temperature sensor, circuit open or circuit short |
| 10 | Voltage at mass air sensor too high/low |
| 11 | Tn-signal (rpm signal ) at right LH-SFI control module faulty |
| 12 | Oxygen sensor heater of right oxygen sensor, circuit open or circuit short |
| 13 | Camshaft position sensor signal of right ignition control module faulty |
| 14 | Intake manifold pressure at startup (in right ignition control module) too low or too high |
| 15 | Wide open throttle position information faulty |
| 16 | Closed throttle position information faulty |
| 17 | Data exchange fault between right-hand control modules LH-SFI ignition control module electronic accelerator |
| 18 | Right adjustable camshaft timing solenoid circuit open or circuit short |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 19 | Right injector circuit open or circuit short or emission control system adaptation in right LH-SFI control module at limit |
| 20 | Vehicle speed signal missing |
| 21 | Right purge switchover valve, circuit open or circuit short |
| 22 | Right camshaft position sensor signal faulty |
| 23 | Intake manifold pressure(in right ignition control module) with engine running too low/high |
| 24 | Starter ring gear segments faulty |
| 25 | Knock sensors or right ignition control module faulty |
| 26 | Upshift delay switchover valve, circuit open or circuit short |
| 27 | Right engine coolant temperature sensor deviation between circuit 1, and sensor circuit 2. |
| 28 | Right engine coolant temperature sensor (engine coolant temperature change monitor) |
| 34 | Left oxygen sensor faulty |
| 35 | Lambda control of left LH-SFI control module faulty |
| 36 | Air injection at left cylinder bank faulty |
| 37 | Exhaust gas recirculation of left LH-SFI control module faulty |
| 38 | Not used |
| 39 | Ignition system for left cylinder faulty |
| 40 | Left engine coolant temperature sensor, circuit open or circuit short |
| 41 | Left intake air temperature sensor, circuit open or circuit short |
| 42 | Voltage at mass air sensor too high/low |
| 43 | Tn-signal (rpm signal ) at left LH-SFI control module faulty |
| 44 | Oxygen sensor heater of left oxygen sensor, circuit open or circuit short |
| 45 | Camshaft position sensor signal of left ignition control module faulty |
| 46 | Intake manifold pressure at (in left ignition control module) faulty |
| 47 | Not used |
| 48 | Not used |
| 49 | Data exchange fault between left LH-SFI ignition control module |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 50 | Left adjustable camshaft timing solenoid circuit open or circuit short |
| 51 | Left injector circuit open or circuit short or emission control system adaptation in left LH-SFI control module at limit |
| 52 | Not used vehicle speed signal missing |
| 53 | Left purge switchover valve, circuit open or circuit short |
| 54 | Left camshaft position sensor signal faulty |
| 55 | Intake manifold pressure(in left ignition control module) with engine running too low/high |
| 56 | Starter ring gear segments and/or left crankshaft position sensor faulty |
| 57 | Knock sensors or left ignition control module faulty |
| 58 | Not used |
| 59 | Left engine coolant temperature sensor deviation between circuit 1, and sensor circuit 2. |
| 60 | Left engine coolant temperature sensor (engine coolant temperature change monitor) |

| Models | Model Year |
| --- | --- |
| 124.028 124.032 124.052 124.092 | 1994-95 |

Connect wires of Scanner as follows

| Scanner | Data link connector 16-pin |
| --- | --- |
| Yellow | Socket 3 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No Fault Found |
| 2 | Heated oxygen sensor faulty |
| 3 | Lambda control faulty |
| 4 | Air injection system faulty hot film mass air flow sensor with hot wire |
| 5 | Exhaust gas recirculation faulty |
| 6 | Idle speed control faulty |
| 7 | Ignition system faulty |
| 8 | Engine coolant temperature sensor open circuit |
| 9 | Intake air temperature sensor, open circuit |
| 10 | Voltage at mass air sensor too high/low |
| 11 | Tn-signal (rpm signal ) at engine control module faulty |
| 12 | Heated oxygen sensor heater circuit open or circuit short |
| 15 | Injector, cylinder 2 |
| 16 | Closed throttle position information faulty |
| 17 | Data exchange malfunction between individual control module |
| 18 | Adjustable camshaft timing solenoid circuit open or circuit short |
| 19 | Injectors circuit open or circuit short emission control module adaptation in engine control module at limit |
| 20 | Vehicle speed signal not present |
| 21 | Purge switchover valve circuit open or circuit short |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 22 | Crankshaft position sensor signal faulty |
| 23 | Intake manifold pressure (in base module pressure sensor-) with engine running too high/low. |
| 24 | Starter ring gear segments and /or crankshaft position sensor faulty |
| 25 | Knock sensors or engine control module faulty |
| 26 | Upshift delay faulty |
| 27 | Not used |
| 28 | Engine coolant temperature sensor (engine coolant temperature change monitor ) |
| 44 | Not used |
| 45 | Fuel safety shut-off electronic accelerator or cruise control active |
| 46 | Resonance intake manifold switchover valve |
| 47 | Not used |
| 48 | Not used |
| 49 | Voltage supply at engine control module 8v |
| 50 | Engine control module |

| Model | Model Years |
| --- | --- |
| 140.032 | 1992-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 17 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Maximum retard setting on at least one cylinder has been reached |
| 3 | Not used |
| 4 | Load sensor in ignition control module faulty. |
| 5 | Knock sensors 1 and/or 2 faulty. |
| 6 | Camshaft position sensor faulty. |
| 7 | Knock output switch in ignition control module faulty. |
| 8 | Transmission overload switch does not close. |
| 9 | Transmission overload switch does not open. |
| 10 | Not used. |
| 11 | Preference resistor faulty . |
| 12 | Tn-signal is outside the tolerance range. |
| 13 | Not used |
| 14 | Not used |
| 15 | Ignition coil 1 output from ignition control module faulty |
| 16 | Ignition coil 2 output from the DI defective or primary winding of the coil has an open circuit |
| 17 | Crankshaft position sensor faulty |
| 18 | Magnets for crankshaft position sensor (CKP) not recognized. |
| 19 | Not used |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 20 | Ignition control module DTC memory faulty |
| 21 | Load sensor in control module faulty. (Recognized with engine running) |
| 22 | Not used |
| 23 | Not used |
| 24 | Not used |
| 25 | Not used |
| 26 | Ignition control module data exchange fault |
| 27 | LH-SFI control module data exchange fault |
| 28 | Electronic accelerator control module/idle speed control data exchange fault |
| 34 | Ignition misfire detected at cylinder 1 (104) / cylinder 1 (119) |
| 35 | Ignition misfire detected at cylinder 5 (104) / cylinder 5 (119) |
| 36 | Ignition misfire detected at cylinder 3 (104) / cylinder 4 (119) |
| 37 | Ignition misfire detected at cylinder 6 (104) / cylinder 8 (119) |
| 38 | Ignition misfire detected at cylinder 2 (104) / cylinder 6 (119) |
| 39 | Ignition misfire detected at cylinder 4 (104) / cylinder 3 (119) |
| 40 | Ignition misfire detected at cylinder 7 (119) |
| 41 | Ignition misfire detected at cylinder 2 (119) |

| Model | Model Years |
| --- | --- |
| 124.051 | 1990-1995 |
| 129.061 129.066 | 1990-1995 |

Connect wires of Scanner as follows:

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 8 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Maximum retard setting on at least one cylinder has been reached |
| 3 | Engine coolant temperature sensor faulty |
| 4 | Load sensor in EAL/AKR control module faulty |
| 5 | Knock sensors 1 and/or 2 faulty |
| 6 | Camshaft position sensor faulty |
| 7 | Knock output switch in EAL/AKR ignition control module faulty |
| 8 | Transmission overload switch does not close |
| 9 | Transmission overload switch does not open |
| 10 | Data exchange from EAL/AKR engine control module to CFI control module faulty. |
| 11 | Preference resistor faulty |
| 12 | Tn-signal is outside the tolerance range |
| 13 | Full load contact does not open. |
| 14 | Idle speed contact does not open. |
| 15 | Ignition coil 1 output from EAL/AKR ignition control module faulty |
| 16 | Ignition coil 2 output from EAL/AKR ignition control module faulty |
| 17 | Crankshaft position sensor faulty |

| Models | Model Years |
| --- | --- |
| 124.034 | 124.036 | 1992-1995 |
| 129.067 | 129.076 | 1992-1995 |
| 140.042 | 140.043 | 140.051 | 140.057 | 140.070 | 140.076 | 1992-1995 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 17 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Maximum retard setting on at least one cylinder has been reached |
| 3 | Not used |
| 4 | Load sensor in EAL/AKR control module faulty |
| 5 | Knock sensors 1 and/or 2 faulty |
| 6 | Camshaft position sensor faulty |
| 7 | Knock output switch in ignition control module faulty |
| 8 | Transmission overload switch does not close |
| 9 | Transmission overload switch does not open |
| 10 | Not used |
| 11 | Reference resistor (ignition control module ) faulty |
| 12 | TN-signal (engine RPM) is outside the tolerance range |
| 13 | Not used |
| 14 | Not used |
| 15 | Ignition coil 1 output from ignition control module faulty or primary winding of ignition coil has open circuit |
| 16 | Ignition coil 2 output from ignition control module faulty or primary winding of ignition coil has open circuit |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 17 | Crankshaft position sensor faulty |
| 18 | Magnets for crankshaft position sensor not recognized |
| 19 | Ground, Coding from Left EZL/AKR Ignition Control Module Not Present |
| 20 | Ignition control module DTC memory faulty |
| 21 | Load sensor in control module faulty. (recognized with engine running) |
| 22 | Not used |
| 23 | Not used |
| 24 | Not used |
| 25 | Not used |
| 26 | Ignition control module data exchange fault |
| 27 | Control module data exchange fault |
| 28 | Electronic accelerator control module/idle speed control data exchange fault |

CCCCLLLLnnnn!!!!2222&&&&

CCCCoooouuuuJJJJLLLLoooollll\\\\ll

qqqqll

&&&&

2222bbbb&&&&&&qq

CCCCoooouuuuJJJJLLLLoooollll

((((CCCCCCCC\\\\llll2222CCCC))))

MMMM\\\\oooo

YYYY2222H'H'

| Models | Model Years |
| --- | --- |
| 124 | 129 | 140 | 202 | 1992-97 |

Connect wires of Scanner as follows (W124)

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 14 |
| Black | Socket 1 |
| Red | Socket 16 |

Connect wires of Scanner as follows (129  140  202)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 7 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Cruise control/idle speed control module |
| 3 | Cruise control/idle speed control actuator |
| 4 | Cruise control switch |
| 5 | Stop lamp switch |
| 6 | Starter lock-out/backup lamp switch |
| 7 | Data bus (CAN) |
| 8 | Left front axle vehicle speed sensor |
| 9 | Left rear axle vehicle speed sensor or Hall-effect speed sensor Rear axle vehicle speed sensor from ABS control module Rear axle vehicle speed sensor from ETS/SPS control module Incorrect CC/ISC control module installed ETS signal |
| 10 | Engine speed (RPM) signal (TNA) |
| 11 | Fuel safety shut-off to LH-SFI control module |
| 12 | Cruise control/idle speed control voltage supply |

El&c.J1ou!c Ycc&l&1s.Jo1 \ C1n!2& Cou.J1ol \ 1ql& 2b&&q Cou.J1ol (EY\CC\12C) M\Y2H

| Models | Model Year |
| --- | --- |
| 124 | 129 | 140 | 202 | 1992-96 |

Connect wires of Scanner as follows (W124)

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 14 |
| Black | Socket 1 |
| Red | Socket 16 |

Connect wires of Scanner as follows (W202  W129  W140)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 7 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | EA/CC/ISC control module (N4/1) or Safety contact switch (M16/1s1) or Stop lamp switch or Cruise control switch or Actual value potentiometer or Starter lock-out/back-up lamp switch or engine speed signal or vehicle speed signal or closed throttle position switch or safety relay in EA/CC/ISC control module |
| 3 | Right EA/CC/ISC actuator (left cylinder bank) (M16/1) |
| 4 | Cruise control switch (S40) |
| 5 | Stop lamp switch (S9/1) |
| 6 | Starter lock-out/backup lamp switch |
| 7 | CAN data bus signal from EA/CC/ISC, ABS/ASR, HFM-SFI or LH-SFI (right or left) control module faulty. |
| 8 | Left front axle vehicle speed sensor from ABS/ASR control module |
| 9 | Left rear axle vehicle speed sensor from ABS/ASR control module or in 124 chassis Hall-effect speed sensor. |
| 10 | Engine speed signal (TN) from base module (LH-SFI) or engine control module (HFM- SFI) |

| 11 | Closed throttle recognition signal to engine control module (HFM-SFI or Left LH-SFI) Fuel safety shut-off to engine control module (HFM-SFI or left or right LH-SFI) |
| --- | --- |
| 12 | EA/CC/ISC control module voltage supply |
| 13 | Left EA/CC/ISC actuator (right cylinder bank) or actual value potentiometer (M16/4r1 or M16/4r2) or actuator motor (M16/4m1)or magnetic clutch (M16/4k1). |
| 14 | Closed throttle position contact switch |
| 15 | CAN data exchange with ABS/ASR control module illogical |

| Models | Model Years |
| --- | --- |
| 129 | 1990-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 13 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Not used |
| 3 | Engine load signal interrupted |
| 4 | Throttle valve switch (potentiometer) interrupted |
| 5 | Engine speed (RPM) signal interrupted |
| 6 | Vehicle speed signal interrupted |
| 7 | Output fault in 5-speed automatic transmission control module or fault in control valve. |
| 8 | 5-speed automatic transmission control module |
| 9 | Control valve |
| 10 | Control valve short circuit |

El&clLou!c Ynlowsl!c .1Lsu2w!22!ou CoulLol (E.1C) M\rH-21:1

| Model | Model Years |
| --- | --- |
| 129 | 1990-1993 |
| 140 | 1990-1996 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 10 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Not used |
| 3 | Transmission overload protection switch (4/5 gear) faulty |
| 4 | CAN data line to Electronic Accelerator/Cruise Control Module |
| 5 | CAN data line to ignition control module (knock sensor) |
| 6 | CAN data line - short or open circuit |
| 7 | Open circuit at control valve or transmission control module (5-speed automatic ) |
| 8 | 5-speed automatic transmission control module |
| 9 | Control valve faulty |
| 10 | Control valve short circuit |

Also test BM and DI systems.

YYYYnnnnJJJJoooowwwwssssJJJJ!!!!cccc----ssssuuuuaa

ssaa

ssqqqq

l:l:l:l:oooonnnnLLLL----MM

l'l'

ssssssllll

DDDDLLLL!!!!AAAAssss

((((����WWWWYYYY.l.l.l.lllllCC

))))

| Models | Model Years |
| --- | --- |
| 124.230 124.290 | 1990-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 5 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | 4MATIC control module |
| 3 | Brake light switch |
| 4 | Left front axle vehicle speed sensor |
| 5 | Right front axle vehicle speed sensor |
| 6 | Rear speed sensor signal |
| 7 | All 3 vehicle speed sensors |
| 8 | Over volts protection relay, front axle train valve |
| 9 | Over volts protection relay, central differential lock valve |
| 10 | Over volts protection relay, stop lamp switch, Rear axle differential lock valve |
| 11 | Steering angle sensor signal |

| Models | Model Years |
| --- | --- |
| 129.061 129.066 | 1991-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 9 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Adaptive damping system control module |
| 3 | Body acceleration sensor |
| 4 | Wheel acceleration sensor |
| 5 | Steering angle sensor |
| 6 | Front axle solenoid valves 1 |
| 7 | Front axle solenoid valves 2 |
| 8 | Rear axle solenoid valves 1 |
| 9 | Rear axle solenoid valves 2 |
| 10 | Not used |
| 11 | Not used |
| 12 | ABS signal |
| 13 | Oil level switch (ADS) |
| 14 | Steering angle sensor not activated |

| Models | Model Years |
| --- | --- |
| 129.067 129.076 | 1991-1995 |

Connect wires of Scanner as follows

| Scanner | Data link connector 38-pin |
| --- | --- |
| Yellow | Socket 11 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 1 | No fault found |
| 2 | Adaptive damping system control module |
| 3 | Body acceleration sensor |
| 4 | Wheel acceleration sensor |
| 5 | Steering angle sensor |
| 6 | Front axle solenoid valves 1 |
| 7 | Front axle solenoid valves 2 |
| 8 | Rear axle solenoid valves 1 |
| 9 | Rear axle solenoid valves 2 |
| 12 | Right front axle vehicle speed signal |
| 13 | Oil level switch (ADS) |
| 14 | Steering angle sensor not activated/initialized |
| 15 | Comfort or sport switch (ADS) short circuit |
| 17 | Vehicle load sensor |
| 18 | Adaptive damping system warning lamp |
| 19 | Volts supply too low |
| 20 | Steering angle sensor |
| 21 | Volts supply too high |
| 22 | Comfort or sport switch (ADS) |

| Models | Model Years |
| --- | --- |
| 140.032 140.042 140.051 140.057 140.070 140.076 140.134 | 1991-1994 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 11 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 1 | No fault found |
| 2 | Adaptive damping system control module |
| 3 | Body acceleration sensor |
| 4 | Wheel acceleration sensor |
| 5 | Steering angle sensor |
| 6 | Front axle solenoid valves 1 |
| 7 | Front axle solenoid valves 2 |
| 8 | Rear axle solenoid valves 1 |
| 9 | Rear axle solenoid valves 2 |
| 12 | Right front axle vehicle speed signal |
| 13 | Oil level switch (ADS) |
| 14 | Steering angle sensor not activated |
| 15 | Comfort or sport switch (ADS) |
| 17 | Vehicle load sensor |
| 18 | Adaptive damping system warning lamp |
| 19 | Volts supply too low |
| 20 | Steering angle sensor |
| 21 | Volts supply too high |
| 22 | Comfort or sport switch (ADS) |

YYYYnnnnlllloooowwwwssssllll!!

cccc

rrrrooooccccl<l<l<l<!!!!uuuuaaaa

DDDD!!!!   &&&&LLLL&&

uull

!!ssssll

((((YYYY2222DDDD))))

| Models | Model Years |
| --- | --- |
| 124.128 | 1991-1995 |
| 126.134 126.135 | 1991 |
| 129.061 | 1991-1995 |
| 140.134 | 1991-1995 |
| 201.028 | 1991-1993 |

Connect wires of Scanner as follows (Model 124 126 129)

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 5 |
| Black | Socket 1 |
| Red | Battery (+) |

Connect wires of Scanner as follows (Model 140.134)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 9 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible cause of faults |
| --- | --- |
| 1 | No fault found |
| 2 | Adaptive damping system control module |
| 3 | Stop lamp switch |
| 4 | Left front axle vehicle speed sensor signal |
| 5 | Right front axle vehicle speed sensor signal |
| 6 | Rear speed sensor signal |
| 7 | No speed signal from any sensor, missing ground |
| 8 | Adaptive damping system valve or stop lamp switch |

VVVVUUUU++++!!!!····IIIIOO

CCI'-I'-I'-I'-

tstststslll9999I'-I'-I'-I'-6666

����AAAA2222++++6666WWWW

llllVVVVtstststs����JJJJ

| Models | Model Years |
| --- | --- |
| 140.032 140.042 140.043 140.134 | 1992-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 6 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 1 | No faults found |
| 2 | Left front axle vehicle speed sensor signal |
| 3 | Right front axle vehicle speed sensor signal |
| 4 | Rear axle speed sensor signal |
| 6 | Left front axle solenoid valve |
| 7 | Right front axle solenoid valve |
| 8 | Rear axle solenoid valve |
| 10 | Return/pressure pump motor or return/pressure pump relay |
| 11 | Solenoid valves relay |
| 12 | Master cylinder switchover valve |
| 13 | Stop lamp switch |
| 14 | ABS Lateral acceleration sensor |
| 15 | ABS control module |
| 16 | Vehicle speed sensors incorrect, dirty or damaged toothed rotor |
| 17 | Low voltage at solenoid valves relay |

YYYYuuuuJJJJ!!!!----llllooooccccllllllll

BBBBlllssssllllllll&&&&

2222AAAA2222JJJJ&&&&wwww

((((YYYYBBBB2222

����

YYYYBBBB2222

MMMM\\\\YYYY2222HHHH))))

| Models | Model Years |
| --- | --- |
| 124.034 | 124.036 | 1992-1995 |
| 140.032 | 140.042 | 140.051 | 140.057 | 140.070 | 140.076 | 1992-1995 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 6 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 1 | No fault found |
| 2 | Left front axle vehicle speed sensor signal |
| 3 | Right front axle vehicle speed sensor signal |
| 4 | Left rear axle vehicle speed sensor signal |
| 5 | Right rear axle vehicle speed sensor signal |
| 6 | Left front axle solenoid valve |
| 7 | Right front axle solenoid valve |
| 8 | Left rear axle solenoid valve |
| 9 | Right rear axle solenoid valve |
| 10 | Return/pressure pump motor or return/pressure pump relay |
| 11 | Solenoid valves relay |
| 12 | Models 140.04/05 Master cylinder switchover valve |
| 13 | Stop lamp switch(ASD/ASR) |
| 14 | Models140.04/05 ABS lateral acceleration sensor |
| 15 | ABS/ASR control module |
| 16 | Vehicle speed sensors incorrect, dirty or damaged toothed rotor |
| 17 | Low volts at solenoid valves relay |
| 20 | Switchover or solenoid valve |

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 21 | Pressure switch charge |
| 22 | Pressure switch charge |
| 23 | Pressure switch hydraulic system |
| 24 | ASR charging pump |
| 30 | CAN data line to electronic accelerator/cruise control/idle speed control module |
| 31 | CAN data line to LH-SFI control module left LH-SFI control module Right LH-SFI control module |
| 32 | CAN data line to left ignition control module right ignition control module Ignition control module, LH-SFI |
| 33 | CAN data line, short or open circuit |

VVVVUUUU++++!!!!····IIIIOO

CCI'-I'-I'-I'-

tstststslll9999I'-I'-I'-I'-6666

����AAAA2222++++6666WWWW

llllVVVVtstststs����JJJJ

| Model | Model Years |
| --- | --- |
| 202 210 | 1994-95 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 6 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 1 | No fault found |
| 2 | Left front axle vehicle speed sensor, open circuit |
| 3 | Right front axle vehicle speed sensor, open circuit |
| 4 | Rear speed sensor, open circuit |
| 6 | Solenoid valve, Left front axle |
| 7 | Solenoid valve, Right front axle |
| 8 | Solenoid valve, Rear axle |
| 10 | Return/pressure pump motor or return/pressure pump relay |
| 11 | Solenoid valves relay |
| 15 | ABS control module |
| 16 | Vehicle speed sensors |
| 17 | Battery volts low |
| 25 | Left front vehicle speed sensors signal Illogical |
| 26 | Right front vehicle speed sensors signal Illogical |
| 27 | Rear front vehicle speed sensors signal Illogical |

YYYYuuuuJJJJ!!!!----llllooooccccllllllll

BBBBlllssssllllllll&&&&

2222AAAA2222JJJJ&&&&wwww

((((YYYYBBBB2222

����

YYYYBBBB2222

MMMM\\\\YYYY2222HHHH))))

| Models | Model Year |
| --- | --- |
| 124.034 | 1994-95 |
| 129 | 1994-95 |
| 140 | 1994-95 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 6 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 1 | No fault found |
| 2 | Left front axle vehicle speed sensor, open circuit |
| 3 | Right front axle vehicle speed sensor, open circuit |
| 4 | Rear speed sensor, open circuit |
| 6 | Left front axle solenoid valves |
| 7 | Right front axle solenoid valves |
| 8 | Solenoid valve, rear axle |
| 10 | Return pump motor or return pump relay |
| 11 | Solenoid valves relay |
| 12 | Models140.04/05Master cylinder switchover valve |
| 13 | Brake lamp switch |
| 14 | Models140.04/05 Lateral acceleration sensor |
| 15 | ABS control module |
| 16 | Vehicle speed sensors signal Illogical |
| 17 | Solenoid valves relay |
| 25 | Left front vehicle speed sensors signal, Illogical |
| 26 | Right front vehicle speed sensors signal, Illogical |
| 27 | Rear front vehicle speed sensors signal, Illogical |
| 29 | Models140.04/05 Lateral acceleration sensor signal, Illogical |

EEEEllllaaaaccccllllLLLLoooouu

!!cccc

.1.1.1.1LLLLssssccccllll!!!!oooouuuu

2222AA

2222llllaa

wwww2222

((((YYYY2222HHHHaaaa

EEEE.1.1.1.12222))))

| Models | Model Years |
| --- | --- |
| 129 | 140 | 202 | 1995 |
| 210 | 1995-96 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 6 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 1 | No fault found |
| 2 | ASR/SPS or ETS/SPS control module |
| 3 | Left front axle VSS sensor, open circuit |
| 4 | Right front axle VSS sensor, open circuit |
| 5 | Left rear axle VSS sensor, open circuit |
| 6 | Right rear axle VSS sensor, open circuit |
| 7 | Left front axle VSS valves, illogical |
| 8 | Right front axle VSS valves illogical |
| 9 | Left rear axle VSS valve illogical |
| 10 | Right rear axle VSS valve illogical |
| 11 | VSS signal illogical |
| 12 | ASR/ETS hydraulic unit, solenoid valves relay |
| 13 | ASR/ETS hydraulic unit, Left front axle solenoid valves(hold) |
| 14 | ASR/ETS hydraulic unit, Left front axle solenoid valve(hold) |
| 15 | ASR/ETS hydraulic unit, right front axle solenoid valve (release) |
| 16 | ASR/ETS hydraulic unit, right front axle solenoid valve (release) |
| 17 | ASR/ETS hydraulic unit, left rear axle solenoid valve(hold) |
| 18 | ASR/ETS hydraulic unit, left rear axle solenoid valve (release) |

| DTC Readout | Possible Cause of Faults |
| --- | --- |
| 19 | ASR/ETS hydraulic unit, right rear axle solenoid valve(hold) |
| 20 | ASR/ETS hydraulic unit, right rear axle solenoid valve (release) |
| 21 | ASR/ETS hydraulic unit, switchover/solenoid valve |
| 22 | ASR/ETS hydraulic unit, inlet solenoid valve |
| 23 | ASR only: ASR system pressure too low |
| 24 | ASR/ETS hydraulic unit, high-pressure/return pump relay |
| 27 | Stop lamp switch |
| 28 | Battery voltage too low, circuit 87 |
| 29 | ETS only Circuit 30, volts supply |
| 30 | ASR only CAN date bus to EA/CC/ISC control module, interrupted |
| 31 | ASR only CAN communication with LH-SFI control module Left LH-SFI control module right LH-SFI control module faulty CAN communication with engine control module faulty |
| 32 | ASR only CAN communication with DI or left and right DI control module, faulty |
| 33 | ASR only CAN communication faulty in general |
| 34 | ETS only Brakes overheated |
| 35 | Model 129.076,140.04/05/07 Master brake cylinder switchover valve |
| 36 | Model 129.076,140.04/05/07 ASR lateral acceleration sensor, open circuit |
| 37 | Model 129.076,140.04/05/07 ASR lateral acceleration sensor, illogical |
| 38 | ETS only EST/SPS control module not identify the software (not coded) |
| 39 | Model 140/210 ETS/SPS or ASR/SPS control module |
| 40 | Model 140 SPS P-valve |
| 41 | Model 140/210 ASR/SPS or ETS/SPS control module |

| Models | Model Years |
| --- | --- |
| 140.032 140.042 140.051 140.057 140.070 140.076 140.134 | 1992-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 12 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Speed sensitive power steering control module |
| 3 | Left/center rear axle speed sensor signal |
| 4 | Right rear axle vehicle speed sensor signal |
| 5 | Diffident vehicle speed signals from right and left rear axle sensor |
| 6 | No vehicle speed sensor signal |
| 7 | Inductive speed sensor, transmission faulty |
| 8 | Short circuit between positive connection of speed sensitive power steering valve and ground (-) |
| 9 | Short circuit at speed sensitive power steering valve |
| 10 | Open circuit at speed sensitive power steering valve |
| 11 | Volts supply at speed sensitive power steering control module |

| Model | Model Years |
| --- | --- |
| 140 | 1994 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 12 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Speed sensitive power steering control module |
| 3 | Comparison of axle vehicle speed signal attars/left front axle vehicle speed signal faulty |
| 4 | Axle vehicle speed signal status missing |
| 5 | Speed-sensitive power steering control module |
| 6 | Speed-sensitive power steering P-valve; short circuit |
| 7 | Speed-sensitive power steering P-valve; open circuit |
| 8 | Short circuit between speed sensitive power steering P-valve (+) and ground (-) |

CCCCssssPPPPLLLL!!!!oooollss

llll

2222oooo llll

lllloooobbbb

((((CCCC2222.1.1.1.1))))

| Model | Model Years |
| --- | --- |
| 124.066 | 1993-95 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector |
| --- | --- |
| Yellow | Power Soft top test connection (4 pole) at Socket 2. The connection is located at the right front passenger footwell. To avoid the need for an extension cable, connect the black lead of code scanner to any good ground and red lead to a battery + source inside vehicle. |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Volts low |
| 3 | Normal operating time exceeded |
| 4 | Limit switch signals Illogical |
| 5 | Soft top compartment cover "locked", limit switch, |
| 6 | Soft top compartment cover "closed", limit switch, |
| 7 | Soft top compartment cover "open", limit switch |
| 8 | Soft top fabric bow "locked", limit switch |
| 9 | Soft top fabric bow "down", limit switch |
| 10 | Soft top fabric bow "raised", limit switch |
| 11 | Left front soft top "locked", limit switch |
| 12 | Right front soft top "locked", limit switch |
| 13 | Soft top "open" switch (soft top in storage compartment), limit switch , |
| 14 | Soft top "overhead", limit switch |
| 15 | Soft top "retracted", limit switch |
| 16 | Roll bar "extended", limit switch, |
| 17 | Automatic deployment of roll bar has occurred |
| 18 | Power soft top switch |
| 19 | Vehicle speed signal |
| 20 | Circuit in power soft top control module, solenoid valve, roll bar retracted |
| 21 | Circuit hydraulic unit, circuit solenoid valve, roll bar retracted |
| 22 | Circuit in power soft top control module, solenoid valve, roll bar extended |
| 23 | Circuit solenoid valve, roll bar extended |
| 24 | Circuit in power soft top control module, Power windows |

| Model | Model Year |
| --- | --- |
| 124.066 | 1993-95 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 9 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No faults found |
| 2 | Roll bar control module |
| 3 | Roll bar control module volts supply |
| 6 | Roll bar deployment solenoid, open circuit, short circuit to Battery + or ground (-). |
| 7 | Rear axle switch, short circuit to Battery + or ground (-). |
| 8 | Roll bar indicator lamp faulty |

| Models | Model Years |
| --- | --- |
| 129.061 129.066 129.067 129.076 | 1990-12/93 |

Connect wires of Scanner as follows (Model 129.061/066)

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 7 |
| Black | Socket 1 |
| Red | Socket 16 |

Connect wires of Scanner as follows (Model 129.067/076, all 129 from 1993)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 22 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No faults found |
| 2 | Roll bar control module |
| 3 | Volts supply |
| 4 | Driver seat belt lock relay open circuit or short circuit to Battery + or ground (-). |
| 5 | Passenger seat belt lock relay open circuit or short circuit to Battery + or ground (-). |
| 6 | Roll bar deployment solenoid, open circuit or short circuit to Battery + or ground (-). |
| 7 | Left and/or right axle switch, roll bar, short circuit to 30 or 31 |
| 8 | Roll bar warning lamp |
| 9 | SRS warning lamp and/or code scanner button held to erase faulty |
| 10 | SRS control unit |

| Models | Model Years |
| --- | --- |
| 129.061 129.066 129.067 129.076 | 1990-12/93 |

Connect wires of Scanner as follows (Model 129.061/066)

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 10 |
| Black | Socket 1 |
| Red | Socket 160 |

Connect wires of Scanner as follows (Model 129.067/076, all 129 from 1993)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 21 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No faults stored |
| 2 | Limit switch, left locked, soft top storage compartment cover |
| 3 | Limit switch, right locked, soft top storage compartment cover |
| 4 | Limit switch, left closed, soft top storage compartment cover |
| 5 | Limit switch, right closed, soft top storage compartment cover |
| 6 | Limit switch, left locked, soft top fabric bow |
| 7 | Limit switch, right locked, soft top fabric bow |
| 8 | Limit switch, left closed, soft top fabric bow |
| 9 | Limit switch, right closed, soft top fabric bow |
| 10 | Limit switch, left front locked, soft top |
| 11 | Limit switch, right front locked, soft top |
| 12 | Limit switch soft top storage compartment cover open |
| 13 | Limit switch soft top fabric bow raised |
| 14 | Limit switch soft top down (in storage compartment) |
| 15 | Limit switch soft top up (secondary closing speed ) |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 16 | Limit switch roll bar retracted |
| 17 | Limit switch left side window down Circuit in power soft top control module, solenoid valve, roll bar retracted |
| 18 | Limit switch right side window down Circuit hydraulic unit, circuit solenoid valve, roll bar retracted |
| 19 | Axle vehicle speed signal illogical Circuit in power soft top control module, solenoid valve, roll bar extended |
| 20 | Hardtop installed recognition Circuit solenoid valve, roll bar extended |
| 21 | Power soft top switch Circuit in power soft top control module, Power windows |
| 22 | Roll bar switch |
| 23 | Roll bar control module |
| 24 | Roll bar crash deployment |
| 25 | Limit switch signals illogical |
| 26 | Operation time exceeded |
| 27 | Insufficient volts |
| 28 | No speedometer signal |
| 29 | No axle vehicle wheel speed sensor signal |
| 30 | Soft top operation blocked |

| Model | Model Years |
| --- | --- |
| 129 | 1/94-6/96 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 21 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No faults stored |
| 2 | Low voltage |
| 3 | RST/RB hydraulic unit locked up. |
| 4 | Vehicle speed sensor fault |
| 5 | RST/RB hydraulic unit |
| 6 | Right or left power window activation |
| 7 | Right or left front soft top “locked” switch fault, Soft top open/closed switch, Fabric bow locked switch, |
| 8 | Power soft top control module defective |
| 9 | Roll bar crash deployment has occurred |
| 10 | Power soft top switch or Roll bar switch. |
| 11 | Power soft top switch indicator lamp or Roll bar switch indicator lamp or Warning buzzer. |

| Models | Model Years |
| --- | --- |
| 129.061 129.066 129.067 129.076 | 1990-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 12 |
| Black | Socket 1 |
| Red | Socket 16 |

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 31 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Infrared remote control module |
| 3 | Supply pump, central locking system short to ground |
| 4 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Red indicator lamps, short to ground |
| 5 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Green indicator lamps, short to ground |
| 6 | Supply pump, central locking system, short to circuit 30 |
| 7 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Red indicator lamps, short to circuit 30 or open circuit |
| 8 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Green indicator lamps, in receiver have short to short to circuit 30 or open circuit |
| 9 | Driver door switch group wiring, short to circuit 30 ATA/convenience microswitch wiring short to circuit 30 ATA/convenience microswitch wiring short to circuit 30 |
| 10 | Ignition/starter switch-position recognition switch, open circuit |
| 11 | Ignition/starter switch-position recognition switch, open circuit 31 |
| 12 | Left front door actuator, open circuit |
| 13 | Right door actuator, open circuit |
| 14 | Trunk lid lock actuator, open circuit |

| Model | Model Years |
| --- | --- |
| 140 | 1992-96 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 31 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Left front door actuator, open circuit |
| 3 | Warning buzzer -open circuit |
| 4 | Warning buzzer -open circuit to ground |
| 5 | Red indicator lamps, short to ground |
| 6 | Green indicator lamps, short to ground |
| 7 | Short to positive, lock circuit 1 |
| 8 | Short to positive, lock circuit 2 |
| 9 | Red indicator lamps, short to positive |
| 10 | Green indicator lamps, short to positive |
| 11 | Infrared remote control module faulty |
| 12 | Immobilization output, short to circuit 30 (Battery +) |

| Model | Model Years |
| --- | --- |
| 129 | 1993-96 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 31 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | IRCL control module |
| 3 | Supply pump, central locking system short to ground |
| 4 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Red indicator lamps, short to ground |
| 5 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Green indicator lamps, short to ground |
| 6 | Supply pump, central locking system, short to B (+) |
| 7 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Red indicator lamps , short to B (+) or open circuit |
| 8 | Infrared remote control receiver, Left front door/Right front door/Trunk lid Green indicator lamps, short to B (+) or open circuit |
| 9 | Driver door switch group wiring, short to B (+) ATA/CF microswitch wiring short to B (+) ATA/CF microswitch wiring short to B (+) |
| 10 | Ignition/starter switch-position recognition switch, open circuit |
| 11 | Ignition/starter switch-position recognition switch, open circuit 31 |
| 12 | Left front door actuator, open circuit |
| 13 | Right door actuator, open circuit |
| 14 | Trunk lid lock actuator, open circuit |
| 15 | Immobilization output, short to B (+) |

| Models | Model Years |
| --- | --- |
| 129 140 | 1992-94 |

Connect wires of Scanner as follows

| Scanner | Data link connector 38-pin |
| --- | --- |
| Yellow | Socket 20 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Central locking system, air demand too high, leakage |
| 3 | Retractable trunk lid grip, air demand too high, leakage |
| 4 | Backup assist, air demand too high, leakage |
| 5 | Orthopedic backrest pressure, air demand too high, leakage |
| 6 | Manifold vacuum assist, air demand too high, leakage |
| 7 | Short to positive, lock circuit 1 |
| 8 | Short to positive, lock circuit 2 |
| 9 | Signal fault, Rear head restraint retraction |
| 10 | Signal fault, Central locking interior control switch |
| 11 | Signal fault, Front door |
| 12 | Signal from lock circuit 1 is present for longer than 2 minutes |
| 13 | Signal from lock circuit 2 is present for longer than 2 minutes, |
| 14 | Central locking interior control switch signal is present for longer than 2 minutes |
| 15 | Rear head restraint retraction signal is present for longer than 2 minutes |
| 16 | Not used |
| 17 | Pneumatic control module faulty |

| Models | Model Years |
| --- | --- |
| 129.061 129.066 129.067 129.076 | 1990-93 |
| 140.032 140.042 140.051 140.057 140.070 140.076 140.134 | 1990-93 |
| 129 140 202 | 1994-96 |

Connect wires of Scanner as follows (Model 129.061, 129.066)

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 11 |
| Black | Socket 1 |
| Red | Battery (+) |

Connect wires of Scanner as follows (Model 129, 140, 202)

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 23 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Alarm activated, trunk sensor circuit |
| 3 | Alarm activated, engine hood circuit |
| 4 | Alarm triggered, glove compartment |
| 5 | Alarm activated, rear door circuit Console compartment circuit |
| 6 | Alarm activated, front door circuit |
| 10 | Alarm activated, radio circuit |
| 12 | Alarm activated, ignition circuit |
| 14 | Alarm activated, brake circuit |
| 19 | AT Control module faulty |
| 20 | Left front door actuator, No ground connection |
| 21 | ATA disarmed, Starter lock-out relay module. short to circuit 30 |
| 23 | ATA armed, Open to circuit 30 |

| Models | Model Years |
| --- | --- |
| 129.061 | 129.066 | 129.067 | 129.076 | 1992-95 |
| 140.032 | 140.042 | 140.051 | 140.057 | 140.070 | 140.076 | 140.134 | 1992-95 |

If a fault code is set, the code is shown on the in-car telephones display and the phone goes off-line.

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | TR memory defect (ROM) |
| 2 | TR memory defect (RAM) |
| 3 | NAM defect |
| 4 | ESN defect |
| 5 | TR memory defect (EE PROM) |
| 6 | TR output power defect |
| 7 | IDCM defect |
| 8 | TR output power control defect |

CCCCoooouuuuAAAAssssuuuu!!!!ssssuu

ccssss

l:l:l:l:ssssssssJJJJnnnnLLLLssss2222

((((CCCCl:l:l:l:))))

| Model | Model Year |
| --- | --- |
| 140 | 1992-96 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 21 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Control module, Close circuit for left front power window motor |
| 3 | Control module, Open circuit for left front power window motor |
| 4 | Control module, Close circuit for right front power window motor |
| 5 | Control module, Open circuit for right front power window motor |
| 6 | Control module, Close circuit for left rear power window motor |
| 7 | Control module, Open circuit for left rear front power window motor |
| 8 | Control module, Close circuit for right rear power window motor |
| 9 | Control module, Open circuit for right rear power window motor |
| 10 | Switch for left front power window Closing time exceeded |
| 11 | Switch for left front power window Opening time exceeded |
| 12 | Switch for right front power window Closing time exceeded |
| 13 | Switch for right front power window Opening time exceeded |
| 14 | Left rear power window circuit and left rear power window switch front console closing time exceeded |
| 15 | Left rear power window circuit and left rear power window switch front console opening time exceeded |
| 16 | Right rear power window circuit and right rear power window switch front console closing time exceeded |
| 17 | Right rear power window circuit and right rear power window switch front console opening time exceeded |
| 18 | Circuit for left front lock switch, right front, trunk lid lock switch closing time exceeded, lock switch circuit 2 |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 19 | Circuit for left front lock switch, right front, trunk lid lock switch opening time exceeded, lock switch circuit 1 |
| 20 | Left front power window switch short to ground or wires reversed |
| 21 | Right front power window switch short to ground or wires reversed |
| 22 | Left rear window circuit and left rear power window switch front console short to ground or wires reversed |
| 23 | Right rear power window circuit and right rear power window switch front console short to ground or wires reversed |
| 24 | Left front power window motor , wiring or speed sensor |
| 25 | Right front power window motor, wiring or speed sensor |
| 26 | Left rear power window motor, wiring or speed sensor |
| 27 | Right rear power window motor, wiring or speed sensor |
| 28 | Left front power window motor, sensor wiring reversed |
| 29 | Right front power window motor, sensor wiring reversed |
| 30 | Left rear power window motor, sensor wiring reversed |
| 31 | Right rear power window motor, sensor wiring reversed |
| 32 | Left front power window motor, Speed sensor signal faulty |
| 33 | Right front power window motor, Speed sensor signal faulty |
| 34 | Left rear power window motor, Speed sensor signal faulty |
| 35 | Right rear power window motor, Speed sensor signal faulty |
| 36 | Convenience control module faulty |
| 37 | Volts too low(9V), circuit 30E fuse F4-11 |
| 38 | Sliding/pop-up roof switch circuit short, check wiring harness |
| 39 | Volts supply circuit 30 A, control module |
| 40 | Volts supply circuit 30 B, control module |

| Models | Model Year |
| --- | --- |
| 201.028 | 201.029 | 201.034 | 201.126 | 201.128 | 1988-93 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | In car temperature sensor, short circuit |
| 3 | In car temperature sensor, open circuit |
| 4 | Outside temperature sensor, short circuit |
| 5 | Outside temperature sensor, open circuit |
| 6 | Evaporator temperature sensor, short circuit |
| 7 | Evaporator temperature sensor, open circuit |
| 12 | Coolant temperature gauge sensor, short circuit |
| 13 | Coolant temperature gauge sensor, open circuit |
| 14 | Feedback potentiometer, short circuit |
| 15 | Feedback potentiometer, open circuit |
| 30 | Coolant pump, short circuit |
| 33 | A/C compressor control module, short circuit |
| 34 | Auxiliary fan relay short circuit |
| 50 | Switchover valve unit (5 connections) between pins 5 and 4 faulty |
| 51 | Switchover valve unit (5 connections) between pins 5 and 6 faulty |
| 52 | Switchover valve unit (5 connections) between pins 5 and 2 faulty |
| 54 | Switchover valve unit (5 connections) between pins 5 and 3 faulty |
| 55 | Switchover valve unit (4 connections) between pins 5 and 1 faulty |
| 56 | Switchover valve unit (4 connections) between pins 5 and 2 faulty |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 57 | Switchover valve unit (4 connections) between pins 5 and 1 faulty |
| 58 | Switchover valve blend air flaps (warm) short circuit |
| 59 | Switchover valve blend air flaps (cold) short circuit |
| 60 | Switchover valve blend air flaps (closes) short circuit |
| 61 | Blower switch, low speed faulty |
| 62 | Blower switch, high speed faulty |

| Models | Model Year |
| --- | --- |
| 124.034 124.036 | 1992-1995 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 16 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Short circuit, In car temperature sensor |
| 3 | Open circuit, In car temperature sensor |
| 4 | Short circuit, Outside temperature sensor |
| 5 | Open circuit, Outside temperature sensor |
| 6 | Short circuit, Evaporator temperature sensor |
| 7 | Open circuit, Evaporator temperature sensor |
| 8 | Short circuit Left heat exchanger temperature sensor |
| 9 | Left heat exchanger sensor, open |
| 10 | Right heat exchanger temperature sensor, short circuit |
| 11 | Right heat exchanger temperature sensor, open |
| 12 | Engine coolant temperature sensor, short circuit |
| 13 | Engine coolant temperature sensor, open circuit |
| 30 | Circulation pump, short or open circuit |
| 31/32 | Duo valve short circuit/open |
| 33 | compressor cut-out control module short circuit/open |
| 34 | Auxiliary fan 2nd stage (actuation), short circuit |
| 56 | Switchover valve fresh air/recirculated air flaps, long stroke short circuit |
| 57 | Switchover valve fresh air/recalculated air flaps, long stroke short circuit |

YYYY\\\\CCCC

| Models | Model Years |
| --- | --- |
| 124.026 | 124.030 | 124.050 | 124.090 | 124.051 | 124.230 | 124.290 | 1988-95 |
| 126.024 | 126.025 | 126.035 | 126.039 | 126.045 | 126.134 | 126.135 | 1988-91 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 7 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | In car temperature sensor, short circuit |
| 3 | In car temperature sensor, open circuit |
| 4 | Outside temperature sensor, short circuit |
| 5 | Outside temperature sensor, open circuit |
| 6 | Evaporator temperature sensor, short circuit |
| 7 | Evaporator temperature sensor, open circuit |
| 8 | Heater core temperature sensor, short-circuit |
| 9 | Heater core sensor, open |
| 12 | Engine coolant temperature sensor, short circuit |
| 13 | Engine coolant temperature sensor, open circuit |
| 30 | Coolant pump, short circuit |
| 31 | Duo valve short circuit/open |
| 33 | A/C compressor control module short circuit |
| 34 | Auxiliary fan relay faulty |
| 50 | Switchover valve unit, faulty at between pins 5 and 8 (7 connections) |
| 51 | Switchover valve unit, faulty between pins 8 and 7 (7 connections) |
| 52 | Switchover valve unit, faulty between pins 8 and 3(7 connections) |
| 54 | Switchover valve unit, faulty between pins 8 and 4 (7 connections) |
| 55 | Switchover valve unit, faulty between pins 8 and 6(7 connections) |
| 56 | Switchover valve unit, faulty between pins 8 and 2(7 connections) |
| 57 | Switchover valve unit, faulty between pins 8 and 1(7 connections) |

J.J.J.J.YYYY

READING ACTUAL VALUES

Remove the operating console from the TAU

At the upper side of the operating consol there is a display.

Ignition ON : Position 1

The fan speed selector NOT on position 1

The display alternates between the sensor/component number and the value of that sensor/component. Example:  "OP E" : Open circuit or "CL O" : Closed circuit.

COMPONENT UNDER TEST

| Number | Component |
| --- | --- |
| 02 | Interior Temperature Sensor |
| 04 | Exterior Temperature Sensor |
| 06 | Evaporator Temperature Sensor |
| 08 | Left Heater Core Temperature Sensor |
| 10 | Right Heater Core Temperature Sensor |
| 12 | Engine Coolant Temperature Sensor (ECT) |
| 14 | Left Temperature Selector Wheel Setting (Degree C) |
| 16 | Right Temperature Selector Wheel Setting (Degree C) |
| 18 | Vehicle Speed Signal(km/h) |
| 20 | Soft Top OPEN : "U", Soft Top CLOSED : "O" |
| 22 | Power Supply Voltage |
| 83 | OFF/ON (Not Used) |
| 84 | Blower Motor Voltage "050" (0.5v) - "600" (6.0v) |

FAULT DIAGNOSIS

Turn temperature selector wheel into the white area.

Place the air speed selector at position 0 and the air direction to "DOWN"

IGNITION = ON : Position 1

Within the next 10 sec., press the "RECIRCULATE AIR" and "REST" button simultaneously for 3 sec.

Press the AUTO button until all error numbers are read and recorded.

| FAULT CODES - TAU 2.1 |
| --- |
| DTC Readout | Description | Cause |
| 1 | No DTC's Stored in System Memory. | No faults |
| 2 | In-Car Temperature Sensor (B10/4) | Short Circuit |
| 3 | In-Car Temperature Sensor (B10/4) | Open Circuit |
| 4 | Outside Temperature Sensor (B10/5) | Short Circuit |
| 5 | Outside Temperature Sensor (B10/5) | Open Circuit |
| 6 | Evaporator Temperature Sensor (B10/6) | Short Circuit |
| 7 | Evaporator Temperature Sensor (B10/6) | Open Circuit |
| 8 | Heater Core Temperature Sensor (B10/1)) | Short Circuit |
| 9 | Heater Core Temperature Sensor (B10/1) | Open Circuit |
| 10 | Heater Core Temperature Sensor (Right) | Short Circuit |
| 11 | Heater Core Temperature Sensor(Right) | Open Circuit |
| 12 | Engine Coolant Temperature Sensor (B10/8) | Short Circuit |
| 13 | Engine Coolant Temperature Sensor (B10/8) | Open Circuit |
| 16 | Center Air Vent Control Module (N18/2r2) | Short Circuit |
| 17 | Center Air Vent Control Module (N18/2r2) | Open Circuit |
| 18 | Center Air Vent Feedback Potentiometer (R23/3) | Short Circuit |
| 19 | Center Air Vent Feedback Potentiometer (R23/3) | Open Circuit |
| 20 | Left Air Vent Control Module (N18/2r1) | Short Circuit |
| 21 | Left Air Vent Control Module (N18/2r1) | Open Circuit |
| 22 | Left Air Vent Feedback Potentiometer (R23/1) | Short Circuit |
| 23 | Left Air Vent Feedback Potentiometer (R23/1) | Open Circuit |
| 24 | Right Air Vent Control Module (N18/2r3) | Short Circuit |
| 25 | Right Air Vent Control Module (N18/2r3) | Open Circuit |
| 26 | Right Air Vent Feedback Potentiometer (R23/2) | Short Circuit |
| 27 | Right Air Vent Feedback Potentiometer (R23/2) | Open Circuit |
| 30 | Auxiliary Coolant Pump | Short Circuit |
| 31 | Automatic A/C Monovalve (Left) | Short Circuit |
| 32 | Automatic A/C Monovalve (Right) | Short Circuit |
| 33 | A/C Compressor Signal | Short Circuit |

| FAULT CODES - TAU 2.1 |
| --- |
| DTC Readout | Description | Cause |
| 34 | Auxiliary Fan Signal 2 Stage | Short Circuit |
| 35 | Auxiliary Fan Signal 1 Stage | Short Circuit |
| 50 | Switchover Valve Block Signal | Short Circuit |
| 70 | Auxiliary Coolant Pump | Open Circuit |
| 71 | Automatic A/C Monovalve (Left) | Open Circuit |
| 72 | Automatic A/C Monovalve (Right) | Open Circuit |
| 73 | A/C Compressor Signal | Open Circuit |
| 74 | Auxiliary Fan Signal 2nd Stage | Open Circuit |
| 75 | Auxiliary Fan Signal 1st Stage | Open Circuit |

............SSSS8888

CCCC1J1J1J1Jss

222222

!!2222

JJJJoooo

8888\\\\88882222

READING ACTUAL VALUES

IGNITION ON : Position 1

Press the REST button and within 1 second press blower speed button 4.

The temperature window (upper left) will alternately display the test step number (ex. "02" In-car Temp) or "0P E" for Open Circuit or "Cl 0" for Closed Circuit.

Press "F" button to go to higher test.

Press "C" button to go to a lower test.

To end this test mode turn IGNITION OFF : Position 0 for longer then 5 seconds.

COMPONENT UNDER TEST

| Number | Component |
| --- | --- |
| 02 | In-Car Temperature Sensor |
| 04 | Outside Temperature Sensor |
| 06 | Evaporator Temperature Sensor |
| 08 | Heater Core Temperature Sensor |
| 12 | Engine Coolant Temperature (ETC) Sensor |
| 14 | Temperature Selector Wheel Setting |
| 18 | Vehicle Speed Signal(km/h) |
| 20 | Soft Top OPEN : "U" ; Soft Top CLOSED : "O" |
| 22 | Power Supply Voltage |
| 83 | OFF/ON (Not Used) |
| 84 | Blower motor voltage "050" (0,5V) - "600" (6,0V) |

FAULT DIAGNOSIS

Turn temperature selector wheel into the white area.

IGNITION ON : Position 1

Within the next 10 sec., press the "F", "RECIRCULATE AIR" and "REST" buttons simultaneously for 2 to 4 seconds.

The display will show the permanent DTC's stored. press the "RECIRCULATE AIR" button after each is displayed until the display reads "END"

Press "RECIRCULATE AIR" button again and the intermittent DTC's will be shown. A SQUARE is shown after each DTC to indicate that it is intermittent. Press the "RECIRCULATE AIR" button again to see the next DTC. Until "END" is shown.

To erase the DTC's : IGNITION ON : Position 1 Press the "RECIRCULATE AIR", "REST" and "UP" buttons simultaneously until --- is displayed in the window.

| FAULT CODES - 129 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause |
| 1 | No DTC's Stored in System Memory. | No Faults |

| FAULT CODES - 129 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause |
| 2 | In-Car Temperature Sensor (B10/4) | Short Circuit |
| 3 | In-Car Temperature Sensor (B10/4) | Open Circuit |
| 4 | Outside Temperature Sensor (B10/5) | Short Circuit |
| 5 | Outside Temperature Sensor (B10/5) | Open Circuit |
| 6 | Evaporator Temperature Sensor (B10/6) | Short Circuit |
| 7 | Evaporator Temperature Sensor (B10/6) | Open Circuit |
| 8 | Heater Core Temperature Sensor (B10/1)(Left) | Short Circuit |
| 9 | Heater Core Temperature Sensor (B10/1)(Left) | Open Circuit |
| 10 | Heater Core Temperature Sensor (Right) | Short Circuit |
| 11 | Heater Core Temperature Sensor(Right) | Open Circuit |
| 12 | Engine Coolant Temperature Sensor (B10/8) | Short Circuit |
| 13 | Engine Coolant Temperature Sensor (B10/8) | Open Circuit |
| 16 | Center Air Vent Control Module (N18/2r2) | Short Circuit |
| 17 | Center Air Vent Control Module (N18/2r2) | Open Circuit |
| 18 | Center Air Vent Feedback Potentiometer (R23/3) | Short Circuit |
| 19 | Center Air Vent Feedback Potentiometer (R23/3) | Open Circuit |
| 20 | Left Air Vent Control Module (N18/2r1) | Short Circuit |
| 21 | Left Air Vent Control Module (N18/2r1) | Open Circuit |
| 22 | Left Air Vent Feedback Potentiometer (R23/1) | Short Circuit |
| 23 | Left Air Vent Feedback Potentiometer (R23/1) | Open Circuit |
| 24 | Right Air Vent Control Module (N18/2r3) | Short Circuit |
| 25 | Right Air Vent Control Module (N18/2r3) | Open Circuit |
| 26 | Right Air Vent Feedback Potentiometer (R23/2) | Short Circuit |
| 27 | Right Air Vent Feedback Potentiometer (R23/2) | Open Circuit |
| 30 | Auxiliary Coolant Pump (M13) | Short Circuit |
| 31 | Automatic A/C Monovalve (Y19) | Short Circuit |
| 32 | Automatic A/C Monovalve (Right) | Short Circuit |
| 33 | A/C Compressor Signal | Short Circuit |
| 34 | Auxiliary Fan Signal, 2nd Stage | Short Circuit |
| 35 | Auxiliary Fan Signal, 1st Stage | Short Circuit |
| 50 | Switchover Valve Block Signal (Y11) | Short Circuit |
| 70 | Auxiliary Coolant Pump (M13) | Open Circuit |

| FAULT CODES - 129 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause |
| 71 | Automatic A/C Monovalve (Y19) | Open Circuit |
| 72 | Automatic A/C Monovalve (Right) | Open Circuit |
| 73 | A/C Compressor Signal | Open Circuit |
| 74 | Auxiliary Fan Signal, 2nd Stage | Open Circuit |
| 75 | Auxiliary Fan Signal, 1st Stage | Open Circuit |

-1-1-1-1ssssaaaa

CCCC1J1J1J1Jss

222222

!!2222

llllLLLLoooowwww

aaaa\\\\aaaa2222

READING ACTUAL VALUES

IGNITION : Position 1

Set temperature selector to 72 degrees F.

Press the REST button for more than 6 seconds.

The left display will alternately show the number "01" and the in-car temperature.

Press the FAN button and the next component number and its value will be displayed.

Press the REST button to end the test program.

COMPONENT UNDER TEST

| Number | Component |
| --- | --- |
| 01 | In-Car Temperature Sensor with Aspirator Blower (B10/4) |
| 02 | Outside Temperature Sensor (B14) |
| 03 | Left Heater Core Temperature Sensor (B10/2) |
| 05 | Evaporator Temperature Sensor (B10/6) |
| 06 | Engine Coolant Temperature Sensor (ECT) (B11/4) |
| 07 | Refrigerant Pressure in Bar |
| 08 | Refrigerant Temperature Sensor (B12/1) |
| 09 | Not Used |
| 10 | Blower Control Voltage |
| 20 | Control Current for Auxiliary Fan exp. : 7 = 7 mA |
| 21 | Engine RPM. example 00..99 (x100) = 9900 |
| 22 | Vehicle Speed |
| 23 | PIN 58D exp. 99.0 = 99% of Battery Voltage |
| 24 | Battery Voltage : 12.8 = 12,8 Volt |
| 40 | A/C Controller Software Version Coding |
| 41 | A/C Controller Hardware Version |
| 42 | Variant code 1 |
| 43 | Variant code 2 |
| 50 | Not Used |
| 51 | Not Used |
| 52 | Not Used |
| 54 | ON/OFF A/C Compressor emergency off signal from engine control module. |

| 60 | Roof "OPE" = OPEN, "CLO" = CLOSED |
| --- | --- |
| 61 | Left Air Outlet, Potentiometer Voltage |
| 62 | Vacuum Actuator 46, Feedback Potentiometer Voltage |
| 63 | Center Air Outlet, Potentiometer Voltage |
| 64 | Vacuum Actuator 47, Feedback Potentiometer Voltage |
| 65 | Right Air Outlet, Potentiometer Voltage |
| 66 | Vacuum Actuator 47, Feedback Potentiometer Voltage |

FAULT DIAGNOSIS

IGNITION : Position 1

Temperature selector wheel : "LO"

Within 20 seconds press the REST and DEFROST buttons simultaneously  for more than 5 seconds.

The LED in the RECIRCULATE button flashes and "dI A" appears on the display.

Press the AUTO button until all DTC's are displayed and recorded.

The current faults are displayed first, then the intermittent faults. "END'" is displayed when all codes have been displayed.

To erase codes press AUTO again, "dEL" will be displayed. Press v and ^ simultaneously for more than 5 seconds. The display will then show "---". Press AUTO to cancel the erase.

IGNITION : OFF to end the test program.

| FAULT CODES - 129 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 026 | CAN Bus Communication |
| 226 | In-Car Air Temperature Sensor (B10/4) |
| 227 | Outside Air Temperature Sensor (B14) |
| 228 | Heater Core Temperature Sensor (B10/2) |
| 230 | Evaporator Temperature Sensor (B10/6) |
| 231 | Engine Coolant Temperature Sensor (B11/4) |
| 232 | Refrigerant Pressure Sensor (B12) |
| 233 | Refrigerant Temperature Sensor (B12/1) |
| 241 | Refrigerant Level |
| 416 | Coolant Circulation Pump (A31m1) |
| 417 | Automatic A/C Monovalve (Y19) |
| 419 | A/C Compressor Electromagnetic Clutch (A9k1) |
| 420 | Closed (Idle) Throttle Speed Increase |

| FAULT CODES - 129 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 421 | Auxiliary Fan Control Module (N65/1) |
| 422 | Serial Interface Connection (K1) to Instrument Cluster (IC) |
| 423 | Switchover Valve Block (15 connection multiplex) (Y11) |
| 459 | Serial Interface Connection (K2) to Instrument Cluster (IC) |

READING ACTUAL VALUES

Turn temperature selector wheel into the white area.

IGNITION = ON : Position 1

Press the left and right "AUTO" buttons.

Within 20 seconds press the "REST" button for more than 5 sec.

LEFT DISPLAY = Component Number

RIGHT DISPLAY = Actual Component Value or "HI" for a short circuit or "LO" for an open circuit

Press the left "AUTO" button to monitor the next component.

Press the "REST" button to end the test mode.

COMPONENTS UNDER TEST

| Number | Component |
| --- | --- |
| 01 | In-Car Temperature Sensor with Aspirator Blower (B10/4) |
| 02 | Outside Temperature Sensor (B10/5) |
| 03 | Left Heater Core Temperature Sensor (B10/2) |
| 04 | Right Heater Core Temperature Sensor (B10/3) |
| 05 | Evaporator Temperature Sensor (B10/6) |
| 06 | Engine Coolant Temperature (ECT) Sensor (A/C) (B10/8) |
| 07 | Refrigerant Pressure in Bar : Ex. 06'4 = 6.4 Bar |
| 08 | Blower Control Voltage from 8(min) - 60(max) |
| 09 | Software Status, A/C Pushbutton Control Module(N22) Mfg. |
| 10 | Left rear heater core temperature sensor (B10/9) |
| 11 | Right rear heater core temperature sensor (B10/10) |
| 12 | Rear Evaporator Temperature Sensor (B10/11) |
| 13 | Software Status, Rear A/C Pushbutton Control Module(N22) Mfg. |
| 16 | Control Module Applicable for Charcoal Filter : "A"=YES "0 "=NO |

FAULT DIAGNOSIS

Turn the left selector wheel into the red area.

Turn the right selector wheel into the blue area.

IGNITION = ON : Position 1.

Press the "AUTO" button.

Within 20 seconds, press the "REST" and "O" button for more than 2 seconds.

The display will show the permanent DTC's stored. Left window "E0" or "E1", right window "01", "02"...etc. Record each DTC and press the right "AUTO" button to display the next code. Continue until "END" is displayed.

To erase the DTC's : Turn IGNITION OFF, Then turn IGNITION ON : Position 1. Press the left "AUTO" button. A "d" (delete) is displayed in the left window. By pressing the right "AUTO" button the DTC will be deleted. Alternate left and right "AUTO" buttons until all DTCs are erased and "E0 00" is displayed.

| FAULT CODES - 140 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 001 | No DTC's Stored in System Memory. |  |  |
| 002 | A/C Pushbutton Control Module (N22) |  |  |
| 003 | Rear A/C Pushbutton Control Module (N22/3) |  |  |
| 006 | Connection to the Switchover Valve Block (Y11) |  |  |
| 007 | Data Exchange (CAN B) | Short Circuit. |  |
| 008 | Data Exchange (CAN A) | Short Circuit. |  |
| 009 | Data Exchange (CAN A and CAN B) | Short Circuit. |  |
| 010 | Make the Diagnosis Again. |  |  |
| 011 | Data Exchange (CAN B) | Open Circuit. |  |
| 012 | Data Exchange (CAN A) | Open Circuit. |  |
| 013 | Connection with the Rear A/C Pushbutton Control Module |  |  |
| 014 | Data Exchange (CAN B) : Rear A/C Control Module | Open Circuit. |  |
| 015 | Data Exchange (CAN A) : Rear A/C Control Module | Open Circuit. |  |
| 016 | In-Car Air Temperature Sensor (B10/4) | Short Circuit | CONTINUOUS |
| 017 | In-Car Air Temperature Sensor (B10/4) | Short Circuit | INTERMITTENT |
| 018 | In-Car Air Temperature Sensor (B10/4) | Short or Open Circuit | CONTINUOUS |
| 019 | In-Car Air Temperature Sensor (B10/4) | Short or Open Circuit | INTERMITTENT |
| 024 | Left Heater Core Temperature Sensor (B10/2) | Short Circuit | CONTINUOUS |
| 025 | Left Heater Core Temperature Sensor (B10/2) | Short Circuit | INTERMITTENT |
| 026 | Left Heater Core Temperature Sensor (B10/2) | Short or Open Circuit | CONTINUOUS |
| 027 | Left Heater Core Temperature Sensor (B10/2) | Short or Open Circuit | INTERMITTENT |
| 028 | Right Heater Core Temperature Sensor (B10/3) | Short Circuit | CONTINUOUS |
| 029 | Right Heater Core Temperature Sensor (B10/3) | Short Circuit | INTERMITTENT |
| 030 | Right Heater Core Temperature Sensor (B10/3) | Short or Open Circuit | CONTINUOUS |
| 031 | Right Heater Core Temperature Sensor (B10/3) | Short or Open Circuit | INTERMITTENT |
| 032 | Outside Air Temperature Sensor (B10/5) | Short Circuit | CONTINUOUS |
| 033 | Outside Air Temperature Sensor (B10/5) | Short Circuit | INTERMITTENT |
| 034 | Outside Air Temperature Sensor (B10/5) | Short or Open Circuit | CONTINUOUS |
| 035 | Outside Air Temperature Sensor (B10/5) | Short or Open Circuit | INTERMITTENT |

| FAULT CODES - 140 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 036 | Evaporator Temperature Sensor (B10/6) | Short Circuit | CONTINUOUS |
| 037 | Evaporator Temperature Sensor (B10/6) | Short Circuit | INTERMITTENT |
| 038 | Evaporator Temperature Sensor (B10/6) | Short or Open Circuit | CONTINUOUS |
| 039 | Evaporator Temperature Sensor (B10/6) | Short or Open Circuit | INTERMITTENT |
| 040 | Engine Coolant Temperature Sensor (B10/8) | Short Circuit | CONTINUOUS |
| 041 | Engine Coolant Temperature Sensor (B10/8) | Short Circuit | INTERMITTENT |
| 042 | Engine Coolant Temperature Sensor (B10/8) | Short or Open Circuit | CONTINUOUS |
| 043 | Engine Coolant Temperature Sensor (B10/8) | Short or Open Circuit | INTERMITTENT |
| 044 | Refrigerant Pressure Sensor (B12) | Short Circuit | CONTINUOUS |
| 045 | Refrigerant Pressure Sensor (B12) | Short Circuit | INTERMITTENT |
| 046 | Refrigerant Pressure Sensor (B12) | Short or Open Circuit | CONTINUOUS |
| 047 | Refrigerant Pressure Sensor (B12) | Short or Open Circuit | INTERMITTENT |
| 048 | Left Temperature Wheel | Short Circuit | CONTINUOUS |
| 049 | Left Temperature Wheel | Short Circuit | INTERMITTENT |
| 050 | Left Temperature Wheel | Short or Open Circuit | CONTINUOUS |
| 051 | Left Temperature Wheel | Short or Open Circuit | INTERMITTENT |
| 052 | Right Temperature Wheel | Short Circuit | CONTINUOUS |
| 053 | Right Temperature Wheel | Short Circuit | INTERMITTENT |
| 054 | Right Temperature Wheel | Short or Open Circuit | CONTINUOUS |
| 055 | Right Temperature Wheel | Short or Open Circuit | INTERMITTENT |
| 072 | Heater Supply Unit Coolant Circulation Pump (A31m1) | Short Circuit | CONTINUOUS |
| 073 | Heater Supply Unit Coolant Circulation Pump (A31m1) | Short Circuit | INTERMITTENT |
| 074 | Coolant Circulation Pump (A31m1) | Short or Open Circuit | CONTINUOUS |
| 075 | Coolant Circulation Pump (A31m1) | Short or Open Circuit | INTERMITTENT |
| 076 | Coolant Circulation Pump (A31m1) | Overload | CONTINUOUS |
| 077 | Coolant Circulation Pump (A31m1) | Overload | INTERMITTENT |
| 080 | Left Duovalve (Water Valve) (A31y1) | Short Circuit | CONTINUOUS |
| 081 | Left Duovalve (Water Valve) (A31y1) | Short Circuit | INTERMITTENT |
| 082 | Left Duovalve (Water Valve) (A31y1) | Short or Open Circuit | CONTINUOUS |
| 083 | Left Duovalve (Water Valve) (A31y1) | Short or Open Circuit | INTERMITTENT |
| 084 | Right Duovalve (Water Valve) (A31y2) | Short Circuit | CONTINUOUS |

| FAULT CODES - 140 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 085 | Right Duovalve (Water Valve) (A31y2) | Short Circuit | INTERMITTENT |
| 086 | Right Duovalve (Water Valve) (A31y2) | Short or Open Circuit | CONTINUOUS |
| 087 | Right Duovalve (Water Valve) (A31y2) | Short or Open Circuit | INTERMITTENT |
| 088 | A/C Compressor Ground Activation |  | CONTINUOUS |
| 089 | A/C Compressor Ground Activation |  | INTERMITTENT |
| 090 | A/C Compressor Ground Activation | Short or Open Circuit | CONTINUOUS |
| 091 | A/C Compressor Ground Activation | Short or Open Circuit | INTERMITTENT |
| 096 | Auxiliary Fan, 1ST Stage Activation | Short Circuit | CONTINUOUS |
| 097 | Auxiliary Fan, 1ST Stage Activation | Short Circuit | INTERMITTENT |
| 098 | Auxiliary Fan, 1ST Stage Activation | Short or Open Circuit | CONTINUOUS |
| 099 | Auxiliary Fan, 1ST Stage Activation | Short or Open Circuit | INTERMITTENT |
| 100 | Auxiliary Fan, 2ND Stage Activation | Short Circuit | CONTINUOUS |
| 101 | Auxiliary Fan, 2ND Stage Activation | Short Circuit | INTERMITTENT |
| 102 | Auxiliary Fan, 2ND Stage Activation | Short or Open Circuit | CONTINUOUS |
| 103 | Auxiliary Fan, 2ND Stage Activation | Short or Open Circuit | INTERMITTENT |
| 104 | Auxiliary Fan, 3RD Stage Activation | Short Circuit | CONTINUOUS |
| 105 | Auxiliary Fan, 3RD Stage Activation | Short Circuit | INTERMITTENT |
| 106 | Auxiliary Fan, 3RD Stage Activation | Short or Open Circuit | CONTINUOUS |
| 107 | Auxiliary Fan, 3RD Stage Activation | Short or Open Circuit | INTERMITTENT |
| 108 | Auxiliary Coolant Pump Control Relay Module (K30), Power Supply | Short Circuit | CONTINUOUS |
| 109 | Auxiliary Coolant Pump Control Relay Module (K30), Power Supply | Short Circuit | INTERMITTENT |
| 110 | Auxiliary Coolant Pump Control Relay Module (K30), Power Supply | Short or Open Circuit | CONTINUOUS |
| 111 | Auxiliary Coolant Pump Control Relay Module (K30), Power Supply | Short or Open Circuit | INTERMITTENT |
| 112 | Engine RPM Increase Diode Matrix (V2) | Short Circuit | CONTINUOUS |
| 113 | Engine RPM Increase Diode Matrix (V2) | Short Circuit | INTERMITTENT |
| 114 | Engine RPM Increase Diode Matrix (V2) | Short or Open Circuit | CONTINUOUS |
| 115 | Engine RPM Increase Diode Matrix (V2) | Short or Open Circuit | INTERMITTENT |
| 116 | Activated Charcoal Filter Actuator (A32m2) : (OPEN) | Short Circuit | CONTINUOUS |
| 117 | Activated Charcoal Filter Actuator (A32m2) : (OPEN) | Short Circuit | INTERMITTENT |

| FAULT CODES - 140 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 118 | Activated Charcoal Filter Actuator (A32m2) : (OPEN) | Short or Open Circuit | CONTINUOUS |
| 119 | Activated Charcoal Filter Actuator (A32m2) : (OPEN) | Short or Open Circuit | INTERMITTENT |
| 120 | Activated Charcoal Filter Actuator (A32m2) : (CLOSED) | Short Circuit | CONTINUOUS |
| 121 | Activated Charcoal Filter Actuator (A32m2) : (CLOSED) | Short Circuit | INTERMITTENT |
| 122 | Activated Charcoal Filter Actuator (A32m2) : (CLOSED) | Short or Open Circuit | CONTINUOUS |
| 123 | Activated Charcoal Filter Actuator (A32m2) : (CLOSED) | Short or Open Circuit | INTERMITTENT |
| 128 | Left Rear Heater Core Temperature Sensor (B10/9) | Short Circuit | CONTINUOUS |
| 129 | Left Rear Heater Core Temperature Sensor (B10/9) | Short Circuit | INTERMITTENT |
| 130 | Left Rear Heater Core Temperature Sensor (B10/9) | Short or Open Circuit | CONTINUOUS |
| 131 | Left Rear Heater Core Temperature Sensor (B10/9) | Short or Open Circuit | INTERMITTENT |
| 132 | Right Rear Heater Core Temperature Sensor (B10/10) | Short Circuit | CONTINUOUS |
| 133 | Right Rear Heater Core Temperature Sensor (B10/10) | Short Circuit | INTERMITTENT |
| 134 | Right Rear Heater Core Temperature Sensor (B10/10) | Short or Open Circuit | CONTINUOUS |
| 135 | Right Rear Heater Core Temperature Sensor (B10/10) | Short or Open Circuit | INTERMITTENT |
| 136 | Left Temperature Selector wheel | Short Circuit | CONTINUOUS |
| 137 | Left Temperature Selector wheel | Short Circuit | INTERMITTENT |
| 138 | Left Temperature Selector wheel | Short or Open Circuit | CONTINUOUS |
| 139 | Left Temperature Selector wheel | Short or Open Circuit | INTERMITTENT |
| 140 | Right Temperature Selector wheel | Short Circuit | CONTINUOUS |
| 141 | Right Temperature Selector wheel | Short Circuit | INTERMITTENT |
| 142 | Right Temperature Selector wheel | Short or Open Circuit | CONTINUOUS |
| 143 | Right Temperature Selector wheel | Short or Open Circuit | INTERMITTENT |
| 144 | Rear Evaporator Temperature Sensor (B10/11) | Short Circuit | CONTINUOUS |

| FAULT CODES - 140 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 145 | Rear Evaporator Temperature Sensor (B10/11) | Short Circuit | INTERMITTENT |
| 146 | Rear Evaporator Temperature Sensor (B10/11) | Short or Open Circuit | CONTINUOUS |
| 147 | Rear Evaporator Temperature Sensor (B10/11) | Short or Open Circuit | INTERMITTENT |
| 148 | Coolant Circulation Pump (A31/1m1) | Short Circuit | CONTINUOUS |
| 149 | Coolant Circulation Pump (A31/1m1) | Short Circuit | INTERMITTENT |
| 150 | Coolant Circulation Pump (A31/1m1) | Short or Open Circuit | CONTINUOUS |
| 151 | Coolant Circulation Pump (A31/1m1) | Short or Open Circuit | INTERMITTENT |
| 152 | Coolant Circulation Pump (A31/1m1) | Overload | CONTINUOUS |
| 153 | Coolant Circulation Pump (A31/1m1) | Overload | INTERMITTENT |
| 156 | Left Duovalve (Water Valve) (A31/1y1) | Short Circuit | CONTINUOUS |
| 157 | Left Duovalve (Water Valve) (A31/1y1) | Short Circuit | INTERMITTENT |
| 158 | Left Duovalve (Water Valve) (A31/1y1) | Short or Open Circuit | CONTINUOUS |
| 159 | Left Duovalve (Water Valve) (A31/1y1) | Short or Open Circuit | INTERMITTENT |
| 160 | Right Duovalve (Water Valve) (A31/1y2) | Short Circuit | CONTINUOUS |
| 161 | Right Duovalve (Water Valve) (A31/1y2) | Short Circuit | INTERMITTENT |
| 162 | Right Duovalve (Water Valve) (A31/1y2) | Short or Open Circuit | CONTINUOUS |
| 163 | Right Duovalve (Water Valve) (A31/1y2) | Short or Open Circuit | INTERMITTENT |
| 164 | Rear Refrigerant Shut-Off Valve (Y67) | Short Circuit | CONTINUOUS |
| 165 | Rear Refrigerant Shut-Off Valve (Y67) | Short Circuit | INTERMITTENT |
| 166 | Rear Refrigerant Shut-Off Valve (Y67) | Short or Open Circuit | CONTINUOUS |
| 167 | Rear Refrigerant Shut-Off Valve (Y67) | Short or Open Circuit | INTERMITTENT |
| 168 | Rear Tunnel Flap Vacuum Valve (Y67/1) | Short Circuit | CONTINUOUS |
| 169 | Rear Tunnel Flap Vacuum Valve (Y67/1) | Short Circuit | INTERMITTENT |
| 170 | Rear Tunnel Flap Vacuum Valve (Y67/1) | Short or Open Circuit | CONTINUOUS |
| 171 | Rear Tunnel Flap Vacuum Valve (Y67/1) | Short or Open Circuit | INTERMITTENT |

READING ACTUAL VALUES

IGNITION : Position 1

Press the AUTO button

Set both temperature selectors to 72 degrees F.

Press the REST button for more than 5 seconds.

The left display will alternately show the number "1" and the in-car temperature.

Press the AUTO button and the next component number and its value will be displayed.

Press the REST button to end the test program.

COMPONENT UNDER TEST

| Number | Component |
| --- | --- |
| 01 | In-Car Temperature Sensor with Aspirator Blower (B10/4) |
| 02 | Outside Temperature Sensor (B10/5) 1996, (B14) as of 1997 |
| 03 | Left Heater Core Temperature Sensor (B10/2) |
| 04 | Right Heater Core Temperature Sensor (B10/3) |
| 05 | Evaporator Temperature Sensor (B10/6) |
| 06 | Engine Coolant Temperature (ECT) Sensor (A/C) (B11/4) |
| 07 | Refrigerant Pressure in Bar |
| 08 | Refrigerant Temperature Sensor (B12/1) |
| 10 | Blower Control Voltage |
| 11 | Emissions (Refrigerant Leak) Sensor (B31) |
| 12 | Sun (Excessive Heat) Sensor (B32) |
| 20 | Control Current for Auxiliary Fan example : 7 = 7 mA |
| 21 | Engine RPM. example 00..99 (x100) = 9900 |
| 22 | Vehicle Speed |
| 23 | PIN 58D example. 99.0 = 99% of Battery Voltage |
| 24 | Battery Voltage : 12.8 = 12,8 Volt |
| 30 | Left Rear Heater Core Temperature Sensor (B10/9) |
| 31 | Right Rear Heater Core Temperature sensor (B10/10) |
| 32 | Rear Evaporator Temperature Sensor (B10/11) |
| 33 | Rear Blower Control Voltage |
| 34 | Left Rear Temperature Sensor version |
| 35 | Right Rear Temperature Sensor |
| 38 | Rear A/C Controller Software Version Coding |
| 39 | Rear A/C Controller Hardware Version |
| 40 | Front A/C Controller Software Version Coding |
| 41 | Front A/C Controller Hardware Version |
| 42 | Variant code 1 |
| 43 | Variant code 2 |

FAULT DIAGNOSIS

IGNITION : Position 1

Left Temperature selector wheel : HI Right Temperature selector wheel : LO

Within 20 seconds press the REST and EC buttons simultaneously  for more than 5 seconds.

The LED in the RECIRCULATE button flashes and "OFF" appears on the display.

Press the right AUTO button until all DTC's are displayed and recorded.

To erase all codes must be read out. Press both AUTO buttons simultaneously for more than 2 seconds. "d" will be displayed on the left and "FF" is displayed on the right. The erase can be canceled by pressing the AUTO button.

Reset temperature selector to normal setting.

IGNITION : OFF to end the test program.

| FAULT CODES - 140 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 026 | CAN Bus Communication |
| 226 | In-Car Air Temperature Sensor (B10/4) |
| 227 | Outside Air Temperature Sensor (B10/5) to 1996, (B14) as of 1997 |
| 228 | Left Heater Core Temperature Sensor (B10/2) |
| 229 | Right Heater Core Temperature Sensor (B10/3) |
| 230 | Evaporator Temperature Sensor (B10/6) |
| 231 | Engine Coolant Temperature Sensor (B11/4) DFI or IFI models Right Engine Coolant Temperature Sensor (B11/10) to 1996 |
| 232 | Refrigerant Pressure Sensor (B12) |
| 233 | Refrigerant Temperature Sensor (B12/1) |
| 234 | Sun Sensor (B32) |
| 235 | Emissions (Refrigerant Leak) Sensor (B31) |
| 241 | Refrigerant Level |
| 416 | Coolant Circulation Pump (A31m1) |
| 417 | Left Duovalve (Water Valve) (Y21y1) |
| 418 | Right Duovalve (Water Valve) (Y21y2) |
| 419 | A/C Compressor Electromagnetic Clutch (A9k1) |
| 420 | Closed (Idle) Throttle Speed Increase |
| 421 | Pulse Module (N65) |
| 422 | Serial Interface Connection (K1) to Instrument Cluster (IC) |
| 423 | Switchover Valve Block (Y11) |
| 424 | Activated Charcoal Filter Actuator (A32m2) : OPEN |
| 425 | Activated Charcoal Filter Actuator (A32m2) : CLOSE |
| 432 | Maximum Heat |

| FAULT CODES - 140 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 459 | Serial Interface Connection (K2) to Instrument Cluster (IC) |
| 460 | LED - Center Air Outlet "Warm" |
| 461 | LED - Center Air Outlet "Cold" |
| 462 | Wide Open Throttle (WOT) Position Signal - Diesel Engine Only |

ssssoooossss

CCCC1J1J1J1Jss

222222

!!2222

JJJJoooo

BBBB\\\\aaaa2222

READING ACTUAL VALUES

IGNITION : Position 1

Set temperature selection to 72 degrees F (Press v and ^ simultaneously).

Press the AUTO button.

Press the REST button for more than 5 seconds.

The display will alternately show the number "01" and the in-car temperature or "LO" if there is an open circuit or "HI" if there is a short circuit.

Press the "Top Air Outlet" button to increase the component tested and the "Bottom Air Outlet" button to decrease the component number tested.

Press the REST button to end the test program.

COMPONENT UNDER TEST

| Number | Component |
| --- | --- |
| 01 | In-Car Temperature Sensor with Aspirator Blower (B10/4) |
| 02 | Outside Temperature Sensor (B10/5) |
| 03 | Heater Core Temperature Sensor (B10/1) |
| 05 | Evaporator Temperature Sensor (B10/6) |
| 06 | Engine Coolant Temperature (ECT) Sensor (A/C) (B10/8) |
| 07 | Refrigerant Pressure in Bar |
| 08 | Blower Control Voltage |
| 09 | Software Status of A/C Pushbutton Control Module |
| 15 | Selected In-Car Temperature |
| 20 | Version Code |
| 21 | Engine Speed in RPM |
| 22 | A/C Compressor Speed in RPM |
| 23 | Vehicle Speed in km/h |
| 50 | Not Used |
| 51 | Number of Current Poly-V Belt Slip Recognitions |
| 52 | Number of Stored Poly-V Belt Slip Recognitions |

FAULT DIAGNOSIS

IGNITION : Position 1

Press the V button until "LO" appears on the display.

Within 20 seconds press the REST and BLOWER buttons simultaneously for more then 2 seconds.

The LED in the RECIRCULATE button flashes and "dI R" appears on the display

Press the AUTO button until all DTC's are displayed and recorded. Continuous faults are displayed first. if no faults are stored, "En d" is displayed. Press AUTO again to retrieve intermittent faults. If no intermittent faults are stored, "En d" is displayed.

Press the AUTO button until "dE L" is displayed. To erase codes press both V and ^ simultaneously for at least 5 seconds. The display will show "---"

IGNITION : OFF to end the test program.

| FAULT CODES - 202 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 01 | No ERROR Stored | No Faults |  |
| 02 | A/C Pushbutton Control Module (N22). | Power failure or damaged computer |  |
| 03 | In-Car Temperature Sensor with Aspirator Blower (B10/4) | Short circuit | CONTINUOUS |
| 04 | In Car Temperature Sensor with Aspirator Blower (B10/4) | Short circuit | INTERMITTENT |
| 05 | In-Car Temperature Sensor with Aspirator Blower (B10/4) | Short or Open circuit | CONTINUOUS |
| 06 | In-Car Temperature Sensor with Aspirator Blower (B10/4) | Short or Open circuit | INTERMITTENT |
| 07 | Outside Air Temperature Sensor (B10/5) | Short circuit | CONTINUOUS |
| 08 | Outside Air Temperature Sensor (B10/5) | Short circuit | INTERMITTENT |
| 09 | Outside air Temperature Sensor (B10/5) | Short or Open circuit | CONTINUOUS |
| 10 | Outside air Temperature Sensor (B10/5) | Short or Open circuit | INTERMITTENT |
| 11 | Heater Core Temperature Sensor (B10/1) | Short circuit | CONTINUOUS |
| 12 | Heater Core Temperature Sensor (B10/1) | Short circuit | INTERMITTENT |
| 13 | Heater Core Temperature Sensor (B10/1) | Short or Open circuit | CONTINUOUS |
| 14 | Heater Core Temperature Sensor (B10/1) | Short or Open circuit | INTERMITTENT |
| 19 | Evaporator Temperature Sensor (B10/6) | Short circuit | CONTINUOUS |
| 20 | Evaporator Temperature Sensor (B10/6) | Short circuit | INTERMITTENT |
| 21 | Evaporator Temperature Sensor (B10/6) | Short or Open circuit | CONTINUOUS |
| 22 | Evaporator Temperature Sensor (B10/6) | Short or Open circuit | INTERMITTENT |
| 23 | Engine Coolant Temperature Sensor (ETC) (B10/8) | Short circuit | CONTINUOUS |
| 24 | Engine Coolant Temperature Sensor (ETC) (B10/8) | Short circuit | INTERMITTENT |
| 25 | Engine Coolant Temperature Sensor (ETC) (B10/8) | Short or Open circuit | CONTINUOUS |
| 26 | Engine Coolant Temperature Sensor (ETC) (B10/8) | Short or Open circuit | INTERMITTENT |
| 27 | Refrigerant Pressure Sensor (B12) | Short circuit | CONTINUOUS |
| 28 | Refrigerant Pressure Sensor (B12) | Short circuit | INTERMITTENT |

| FAULT CODES - 202 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 29 | Refrigerant Pressure Sensor (B12) | Short or Open circuit | CONTINUOUS |
| 30 | Refrigerant Pressure Sensor (B12) | Short or Open circuit | INTERMITTENT |
| 31 | A/C Compressor RPM Sensor (A9l1) | Bad Sensor |  |
| 32 | Poly-V Belt Slip Recognition | Slipping Belt |  |
| 47 | Auxiliary Coolant Pump (M13) | Unknown |  |
| 48 | Auxiliary Coolant Pump (M13) | Short circuit | INTERMITTENT |
| 49 | Auxiliary Coolant Pump (M13) | Short or Open circuit | CONTINUOUS |
| 50 | Auxiliary Coolant Pump (M13) | Short or Open circuit | INTERMITTENT |
| 51 | Duovalve (Water Valve) (Y21) | Short circuit | CONTINUOUS |
| 52 | Duovalve (Water Valve) (Y21) | Short circuit | INTERMITTENT |
| 53 | Duovalve (Water Valve) (Y21) | Short or Open circuit | CONTINUOUS |
| 54 | Duovalve (Water Valve) (Y21) | Short or Open circuit | INTERMITTENT |
| 59 | A/C Compressor Electromagnetic Clutch (A9k1) | Short circuit | CONTINUOUS |
| 60 | A/C Compressor Electromagnetic Clutch (A9k1) | Short circuit | INTERMITTENT |
| 61 | A/C Compressor Electromagnetic Clutch (A9k1) | Short or Open circuit | CONTINUOUS |
| 62 | A/C Compressor Electromagnetic Clutch (A9k1) | Short or Open circuit | INTERMITTENT |
| 63 | Activation of Auxiliary Fan Stage 1 | Short circuit | CONTINUOUS |
| 64 | Activation of Auxiliary Fan Stage 1 | Short circuit | INTERMITTENT |
| 65 | Activation of Auxiliary Fan Stage 1 | Short or Open circuit | CONTINUOUS |
| 66 | Activation of Auxiliary Fan Stage 1 | Short or Open circuit | INTERMITTENT |
| 67 | Activation of Auxiliary Fan Stage 2 | Short circuit | CONTINUOUS |
| 68 | Activation of Auxiliary Fan Stage 2 | Short circuit | INTERMITTENT |
| 69 | Activation of Auxiliary Fan Stage 2 | Short or Open circuit | CONTINUOUS |
| 70 | Activation of Auxiliary Fan Stage 2 | Short or Open circuit | INTERMITTENT |
| 71 | Closed (Idle) Throttle Speed Increase | Short or Open circuit | CONTINUOUS |
| 72 | Closed (Idle) Throttle Speed Increase | Short or Open circuit | INTERMITTENT |
| 73 | Closed (Idle) Throttle Speed Increase | Short circuit | CONTINUOUS |
| 74 | Closed (Idle) Throttle Speed Increase | Short circuit | INTERMITTENT |
| 75 | Switchover Valve Block (Y11/3), Diverter Flap |  | CONTINUOUS |

| FAULT CODES - 202 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 76 | Switchover Valve Block (Y11/3), Diverter Flap |  | INTERMITTENT |
| 77 | Switchover Valve Block (Y11/3), Diverter Flap | Short or Open circuit | CONTINUOUS |
| 78 | Switchover Valve Block (Y11/3), Diverter Flap | Short or Open circuit | INTERMITTENT |
| 79 | Switchover Valve Block (Y11/3), Tempering Flap |  | CONTINUOUS |
| 80 | Switchover Valve Block (Y11/3), Tempering Flap |  | INTERMITTENT |
| 81 | Switchover Valve Block (Y11/3), Tempering Flap | Short or Open circuit | CONTINUOUS |
| 82 | Switchover Valve Block (Y11/3), Tempering Flap | Short or Open circuit | INTERMITTENT |
| 83 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap Long Stroke (80%) |  | CONTINUOUS |
| 84 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap Long Stroke (80%) |  | INTERMITTENT |
| 85 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap Long Stroke (80%) | Short or Open circuit | CONTINUOUS |
| 86 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap | Short or Open circuit | INTERMITTENT |
| 87 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap Short Stroke (20%) |  | CONTINUOUS |
| 88 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap Short Stroke (20%) |  | INTERMITTENT |
| 89 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap Short Stroke (20%) | Short or Open circuit | CONTINUOUS |
| 90 | Switchover Valve Block (Y11/3), Fresh/Recirculating Air Flap Short Stroke (20%) | Short or Open circuit | INTERMITTENT |
| 91 | Switchover Valve Block (Y11/3), Defroster Flap Long Stroke (80%) |  | CONTINUOUS |
| 92 | Switchover Valve Block (Y11/3), Defroster Flap Long Stroke (80%) |  | INTERMITTENT |

| FAULT CODES - 202 Chassis to 8/95 |
| --- |
| DTC Readout | Description | Cause | Fault Type |
| 93 | Switchover Valve Block (Y11/3), Defroster Flap Long Stroke (80%) | Short or Open circuit | CONTINUOUS |
| 94 | Switchover Valve Block (Y11/3), Defroster Flap Long Stroke (80%) | Short or Open circuit | INTERMITTENT |
| 95 | Switchover Valve Block (Y11/3), Defroster Flap Short Stroke (20%) |  | CONTINUOUS |
| 96 | Switchover Valve Block (Y11/3), Defroster Flap Short Stroke (20%) |  | INTERMITTENT |
| 97 | Switchover Valve Block (Y11/3), Defroster Flap Short Stroke (20%) | Short or Open circuit | CONTINUOUS |
| 98 | Switchover Valve Block (Y11/3), Defroster Flap Short Stroke (20%) | Short or Open circuit | INTERMITTENT |
| 99 | Switchover Valve Block (Y11/3), Footwell Flap Long Stroke (80%) |  | CONTINUOUS |
| 100 | Switchover Valve Block (Y11/3), Footwell Flap Long Stroke (80%) |  | INTERMITTENT |
| 101 | Switchover Valve Block (Y11/3), Footwell Flap Long Stroke (80%) | Short or Open circuit | CONTINUOUS |
| 102 | Switchover Valve Block (Y11/3), Footwell Flap Long Stroke (80%) | Short or Open circuit | INTERMITTENT |
| 103 | Switchover Valve Block (Y11/3), Footwell Flap Short Stroke (20%) |  | CONTINUOUS |
| 104 | Switchover Valve Block (Y11/3), Footwell Flap Short Stroke (20%) |  | INTERMITTENT |
| 105 | Switchover Valve Block (Y11/3), Footwell Flap Short Stroke (20%) | Short or Open circuit | CONTINUOUS |
| 106 | Switchover Valve Block (Y11/3), Footwell Flap Short Stroke (20%) | Short or Open circuit | INTERMITTENT |

ssssoooossss

CCCC1J1J1J1Jss

222222

!!2222

llllLLLLoooowwww

aaaa\\\\aaaa2222

READING ACTUAL VALUES

IGNITION : Position 1

Set temperature selector to 72 degrees F.

Press the REST button for more than 6 seconds.

The left display will alternately show the number "01" and the in-car temperature.

Press the FAN button and the next component number and its value will be displayed.

Press the REST button to end the test program.

COMPONENT UNDER TEST

| Number | Component |
| --- | --- |
| 01 | In-Car Temperature Sensor with Aspirator Blower (B10/4) |
| 02 | Outside Temperature Sensor (B14) |
| 03 | Heater Core Temperature Sensor (B10/1) |
| 05 | Evaporator Temperature Sensor (B10/6) |
| 06 | Engine Coolant Temperature Sensor (ECT) (B11/4) |
| 07 | Refrigerant Pressure in Bar |
| 08 | Refrigerant Temperature Sensor (B12/1) |
| 09 | Not Used |
| 10 | Blower Control Voltage |
| 20 | Control Current for Auxiliary Fan exp. : 7 = 7 mA |
| 21 | Engine RPM. example 00..99 (x100) = 9900 |
| 22 | Vehicle Speed |
| 23 | PIN 58D exp. 99.0 = 99% of Battery Voltage |
| 24 | Battery Voltage : 12.8 = 12,8 Volt |
| 40 | A/C Controller Software Version Coding |
| 41 | A/C Controller Hardware Version |
| 42 | Variant code 1 |
| 43 | Variant code 2 |
| 50 | Not Used |
| 51 | Not Used |
| 52 | Not Used |
| 54 | ON/OFF A/C Compressor emergency off signal from engine control module. |

FAULT DIAGNOSIS

IGNITION : Position 1

Temperature selector wheel : "LO"

Within 20 seconds press the REST and DEFROST buttons simultaneously  for more than 5 seconds.

The LED in the RECIRCULATE button flashes and "dI A" appears on the display.

Press the AUTO button until all DTC's are displayed and recorded.

The current faults are displayed first, then the intermittent faults. "END'" is displayed when all codes have been displayed.

To erase codes press v and ^ simultaneously for more than 5 seconds. The display will then show "---". Press AUTO to cancel the erase.

IGNITION : OFF to end the test program.

| FAULT CODES - 202 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 026 | CAN Bus Communication |
| 226 | In-Car Air Temperature Sensor (B10/4) |
| 227 | Outside Air Temperature Sensor (B14) |
| 228 | Heater Core Temperature Sensor (B10/1) |
| 230 | Evaporator Temperature Sensor (B10/6) |
| 231 | Engine Coolant Temperature Sensor (B11/4) |
| 232 | Refrigerant Pressure Sensor (B12) |
| 233 | Refrigerant Temperature Sensor (B12/1) |
| 241 | Refrigerant Level |
| 416 | Coolant Circulation Pump (A31m1) |
| 417 | Left Duovalve (Water Valve) (Y21y1) |
| 418 | Right Duovalve (Water Valve) (Y21y2) |
| 419 | A/C Compressor Electromagnetic Clutch (A9k1) |
| 420 | Closed (Idle) Throttle Speed Increase |
| 421 | Pulse Module (N65) |
| 422 | Serial Interface Connection (K1) to Instrument Cluster (IC) |
| 451 | Diverter Flap (Y11/3) |
| 452 | Blend Air Flap (Y11/3) |
| 453 | Fresh/Recirculated Air Flap (Y11/3) Long Stroke |
| 454 | Fresh/Recirculated Air Flap (Y11/3) Short Stroke |
| 455 | Defroster Outlet Flap (Y11/3) Long Stroke |
| 456 | Defroster Outlet Flap (Y11/3) Short Stroke |
| 457 | Footwell Flap (Y11/3) Long Stroke |
| 458 | Footwell Flap (Y11/3) Short Stroke |
| 459 | Serial Interface Connection (K2) to Instrument Cluster (IC) |

| FAULT CODES - 202 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 462 | Wide Open Throttle (WOT) Position Signal - Diesel Engine Only |

READING ACTUAL VALUES

IGNITION : Position 1

Press the AUTO button

Set both temperature selectors to 72 degrees F.

Press the REST button for more than 5 seconds.

The left display will alternately show the number "1" and the in-car temperature.

Press the AUTO button and the next component number and its value will be displayed.

Press the REST button to end the test program.

COMPONENT UNDER TEST

| Number | Component |
| --- | --- |
| 01 | In-Car Temperature Sensor with Aspirator Blower (B10/4) |
| 02 | Outside Temperature Sensor (B14) |
| 03 | Left Heater Core Temperature Sensor (B10/1) |
| 04 | Right Heater Core Temperature Sensor (B10/1) |
| 05 | Evaporator Temperature Sensor (B10/6) |
| 06 | Engine Coolant Temperature (ECT) Sensor (A/C) (B1/4) |
| 07 | Refrigerant Pressure in Bar |
| 08 | Refrigerant Temperature Sensor (B12/1) |
| 10 | Blower Control Voltage |
| 11 | Emissions (Refrigerant Leak) Sensor (B31) |
| 12 | Sun (Excessive Heat) Sensor (B32) |
| 20 | Control Current for Auxiliary Fan exp. : 7 = 7 mA |
| 21 | Engine RPM. example 00..99 (x100) = 9900 |
| 22 | Vehicle Speed |
| 23 | PIN 58D exp. 99.0 = 99% of Battery Voltage |
| 24 | Battery Voltage : 12.8 = 12,8 Volt |
| 40 | Software Version Encoded |
| 41 | Hardware Version |

FAULT DIAGNOSIS

IGNITION : Position 1

Left Temperature selector wheel : HI Right Temperature selector wheel : LO

Within 20 seconds press the REST and EC buttons simultaneously  for more than 5 seconds.

The LED in the RECIRCULATE button flashes and "dI R" appears on the display

Press the right AUTO button until all DTC's are displayed and recorded.

To erase all codes must be read out. Press both AUTO buttons simultaneously for more than 2 seconds. "d" will be displayed on the left and "FF" is displayed on the right. The erase can be canceled by pressing the AUTO.

Reset temperature selector to normal setting.

IGNITION : OFF to end the test program.

| FAULT CODES - 210 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 026 | CAN - Communication |
| 226 | In-Car Air Temperature Sensor (B10/4) |
| 227 | Outside Air Temperature Sensor (B14) |
| 228 | Left Heater Core Temperature Sensor (B10/1) |
| 229 | Right Heater Core Temperature Sensor (B10/1) |
| 230 | Evaporator Temperature Sensor (B10/6) |
| 231 | Engine Coolant Temperature Sensor (B10/8) |
| 232 | Refrigerant Pressure Sensor (B12) |
| 233 | Refrigerant Temperature Sensor (B12/1) |
| 234 | Sun Sensor (B32) |
| 235 | Emissions (Refrigerant Leak) Sensor (B31) |
| 241 | Refrigerant Level |
| 416 | Coolant Circulation Pump (M13) |
| 417 | Left Duovalve (Water Valve) (Y21y1) |
| 418 | Right Duovalve (Water Valve) (Y21y2) |
| 419 | A/C Compressor Electromagnetic Clutch (A9k1) |
| 420 | Closed (Idle) Throttle Speed Increase |
| 421 | Pulse Module |
| 422 | Serial Interface Connection (K1) to Instrument Cluster (IC) |
| 423 | Switchover Valve Block (Y11) |
| 424 | Activated Charcoal Filter Actuator (A32m2) : OPEN |
| 425 | Activated Charcoal Filter Actuator (A32m2) : CLOSE |
| 432 | Maximum Heat |
| 459 | Serial Interface Connection (K2) to Instrument Cluster (IC) |

| FAULT CODES - 210 Chassis from 9/95 |
| --- |
| DTC Readout | Description |
| 462 | Wide Open Throttle (WOT) Position Signal - Diesel Engine Only |

| Models | Model Years |
| --- | --- |
| 107 126 201 140 | 1988-1993 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 6 |
| Black | Socket 1 |
| Red | Battery (+) |

| Scanner | Data link connector 38-pin |
| --- | --- |
| Yellow | Socket 30 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | SRS Control unit |
| 3 | SRS - Driver air bag |
| 4 | Front passenger Airbag |
| 5 | Driver seat beat buckle |
| 6 | Front passenger seat belt buckle |
| 7 | Airbag resistor, Front passenger |
| 8 | Circuit 15R, Voltage supply |
| 9 | Waning lamp faulty |
| 10 | Control unit was activated |

| Models | Model Years |
| --- | --- |
| 124 129 | 1990-93 |

Connect wires of Scanner as follows (124, 129.061/066)

| Scanner | Data Link Connector 8 or 16-pin |
| --- | --- |
| Yellow | Socket 6 |
| Black | Socket 1 |
| Red | Battery (+) |

Connect wires of Scanner as follows (129.067/076)

| Scanner | Data link connector 38-pin |
| --- | --- |
| Yellow | Socket 30 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | SRS Control unit self test failure |
| 3 | Driver Airbag squib |
| 4 | Front passenger Airbag squib |
| 5 | Airbag/ETR, Driver seat beat buckle switch |
| 6 | Front passenger seat belt buckle switch (ETR) |
| 7 | Front passenger Airbag resistor |
| 8 | Voltage supply interrupted |
| 9 | SRS Warning Lamp (with flashing SRS warning lamp Impulse counter scan tool button held too little time to read out the DTC memory or too long to erase DTC codes. Reread codes.) |
| 10 | SRS Control unit activated. |

| F 2 | SRS - Chassis 124 129 140 202 210 (1-2 Airbags) 1994-95) |
| --- | --- |
| F 3 | SRS - Chassis 129 140 202 210 (4 Airbags) 1996-98 |
| F 4 | LH-SFI Current Faults Engines 104 (1992-93) 119 (1992-95) 120 (1990-95) |
| F 5 | LH-SFI Stored or Permanent Faults Engines 104 (1992-93) 119 (1992-95) 120 (1990-95) |
| F 6 | HFM-SFI / PMS Current Faults Engines 104 (1993-96) 111 (1994-96) |
| F 7 | HFM-SFI / PMS Stored or Permanent Faults Engines 104 (1993-96) 111 (1994-96) |
| F 8 | DM Current Faults Engines 104, 119 120 |
| F 9 | DM Stored or Permanent Faults Engines 104 119 120 |
| F10 | DM Registered Faults Engines 104 119 120 |
| F11 | ME1 Current Faults - Engines 119 (1996-98) 120 (1996-98) |
| F12 | ME1 Stored or Permanent Faults Engines 119 (1996-98) 120 (1996-98) |

F2 SRS	CS1000 Code Scanner OB15-11

| Models | Model Years |
| --- | --- |
| 129 | 140 | 124 | 1994-95 |
| 202 | 210 | From beginning of manufacture -1995 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 30 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | SRS Control unit |
| 2 | SRS Driver air bag squib |
| 3 | Left front ETR squib |
| 4 | Right front ETR squib |
| 5 | Model 140R12/8Front passenger airbag squib 1 |
| 17 | Low volts, Voltage supply circuit 15R |
| 19 | SRS indicator lamp. failure |
| 20 | Front passenger seat occupation signal (currently not used) |
| 24 | Driver seat belt buckle switch (Airbag/ETR) |
| 25 | Front passenger seat belt buckle switch (ETR) |
| 73 | Squib short circuit |

F3 SRS	CS1000 Code Scanner OB15-11

| Models | Model Years |
| --- | --- |
| 129 (R) 140 (S) 202 (C) 210 (E) | 1996-98 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 30 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | SRS-Control unit |
| 2 | SRS indicator lamp. failure |
| 3 | low volts, Voltage supply circuit 15R |
| 4 | Driver side air bag squib circuit |
| 5 | Driver side seat belt squib circuit |
| 6 | Front passenger side seat belt squib circuit |
| 7 | Front passenger side air bag squib circuit |
| 8 | Driver side front door air bag squib circuit |
| 9 | Front passenger side door air bag squib circuit |
| 16 | Driver side seat belt buckle switch |
| 17 | Front passenger side seat belt buckle switch |
| 18 | Driver side door air bag detect sensor circuit |
| 19 | Driver side door air bag detect sensor failure |
| 20 | Driver side door air bag detect sensor failure |
| 21 | Passenger side door air bag detect sensor circuit |
| 22 | Passenger side door air bag detect sensor failure |
| 23 | Passenger side door air bag detect sensor failure |
| 24 | Driver side seat occupation signal |
| 25 | Front passenger side seat occupation signal |
| 26 | Coded version not correct with control unit |
| 32 | Driver side door air bag detect sensor signal |
| 33 | Passenger side door air bag detect sensor signal |

Itt �&dn&U+!SI INnI+!bOL+ 1:n&I IU!&C+!OU �.A2+&W {Itt-�1:IJ

| Engines | Model Years |
| --- | --- |
| 104 | 119 | 120 | 1991-193 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 8 |
| Black | Socket 1 |
| Red | Socket 16 |

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Socket 3 |

(These fault codes numbers are only for the CS1000 Code Scanner. They are different from those found in the Mercedes Benz original Diagnostic Manual fault code tables.)

F4	LH-SFI “Current” Fault Codes (These codes do not turn on the MIL.)

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 001 | Injector, cylinder 1 circuit short to positive |
| 002 | Injector, cylinder 5 circuit short to positive |
| 003 | Injector, cylinder 4 circuit short to positive |
| 004 | Injector, cylinder 8 circuit short to positive |
| 005 | Injector, cylinder 6 circuit short to positive |
| 006 | Injector, cylinder 3 circuit short to positive |
| 007 | Injector, cylinder 7 circuit short to positive |
| 008 | Injector, cylinder 2 circuit short to positive |
| 009 | Injector, cylinder 1 open circuit or short to ground |
| 010 | Injector, cylinder 5 open circuit or short to ground |
| 011 | Injector, cylinder 4 open circuit or short to ground |
| 012 | Injector, cylinder 8 open circuit or short to ground |
| 013 | Injector, cylinder 6 open circuit or short to ground |
| 014 | Injector, cylinder 3 open circuit or short to ground |
| 015 | Injector, cylinder 7 open circuit or short to ground |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 016 | Injector, cylinder 2 open circuit or short to ground |
| 017 | HFM sensor Voltage too high or too low, may open circuit |
| 018 | Engine coolant temperature sensor short or open circuit |
| 019 | Engine coolant temperature sensor short or open circuit |
| 020 | Engine coolant temperature sensor signal questionable |
| 021 | Intake air temperature sensor short or open circuit |
| 022 | Exhaust temperature sensor short or open circuit (Japan version only) |
| 023 | CO potentiometer open circuit (non KAT) |
| 024 | LH-SFI control unit coding plug open circuit (not USA version) |
| 025 | Starter signal missing (circuit 50), may short or open circuit |
| 026 | Idle speed recognition from Cruise control/Electronic accelerator (CC/EA), circuit short to ground |
| 027 | Not used |
| 028 | O2S 1 signal, short or open circuit |
| 029 | Not used |
| 030 | Not used |
| 031 | O2S 2 signal, short or open circuit |
| 032 | Not used |
| 033 | CAN communication problem, No communication from LH control unit |
| 034 | CAN communication problem, No communication from ASR control unit |
| 035 | CAN communication problem, No communication from LH control unit |
| 036 | CAN communication problem, No communication from LH control unit |
| 037 | CAN communication problem, No communication from EZL/AKR ignition control unit |
| 038 | CAN communication problem, No communication from EZL/AKR ignition control unit |
| 038 | CAN communication problem, No communication from Cruise control/Electronic accelerator |
| 040 | Not used |
| 041 | Air injection system short or open circuit |
| 042 | Fuel purge switchover valve open or short circuit |
| 043 | Transmission switchover valve, circuit open or short |
| 044 | EGR switchover valve, circuit open or short |
| 045 | Camshaft timing adjust solenoid, circuit open or short |
| 046 | Camshaft timing Adjust solenoid, circuit open or short |
| 047 | First gear start relay, circuit open or short |
| 048 | Not used |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 049 | Air injection system circuit short or open |
| 050 | Fuel purge switchover valve circuit short or open |
| 051 | Transmission switchover valve relay or solenoid, circuit short or open |
| 052 | EGR switchover valve circuit short or open |
| 053 | camshaft timing Adjust solenoid circuit short or open |
| 054 | camshaft timing Adjust solenoid circuit short or open |
| 055 | First gear start relay circuit short or open |
| 056 | Not used |

F5 LH-SFI “Stored” Fault codes	(These codes turn on the MIL.)

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 001 | Not used |
| 002 | HFM sensor Voltage too high or too low, may open circuit |
| 003 | Engine coolant temperature sensor short or open circuit |
| 004 | Engine coolant temperature sensor short or open circuit |
| 005 | Intake air temperature sensor short or open circuit |
| 006 | Japan only Exhaust temperature sensor, circuit short or open |
| 007 | CO potentiometer open circuit (non KAT) |
| 008 | LH-SFI control unit coding plug open circuit (not USA version) |
| 009 | Starter signal circuit 50 missing, circuit short or open |
| 010 | Starter signal missing (circuit 50), may short or open circuit |
| 011 | O2S 1 signal, short or open circuit |
| 012 | CAN communication problem, No communication from LH control unit |
| 013 | CAN communication problem, No communication from Cruise control/Electronic accelerator |
| 014 | Camshaft position sensor circuit short or open |
| 015 | Air injection system circuit short or open |
| 016 | Air mass sensor, hot-wire burn-off control circuit short or open |
| 017 | EGR switchover valve, circuit open or short |
| 018 | CAN communication problem. No communication from EZL/AKR ignition control unit |
| 019 | CAN communication problem. No communication from LH control unit |
| 020 | Fuel purge switchover valve circuit short or open |
| 021 | camshaft timing Adjust solenoid circuit short or open |
| 022 | camshaft timing Adjust solenoid circuit short or open |
| 023 | Transmission switchover valve circuit short or open |
| 024 | Fuel injectors circuit short or open |
| 025 | First gear start relay circuit short or open |

HHHHt:.t:.t:.t:.ININININ ����GGGGdd

nnnnGGGGUUUU++++!!!!99

1111  ININININnnnn1111++++!!!!bbbbOOOOLLLL++++  t:.t:.t:.t:.nnnnGGGG1111  IIIIUUUU!!!!GGGGCCCC++++!!!!OOOOUUUU  ����AAAA2222++++GGGGWWWW  ((((HHHHt:.t:.t:.t:.ININININ----��

t:.t:.

IIIIJJJJ

| Engines | Model Years |
| --- | --- |
| 111 (4 cylinder, 2.2/2.3L engine) | 1994-97 |
| 104 (6 cylinder, 2.8/3.2L engine) | 1994-97 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 8 |
| Black | Socket 1 |
| Red | Socket 16 |

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Socket 3 |

(Code Scanner will display the fault code numbers listed under OB15, Mercedes factory numbers are listed under MB.)

HFM-SFI F6 for Current and F7 Stored Fault codes

| OB15 | MB | Description |
| --- | --- | --- |
| 000 |  | No fault found |
| 001 | (002) | Engine coolant temperature sensor, short circuit |
| 002 | (003) | Engine coolant temperature sensor, open circuit |
| 003 | (004) | Engine coolant temperature sensor signal incorrect |
| 004 | (006) | Intake air temperature sensor, short circuit |
| 005 | (007) | Intake air temperature sensor, open circuit |
| 006 | (009) | Hot film air mass sensor signal too high |
| 007 | (010) | Hot film air mass sensor, open circuit |
| 008 | (011) | Engine idle speed contact Throttle valve position too large |
| 009 |  | Not used |
| 010 | (012) | Engine idle speed contact air mass too large |
| 011 | (113) | HFM-SFI control unit not coded |
| 012 | (014) | Throttle valve potentiometer actual value too high |
| 013 | (015) | Throttle valve potentiometer actual value too low |
| 014 | (017) | Throttle valve potentiometer drive value implausibly high |
| 015 | (018) | Throttle valve potentiometer drive value implausibly low |
| 016 | (020) | ISC (Idle speed control) at lower control stop area, malfunction |

| OB15 | MB | Description |
| --- | --- | --- |
| 017 | (021) | ISC (Idle speed control) at upper control stop area, malfunction |
| 018 | (022) | CC,EFP actuator signals in limp home mode (emergency mode) |
| 019 | (023) | O2 sensor (before/upstream of Cat. Conv.), voltage too large |
| 020 | (024) | O2 sensor (before/upstream of Cat. Conv.), open circuit |
| 021 | (025) | O2 sensor (before/upstream of Cat. Conv.), signal incorrect |
| 022 | (026) | O2 sensor (after/downstream of Cat. Conv.), voltage too large |
| 023 | (027) | O2 sensor (after/downstream of Cat. Conv.), open circuit |
| 024 | (028) | O2 sensor (after/downstream of Cat. Conv.), signal incorrect |
| 025 | (029) | O2 sensor heater (before/upstream of Cat. Conv.), heater current (amp) too small |
| 026 | (030) | O2 sensor heater (before/upstream of Cat. Conv.), heater current (amp) too large |
| 027 | (031) | O2 sensor heater (before/upstream of Cat. Conv.), heater current, short circuit |
| 028 | (032) | O2 sensor heater (after/downstream of Cat. Conv.), heating current (amp) too small |
| 029 | (033) | O2 sensor heater (after/downstream of Cat. Conv.), heating current (amp) too large |
| 030 | (034) | O2 sensor heater (after/downstream of Cat. Conv.), heating current, short circuit |
| 031 | (035) | Fuel adaptation (lambda) control, mixture too lean (rich stop) (Intake air leak, fuel injectors, diaphragm pressure regulator) |
| 032 | (036) | Fuel adaptation (lambda) control, mixture too rich (lean stop) (Intake air leak, fuel injectors, diaphragm pressure regulator) |
| 033 | (037) | Injection valve cylinder 1, short to positive |
| 034 | (038) | Injection valve cylinder 1, open circuit or short to ground |
| 035 | (039) | Injection valve cylinder 2, short to positive |
| 036 | (040) | Injection valve cylinder 2, open circuit or short to ground |
| 037 | (041) | Injection valve cylinder 3, short to positive |
| 038 | (042) | Injection valve cylinder 3, open circuit or short to ground |
| 039 | (043) | Injection valve cylinder 4, short to positive |
| 040 | (044) | Injection valve cylinder 4, open circuit or short to ground |
| 041 | (045) | Injection valve cylinder 5, short to positive |
| 042 | (046) | Injection valve cylinder 5, open circuit or short to ground |
| 043 | (047) | Injection valve cylinder 6, short to positive |
| 044 | (048) | Injection valve cylinder 6, open circuit or short to ground |
| 045 | (049) | Self-adjustment too rich at Idle (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 046 | (050) | Self-adjustment too lean at Idle (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 047 | (051) | Self-adjustment too rich at Lower part load (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |

| OB15 | MB | Description |
| --- | --- | --- |
| 048 | (052) | Self-adjustment too lean at Lower part load (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 049 | (053) | Self-adjustment too rich at Upper part load (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 050 | (054) | Self-adjustment too lean at Upper part load (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 051 | (061) | Ignition system output stage 3, Cylinder 1 misfires |
| 052 | (062) | Ignition system output stage 3, Cylinder 6 misfires |
| 053 | (063) | Ignition system output stage 3, Current value not reached |
| 054 | (055) | Ignition system output stage 1, Cylinder 2 misfires |
| 055 | (056) | Ignition system output stage 1, Cylinder 5 misfires |
| 056 | (057) | Ignition system output stage 1, Current value not reached |
| 057 | (058) | Ignition system output stage 2, Cylinder 3 misfires |
| 058 | (059) | Ignition system output stage 2, Cylinder 4 misfires |
| 059 | (060) | Ignition system output stage 2, Current value not reached |
| 060 | (064) | Crankshaft signal incorrect |
| 061 | (065) | Crankshaft signal Magnet missing or Number of teeth incorrect |
| 062 | (066) | Crankshaft signal Speed incorrect, too high |
| 063 | (067) | Camshaft signal incorrect/not recognized |
| 064 | (068) | HFM circuit/trimming plug short to ground |
| 065 | (069) | HFM circuit/trimming plug open circuit or short to positive |
| 066 | (070) | TN speed signal (rpm) Output short to ground |
| 067 | (071) | TN speed signal (rpm) Output short to positive |
| 068 | (072) | Vehicle speed signal not recognized, short circuit |
| 069 | (073) | Vehicle speed signal implausibly high, short circuit |
| 070 | (074) | PSV relay K3/1 circuit short to positive |
| 071 |  | Not used |
| 072 | (076) | Fuel pump relay open circuit or short circuit |
| 073 |  | Not used |
| 074 | (077) | CO potentiometer Input short to positive |
| 075 | (079) | Knock sensor 1 signal open circuit |
| 076 | (080) | Knock sensor 2 signal open circuit |
| 077 | (081) | Ignition timing max retardation reached at least one cylinder |
| 078 | (082) | Ignition angle deviation between the individual cylinders too high |
| 079 | (083) | Knock control analysis, HFM control unit defective |
| 080 | (084) | Short-term self-adjustment Idle/Part-load fault |
| 081 | (085) | Air pump relay-module/switch-valve output, open circuit or short circuit |

| OB15 | MB | Description |
| --- | --- | --- |
| 082 |  | Not used |
| 083 |  | Not used |
| 084 | (086) | Fuel purge switch-valve, open circuit/short circuit |
| 085 | (087) | Fuel purge switch-valve, short to positive |
| 086 | (088) | Transmission shifting delay/smooth switch-valve, open circuit or short circuit |
| 087 |  | Not used |
| 088 |  | Not used |
| 089 | (089) | Camshaft timing adjust actuator circuit short to positive |
| 090 | (090) | Camshaft timing adjust actuator open circuit or short to ground |
| 091 | (091) | EGR switch-valve short to positive |
| 092 | (092) | EGR switch-valve open circuit or short to ground |
| 093 | (093) | Transmission overload protection switch short to ground |
| 094 | (094) | Transmission overload protection switch, circuit short or open |
| 095 | (095) | Transmission overload protection switch, circuit short or open |
| 096 | (096) | Transmission overload protection switch signal implausible |
| 097 | (097) | CAN problem Transmission communication from HFM control system faulty |
| 098 | (098) | CAN problem No data reception from ASR |
| 099 | (116) | CAN problem No data reception from IRCL. ( if equip with IRCL) Voltage supply at Circuit 87M, low voltage or implausible (Starting 06/93) |
| 100 |  | Not used |
| 101 | (099) | CAN problem No data reception from EFP,TPM |
| 102 | (100) | CAN problem No data reception from Diagnosis Module |
| 103 |  | Not used |
| 104 | (117) | Attempt to start with IRCL locked |
| 105 | (101) | No starter signal (Terminal 50), open or short circuit |
| 106 | (102) | Thermocouple CAT B16/6 Temperature too high |
| 107 | (103) | Thermocouple CAT B16/6 Temperature too low |
| 108 | (104) | Fuel safety cut-off settled |
| 109 |  | Not used |
| 110 | (105) | Resonance intake manifold switchover valve, short to positive |
| 111 | (106) | Resonance intake manifold switchover valve, open circuit/short to ground |
| 112 | (107) | Ignition dwell angle control output stage, short to ground |
| 113 | (114) | HFM control unit identification illogical |
| 114 | (108) | Oxygen sensor heater (after/downstream of Cat. Conv.), short to positive |
| 115 | (109) | Oxygen sensor heater (after/downstream of Cat. Conv.), open circuit or short to ground |

| OB15 | MB | Description |
| --- | --- | --- |
| 116 | (115) | HFM-SFI control unit N3/4 coding bytes illogical |
| 117 |  | Not used |
| 118 | (110) | Voltage supply to HFM-SFI control unit, incorrect |
| 119 | (111) | Voltage supply at HFM-SFI control unit, voltage too low |
| 120 | (112) | HFM control unit faulty |
| 121 | (005) | Coolant temperature sensor, Loose contact |
| 122 | (008) | Intake air temperature sensor, Loose contact |
| 123 | (013) | Idle speed contact, Loose contact |
| 124 | (016) | Potentiometer throttle valve, Loose contact |
| 125 | (019) | Potentiometer throttle valve drive, Loose contact |
| 126 | (078) | CO potentiometer R33 Loose contact |
| 127 |  | Not used |
| 128 |  | Not used |

DIN� 1:n&1 IUl&C+!OU �A2+&W

| Engines | Model Years |
| --- | --- |
| 111 (4 cylinders, 1.8/2.0L engine) | 1994-97 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 8 |
| Black | Socket 1 |
| Red | Socket 16 |

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Socket 3 |

(Code Scanner will display the fault code numbers listed under OB15, Mercedes factory numbers are listed under MB.)

PMS F6 for “Current” and F7 “Stored” Fault Codes

| OB15 | MB | Description |
| --- | --- | --- |
| 001 | (002) | Coolant temperature sensor, short circuit |
| 002 | (003) | Coolant temperature sensor, open circuit |
| 003 | (004) | Coolant temperature sensor, incorrect |
| 004 | (006) | Intake air temperature sensor, short circuit |
| 005 | (007) | Intake air temperature sensor, open circuit |
| 006 | (009) | PMS Control unit, Intake manifold pressure implausible |
| 007 | (010) | PMS Control unit, No Intake manifold pressure |
| 008 | (011) | Idle speed contact closed signal incorrect |
| 009 | (068) | Idle speed contact open circuit |
| 010 |  | Not used |
| 011 |  | Not used |
| 012 | (013) | Potentiometer throttle valve, value too high |
| 013 | (014) | Potentiometer throttle valve, value too low |
| 014 | (016) | Potentiometer throttle valve drive value too high/incorrect |
| 015 | (017) | Potentiometer throttle valve drive value too low/incorrect |
| 016 | (019) | Idle speed control at lower control stop area, malfunction |
| 017 | (020) | Idle speed control at upper control stop area, malfunction |
| 018 | (021) | Idle speed control in limp home-mode (emergency operation) |

| OB15 | MB | Description |
| --- | --- | --- |
| 019 | (022) | O2 sensor voltage too large |
| 020 | (023) | O2 sensor, open circuit |
| 021 | (024) | O2 sensor signal illogical |
| 022 | (069) | Exhaust flap short to positive |
| 023 | (070) | Exhaust flap open circuit or short to ground |
| 024 |  | Not used |
| 025 | (025) | O2 sensor heater current (amps) too small |
| 026 | (026) | O2 sensor heater current (amps) too large |
| 027 | (027) | O2 sensor heater, short circuit |
| 028 |  | Not used |
| 029 |  | Not used |
| 030 |  | Not used |
| 031 | (028) | Fuel adaptation (lambda) control mixture too lean (Intake air leak, fuel injectors, diaphragm pressure regulator) |
| 032 | (029) | Fuel adaptation (lambda) control mixture too rich (Intake air leak, fuel injectors, diaphragm pressure regulator) |
| 033 | (030) | Injection valve cylinder 1/4 short to positive |
| 034 | (031) | Injection valve cylinder 1/4 open circuit or short to ground |
| 035 | (032) | Injection valve cylinder 2/3 short to positive |
| 036 | (033) | Injection valve cylinder 2/3 open circuit or short to ground |
| 037 | (064) | Input signal from IFZ, open circuit or short to positive |
| 038 | (065) | Input signal from IFZ, short to ground |
| 039 | (066) | IFZ system unresponsive |
| 040 | (067) | Input signal from IFZ incorrect |
| 041 |  | Not used |
| 042 |  | Not used |
| 043 |  | Not used |
| 044 |  | Not used |
| 045 | (034) | Self-adjustment too rich at Idle (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 046 | (035) | Self-adjustment too lean at Idle (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 047 | (036) | Self-adjustment too rich at Part load (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 048 | (037) | Self-adjustment too lean at Part load (Intake air leak, fuel injectors, diaphragm pressure regulator, wear engine) |
| 049 |  | Not used |

| OB15 | MB | Description |
| --- | --- | --- |
| 050 |  | Not used |
| 051 | (038) | Ignition system output stage 1, short to positive |
| 052 | (039) | Ignition system output stage 1, Cylinder 1/4 misfires |
| 053 | (040) | Ignition system output stage 1, Amperage not achieved |
| 054 | (041) | Ignition system output stage 2, short to positive |
| 055 | (042) | Ignition system output stage 2, Cylinder 2/3 misfires |
| 056 | (043) | Ignition system output stage 2, Amperage not achieved |
| 057 |  | Not used |
| 058 |  | Not used |
| 059 |  | Not used |
| 060 | (044) | Crankshaft signal incorrect |
| 061 | (045) | Crankshaft signal Magnet missing or Numbers of teeth incorrect |
| 062 | (046) | Crankshaft signal Speed incorrect, too high |
| 063 |  | Not used |
| 064 | (047) | PMS circuit/trimming plug short to ground |
| 065 | (048) | PMS circuit/trimming plug open circuit or short to positive |
| 066 | (049) | TN speed signal (rpm) Output short to ground |
| 067 | (050) | TN speed signal (rpm) Output short to positive |
| 068 | (051) | Vehicle speed signal not recognized, short circuit |
| 069 | (052) | Vehicle speed signal too high, short circuit |
| 070 | (053) | PSV relay open circuit or short to positive |
| 071 | (054) | PSV relay short to ground |
| 072 | (055) | Fuel pump relay open circuit or short to positive |
| 073 | (056) | Fuel pump relay short to ground |
| 074 | (057) | CO potentiometer Input circuit short to positive |
| 075 ~079 |  | Not used |
| 080 | (061) | Short-term self-adjustment faulty at idle speed or part load |
| 081 | (071) | Rear axle ratio was changed |
| 082 | (072) | Rear axle ratio signal incorrect |
| 083 |  | Not used |
| 084 | (059) | Fuel purge switch-valve open circuit or short to positive |
| 085 | (060) | Fuel purge switch-valve short to ground |
| 086 | (062) | Transmission shifting delay/smooth switch-valve, open circuit or short circuit |
| 087 ~092 |  | Not used |
| 093 | (073) | Transmission protection short to ground or active too long |
| 094 |  | Not used |

| OB15 | MB | Description |
| --- | --- | --- |
| 095 |  | Not used |
| 096 | (074) | Transmission protection open circuit or short to positive |
| 097 ~ 118 |  | Not used |
| 119 | (063) | PMS control unit voltage supply too low |
| 120 |  | Not used |
| 121 | (005) | Coolant temperature sensor, Loose contact |
| 122 | (008) | Intake air temperature sensor, Loose contact |
| 123 | (012) | Idle speed contact, Loose contact |
| 124 | (015) | Potentiometer throttle valve, Loose contact |
| 125 | (018) | potentiometer throttle valve drive value, Loose contact |
| 126 | (058) | CO potentiometer circuit, Loose contact |
| 127 |  | Not used |
| 128 |  | Not used |

SEE ME-SFI INJECTION FOR ALL DIAGNOSTIC CODES FROM 8/96 PRODUCTION AND LATER FOR ALL MODELS.

| Engines | Model Years |
| --- | --- |
| 104 | 119 | 120 | 1991-96 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 3 |
| Black | Socket 1 |
| Red | Socket 16 |

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 19 |
| Black | Socket 1 |
| Red | Socket 3 |

DM F8 for “Current”, F9 “Stored” and F10 “Registered” Fault Codes

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 000 | No fault found |
| 002 | Oxygen sensor. No signal (right bank in 120) |
| 003 | Fuel adaptation (lambda control), inoperative. Engine control module (right bank in 120) |
| 004 | Air injection defective, fault from Fuel control system (right bank in 120) |
| 005 | EGR exhaust gas recirculation incorrect, fault. Engine control module (right bank in 120) |
| 006 | Idle speed control incorrect, fault from EA/CC/ISC |
| 007 | Ignition system defective, fault from Fuel/Ignition control system (right bank in 120) |
| 008 | Coolant temperature sensor signal. Open or short circuit (right bank in 120) |
| 009 | Intake air temperature sensor signal. Open or short circuit (right bank in 120) |
| 010 | Air mass sensor voltage signal too high /low. (right bank in 120) |
| 011 | Engine speed signal TN (RPM) or Engine control module (right bank in 120) defective |
| 012 | Oxygen sensor heater circuit. Open or short circuit (right bank in 120) |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 013 | Camshaft position sensor (CMP) signal, fault from Fuel/Ignition control system (right bank in 120) |
| 014 | Intake manifold pressure value at start too high/low, fault from Fuel/Ignition control system (right bank in 120) |
| 015 | Wide open throttle (WOT) signal incorrect/implausible. |
| 016 | Closed throttle position (CTP) sensor signal incorrect/implausible. |
| 017 | CAN communication faulty in between control units (right bank in 120). |
| 018 | Camshaft timing adjust solenoid, open or short circuit (right bank in 120) |
| 019 | Fuel injector circuit, open or short circuit or self adaptation at limit. (right bank in 120) |
| 020 | Speed signal missing |
| 021 | Fuel purge control valve, open or short circuit (right bank in 120) |
| 022 | Camshaft position sensor (CMP) signal defective (right bank in 120) |
| 023 | Intake manifold pressure sensor signal incorrect, too high/low. (right bank in 120) |
| 024 | Crankshaft position sensor (CKP) signal incorrect or starter ring gear segment damaged. |
| 025 | Knock sensors circuit or Ignition control module defective (right bank in 120) |
| 026 | Transmission upshift delay switch over valve, open or short circuit. |
| 027 | Engine coolant temperature (ECT) sensors circuit 1 and 2 have difference values. (right bank in 120) |
| 028 | Engine coolant sensor/Operating temperature error. (right bank in 120) |
| 034 | Oxygen sensor. No signal (left bank in 120) |
| 035 | Fuel adaptation (lambda control), inoperative. Engine control module (left bank in 120) |
| 036 | Air injection defective, fault from Fuel control system (left bank in 120) |
| 037 | EGR exhaust gas recirculation incorrect, fault. Engine control module (left bank in 120) |
| 038 | Not used |
| 039 | Ignition system defective, fault from Fuel/Ignition control system (left bank in 120) |
| 040 | Coolant temperature sensor signal. Open or short circuit (left bank in 120) |
| 041 | Intake air temperature sensor signal. Open or short circuit (left bank in 120) |
| 042 | Air mass sensor voltage signal too high /low. (left bank in 120) |
| 043 | Engine speed signal TN (RPM) or Engine control module (left bank in 120) defective |
| 044 | Oxygen sensor heater circuit. Open or short circuit (left bank in 120) |

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 045 | Camshaft position sensor (CMP) signal, fault from Fuel/Ignition control system (left bank in 120) |
| 046 | Intake manifold pressure value at start too high/low, fault from Fuel/Ignition control system (left bank in 120) |
| 047 | Not used. |
| 048 | Not used. |
| 049 | CAN communication faulty in between control units (left bank in 120). |
| 050 | Camshaft timing adjust solenoid, open or short circuit (left bank in 120) |
| 051 | Fuel injector circuit, open or short circuit or self adaptation at limit. (left bank in 120) |
| 052 | Not used. |
| 053 | Fuel purge control valve, open or short circuit (left bank in 120) |
| 054 | Camshaft position sensor (CMP) signal defective (left bank in 120) |
| 055 | Intake manifold pressure sensor signal incorrect, too high/low. (left bank in 120) |
| 056 | Crankshaft position sensor (CKP) signal incorrect or starter ring gear segment damaged. |
| 057 | Knock sensors circuit or Ignition control module defective (left bank in 120) |
| 058 | Not used. |
| 059 | Engine coolant temperature (ECT) sensors circuit 1 and 2 have difference values. (left bank in 120) |
| 060 | Engine coolant sensor/Operating temperature error. (left bank in 120) |
| 063 | Annomalous Code (Battery Jump most likely Caused) |

INt: �6dn6U+!91 INn1+!bOL+ 1:n61 IU!6C+!OU �A2+6W (INt:-�1:IJ

*ME Injection includes both EA/CC/ISC and DM codes.

| Engines | Model Years |
| --- | --- |
| 104 (6 cylinders, 2.8/3.2L engine) | 8/96- |
| 111 (4 cylinder | 8/96- |
| 112 (V6 engine, 2.4/2.8/3.2L) | 8/97- |
| 119 (V8 engine 4.2/5.0L) | 8/95-1998 |
| 120 (12 cylinder engine) | 8/95-1998 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 4 |
| Black | Socket 1 |
| Red | Socket 3 |

There are five digital numbers in one fault code. Code Scanner will automatically to display the one digital number first then display the four digital numbers later. For example, the fault code "00100" will display C	0 then  0 1 0 0.

ME-SFI F11 “Current” and F12 “Stored” Fault Codes

| OB15 | MB | Description |
| --- | --- | --- |
| 00100 | P0100 | Hot-film mass air flow sensor signal incorrect |
| 00101 | P0101 | Mass or Volume Air flow Circuit Range/Performance Problem |
| 00102 | P0102 | Mass or Volume Air Flow Circuit low Input |
| 00103 | P0103 | Mass or Volume Air flow Circuit High Input |
| 00104 | P0104 | Mass or Volume Air flow Circuit Intermittent |
| 00105 | P0105 | Manifold Absolute Pressure (MAP) Pressure Circuit Malfunction |
| 00106 | P0106 | Manifold Absolute Pressure/Barometric Pressure Circuit Range/Performance Problem |
| 00107 | P0107 | Manifold Absolute Pressure/Barometric Pressure Circuit Low Input |
| 00108 | P0108 | Manifold Absolute Pressure/Barometric Pressure Circuit High Input |
| 00109 | P0109 | Manifold Absolute Pressure/Barometric Pressure Circuit Intermittent |
| 00110 | P0110 | Intake air temp. sensor signal in the Hot film mass air flow sensor |
| 00111 | P0111 | Intake Air Temperature Circuit Range/Performance Problem |
| 00112 | P0112 | Intake Air Temperature Circuit Low Input |
| 00113 | P0113 | Intake Air Temperature Circuit High Input |
| 00114 | P0114 | Intake Air Temperature Circuit Intermittent |
| 00115 | P0115 | Engine Coolant Temperature Circuit Malfunction |

| OB15 | MB | Description |
| --- | --- | --- |
| 00116 | P0116 | Engine Coolant Temperature Circuit Range/Performance Problem |
| 00117 | P0117 | Engine Coolant Temperature Circuit Low Input |
| 00118 | P0118 | Engine Coolant Temperature Circuit High Input |
| 00119 | P0119 | Engine Coolant Temperature Circuit Intermittent |
| 00120 | P0120 | Throttle Potentiometer Actuator Actual value, EA/CC/ISC Actuator |
| 00121 | P0121 | Throttle/Pedal Position Sensor/Switch A Circuit Range/Performance Problem |
| 00122 | P0122 | Throttle/Pedal Position Sensor/Switch A Circuit low Input |
| 00123 | P0123 | Throttle/Pedal Position Sensor/Switch A Circuit High Input |
| 00124 | P0124 | Throttle/Pedal Position Sensor/Switch A Circuit Intermittent |
| 00125 | P0125 | Insufficient Coolant Temperature for Closed Loop Fuel Control |
| 00126 | P0126 | Insufficient Coolant Temperature for Stable Operation |
| 00130 | P0130 | O2 Sensor Circuit Malfunction (Bank 1 Sensor 1) |
| 00131 | P0131 | O2 Sensor Circuit Low Voltage (Bank 1 Sensor 1) |
| 00132 | P0132 | O2 Sensor Circuit High Voltage (Bank 1 Sensor 1) |
| 00133 | P0133 | O2 Sensor Circuit Slow Response (Bank 1 Sensor 1) |
| 00134 | P0134 | O2 Sensor Circuit No Activity Detected (Bank 1 Sensor 1) |
| 00135 | P0135 | O2 Sensor Heater Circuit Malfunction (Bank 1 Sensor 1) |
| 00136 | P0136 | O2 Sensor Circuit Malfunction (Bank 1 Sensor 2) |
| 00137 | P0137 | O2 Sensor Circuit Low Voltage (Bank 1 Sensor 2) |
| 00138 | P0138 | O2 Sensor Circuit High Voltage (Bank 1 Sensor 2) |
| 00139 | P0139 | O2 Sensor Circuit Slow Response (Bank 1 Sensor 2) |
| 00140 | P0140 | O2 Sensor Circuit No Activity Detected (Bank 1 Sensor 2) |
| 00141 | P0141 | O2 Sensor Heater Circuit Malfunction (Bank 1 Sensor 2) |
| 00142 | P0142 | O2 Sensor Circuit Malfunction (Bank 1 Sensor 3) |
| 00143 | P0143 | O2 Sensor Circuit Low Voltage (Bank 1 Sensor 3) |
| 00144 | P0144 | O2 Sensor Circuit High Voltage (Bank 1 Sensor 3) |
| 00145 | P0145 | O2 Sensor Circuit Slow Response (Bank 1 Sensor 3) |
| 00146 | P0146 | O2 Sensor Circuit No Activity Detected (Bank 1 Sensor 3) |
| 00147 | P0147 | O2 Sensor Heater Circuit Malfunction (Bank 1 Sensor 3) |
| 00150 | P0150 | O2 Sensor Circuit Malfunction (Bank 2 Sensor 1) |
| 00151 | P0151 | O2 Sensor Circuit Low Voltage (Bank 2 Sensor 1) |
| 00152 | P0152 | O2 Sensor Circuit High Voltage (Bank 2 Sensor 1) |
| 00153 | P0153 | O2 Sensor Circuit Slow Response (Bank 2 Sensor 1) |
| 00154 | P0154 | O2 Sensor Circuit No Activity Detected (Bank 2 Sensor 1) |
| 00155 | P0155 | O2 Sensor Heater Circuit Malfunction (Bank 2 Sensor 1) |
| 00156 | P0156 | O2 Sensor Circuit Malfunction (Bank 2 Sensor 2) |
| 00157 | P0157 | O2 Sensor Circuit Low Voltage (Bank 2 Sensor 2) |

| OB15 | MB | Description |
| --- | --- | --- |
| 00158 | P0158 | O2 Sensor Circuit High Voltage (Bank 2 Sensor 2) |
| 00159 | P0159 | O2 Sensor Circuit Slow Response (Bank 2 Sensor 2) |
| 00160 | P0160 | O2 Sensor Circuit No Activity Detected (Bank 2 Sensor 2) |
| 00161 | P0161 | O2 Sensor Heater Circuit Malfunction (Bank 2 Sensor 2) |
| 00162 | P0162 | O2 Sensor Circuit Malfunction (Bank 2 Sensor 3) |
| 00163 | P0163 | O2 Sensor Circuit Low Voltage (Bank 2 Sensor 3) |
| 00164 | P0164 | O2 Sensor Circuit High Voltage (Bank 2 Sensor 3) |
| 00165 | P0165 | O2 Sensor Circuit Slow Response (Bank 2 Sensor 3) |
| 00166 | P0166 | O2 Sensor Circuit No Activity Detected (Bank 2 Sensor 3) |
| 00167 | P0167 | O2 Sensor Heater Circuit Malfunction (Bank 2 Sensor 3) |
| 00170 | P0170 | Fuel Trim Malfunction (Bank 1) |
| 00171 | P0171 | System Too Lean (Bank 1) |
| 00172 | P0172 | System Too Rich (Bank 1) |
| 00173 | P0173 | Fuel Trim Malfunction (Bank 2) |
| 00174 | P0174 | System Too Lean (Bank 2) |
| 00175 | P0175 | System Too Rich (Bank 2) |
| 00176 | P0176 | Fuel Composition Sensor Circuit Malfunction |
| 00177 | P0177 | Fuel Composition Sensor Circuit Range/Performance |
| 00178 | P0178 | Fuel Composition Sensor Circuit Low Input |
| 00179 | P0179 | Fuel Composition Sensor Circuit High Input |
| 00180 | P0180 | Fuel Temperature Sensor A Circuit Malfunction |
| 00181 | P0181 | Fuel Temperature Sensor A Circuit Performance |
| 00182 | P0182 | Fuel Temperature Sensor A Circuit low Input |
| 00183 | P0183 | Fuel Temperature Sensor A Circuit High Input |
| 00184 | P0184 | Fuel Temperature Sensor A Circuit Intermittent |
| 00185 | P0185 | Fuel Temperature Sensor B Circuit Malfunction |
| 00186 | P0186 | Fuel Temperature Sensor B Circuit Range/Performance |
| 00187 | P0187 | Fuel Temperature Sensor U Circuit Low Input |
| 00188 | P0188 | Fuel Temperature Sensor B Circuit High Input |
| 00189 | P0189 | Fuel Temperature Sensor B Circuit Intermittent |
| 00190 | P0190 | Fuel Rail Pressure Sensor Circuit Malfunction |
| 00191 | P0191 | Fuel Rail Pressure Sensor Circuit Range/Performance |
| 00192 | P0192 | Fuel Rail Pressure Sensor Circuit Low Input |
| 00193 | P0193 | Fuel Rail Pressure Sensor Circuit High Input |
| 00194 | P0194 | Fuel Rail Pressure Sensor Circuit Intermittent |
| 00195 | P0195 | Engine Oil Temperature Sensor Malfunction |
| 00196 | P0196 | Engine Oil Temperature Sensor Range/Performance |

| OB15 | MB | Description |
| --- | --- | --- |
| 00197 | P0197 | Engine Oil Temperature Sensor Low |
| 00198 | P0198 | Engine Oil Temperature Sensor High |
| 00199 | P0199 | Engine Oil Temperature Sensor Intermittent |
| 00200 | P0200 | Injector Circuit Malfunction |
| 00201 | P0201 | Injector Circuit Malfunction - Cylinder 1 |
| 00202 | P0202 | Injector Circuit Malfunction - Cylinder 2 |
| 00203 | P0203 | Injector Circuit Malfunction - Cylinder 3 |
| 00204 | P0204 | Injector Circuit Malfunction - Cylinder 4 |
| 00205 | P0205 | Injector Circuit Malfunction - Cylinder 5 |
| 00206 | P0206 | Injector Circuit Malfunction - Cylinder 6 |
| 00207 | P0207 | Injector Circuit Malfunction - Cylinder 7 |
| 00208 | P0208 | Injector Circuit Malfunction - Cylinder 8 |
| 00209 | P0209 | Injector Circuit Malfunction - Cylinder 9 |
| 00210 | P0210 | Injector Circuit Malfunction - Cylinder 10 |
| 00211 | P0211 | Injector Circuit Malfunction - Cylinder 11 |
| 00212 | P0212 | Injector Circuit Malfunction - Cylinder 12 |
| 00213 | P0213 | Cold Start Injector 1 Malfunction |
| 00214 | P0214 | Cold Start Injector 2 Malfunction |
| 00215 | P0215 | Engine Shutoff Solenoid Malfunction |
| 00216 | P0216 | Injection Timing Control Circuit Malfunction |
| 00217 | P0217 | Engine Overtemp Condition |
| 00218 | P0218 | Transmission Over Temperature Condition |
| 00219 | P0219 | Engine Over Speed Condition |
| 00220 | P0220 | Throttle/Pedal Position Sensor/Switch B Circuit Malfunction |
| 00221 | P0221 | Throttle/pedal Position Sensor/Switch B Circuit Range/Performance Problem |
| 00222 | P0222 | Throttle/pedal Position Sensor/Switch B Circuit Low Input |
| 00223 | P0223 | Throttle/Pedal Position Sensor/Switch B Circuit High Input |
| 00224 | P0224 | Throttle/Pedal Position Sensor/Switch B Circuit Intermittent |
| 00225 | P0225 | Throttle/Pedal Position Sensor/Switch C Circuit Malfunction |
| 00226 | P0226 | Throttle/Pedal Position Sensor/Switch C Circuit Range/Performance Problem |
| 00227 | P0227 | Throttle/Pedal Position Sensor/Switch C Circuit Low Input |
| 00228 | P0228 | Throttle/Pedal Position Sensor/Switch C Circuit High Input |
| 00229 | P0229 | Throttle/Pedal Position Sensor/Switch C Circuit Intermittent |
| 00230 | P0230 | Fuel Pump Primary Circuit Malfunction |
| 00231 | P0231 | Fuel Pump Secondary Circuit Low |
| 00232 | P0232 | Fuel Pump Secondary Circuit High |
| 00233 | P0233 | Fuel Pump Secondary Circuit Intermittent |

| OB15 | MB | Description |
| --- | --- | --- |
| 00234 | P0234 | Engine Overboost Condition |
| 00235 | P0235 | Turbocharger Boost Sensor A Circuit Malfunction |
| 00236 | P0236 | Turbocharger Boost Sensor A Circuit Range/Performance |
| 00237 | P0237 | Turbocharger Boost Sensor A Circuit Low |
| 00238 | P0238 | Turbocharger Boost Sensor A Circuit High |
| 00239 | P0239 | Turbocharger Boost Sensor B Circuit Malfunction |
| 00240 | P0240 | Turbocharger Boost Sensor B Circuit Range/Performance |
| 00241 | P0241 | Turbocharger Boost Sensor B Circuit Low |
| 00242 | P0242 | Turbocharger Boost Sensor B Circuit High |
| 00243 | P0243 | Turbocharger Wastegate Solenoid A Malfunction |
| 00244 | P0244 | Turbocharger Wastegate Solenoid A Range/Performance |
| 00245 | P0245 | Turbocharger Wastegate Solenoid A low |
| 00246 | P0246 | Turbocharger Wastegate Solenoid A High |
| 00247 | P0247 | Turbocharger Wastegate Solenoid B Malfunction |
| 00248 | P0248 | Turbocharger Wastegate Solenoid B Range/Performance |
| 00249 | P0249 | Turbocharger Wastegate Solenoid B Low |
| 00250 | P0250 | Turbocharger Wastegate Solenoid B High |
| 00251 | P0251 | Injection Pump Fuel Metering Control "A" Malfunction (Cam/Rotor/Injector) |
| 00252 | P0252 | Injection Pump Fuel Metering Control "A" Range/Performance (Cam/Rotor/Injector) |
| 00253 | P0253 | Injection Pump Fuel Metering Control "A" Low (Cam/Rotor/Injector) |
| 00254 | P0254 | Injection Pump Fuel Metering Control "A" High (Cam/Rotor/Injector) |
| 00255 | P0255 | Injection Pump Fuel Metering Control "A" Intermittent (Cam/Rotor/Injector) |
| 00256 | P0256 | Injection Pump Fuel Metering Control "B" Malfunction (Cam/Rotor/Injector) |
| 00257 | P0257 | Injection Pump Fuel Metering Control "B" Range/Performance (Cam/Rotor/Injector) |
| 00258 | P0258 | Injection Pump Fuel Metering Control "B" Low (Cam/Rotor/Injector) |
| 00259 | P0259 | Injection lump Fuel Metering Control "B" High (Cam/Rotor/Injector) |
| 00260 | P0260 | Injection Pump Fuel Metering Control "B" Intermittent (Cam/Rotor/Injector) |
| 00261 | P0261 | Cylinder 1 Injector Circuit Low |
| 00262 | P0262 | Cylinder 1 Injector Circuit High |
| 00263 | P0263 | Cylinder 1 Contribution/Balance Fault |
| 00264 | P0264 | Cylinder 2 Injector Circuit Low |
| 00265 | P0265 | Cylinder 2 Injector Circuit High |
| 00266 | P0266 | Cylinder 2 Contribution/Balance Fault |
| 00267 | P0267 | Cylinder 3 Injector Circuit Low |
| 00268 | P0268 | Cylinder 3 Injector Circuit High |
| 00269 | P0269 | Cylinder 3 Contribution/Balance Fault |

| OB15 | MB | Description |
| --- | --- | --- |
| 00270 | P0270 | Cylinder 4 Injector Circuit Low |
| 00271 | P0271 | Cylinder 4 Injector Circuit High |
| 00272 | P0272 | Cylinder 4 Contribution/Balance Fault |
| 00273 | P0273 | Cylinder 5 Injector Circuit Low |
| 00274 | P0274 | Cylinder 5 Injector Circuit High |
| 00275 | P0275 | Cylinder 5 Contribution/Balance Fault |
| 00276 | P0276 | Cylinder 6 Injector Circuit Low |
| 00277 | P0277 | Cylinder 6 Injector Circuit High |
| 00278 | P0278 | Cylinder 6 Contribution/Balance Fault |
| 00279 | P0279 | Cylinder 7 Injector Circuit Low |
| 00280 | P0280 | Cylinder 7 Injector Circuit High |
| 00281 | P0281 | Cylinder 7 Contribution/Balance Fault |
| 00282 | P0282 | Cylinder 8 Injector Circuit Low |
| 00283 | P0283 | Cylinder 8 Injector Circuit High |
| 00284 | P0284 | Cylinder 8 Contribution/Balance Fault |
| 00285 | P0285 | Cylinder 9 Injector Circuit Low |
| 00286 | P0286 | Cylinder 9 Injector Circuit High |
| 00287 | P0287 | Cylinder 9 Contribution/Balance Fault |
| 00288 | P0288 | Cylinder 10 Injector Circuit Low |
| 00289 | P0289 | Cylinder 10 Injector Circuit High |
| 00290 | P0290 | Cylinder 10 Contribution/balance Fault |
| 00291 | P0291 | Cylinder 11 Injector Circuit Low |
| 00292 | P0292 | Cylinder 11 Injector Circuit High |
| 00293 | P0293 | Cylinder 11 Contribution/balance Fault |
| 00294 | P0294 | Cylinder 12 Injector Circuit Low |
| 00295 | P0295 | Cylinder 12 Injector Circuit High |
| 00296 | P0296 | Cylinder 12 Contribution/Balance Fault |
| 00300 | P0300 | Random/Multiple Cylinder Misfire Detected |
| 00301 | P0301 | Cylinder 1 Misfire Detected |
| 00302 | P0302 | Cylinder 2 Misfire Detected |
| 00303 | P0303 | Cylinder 3 Misfire Detected |
| 00304 | P0304 | Cylinder 4 Misfire Detected |
| 00305 | P0305 | Cylinder 5 Misfire Detected |
| 00306 | P0306 | Cylinder 6 Misfire Detected |
| 00307 | P0307 | Cylinder 7 Misfire Detected |
| 00308 | P0308 | Cylinder 8 Misfire Detected |
| 00309 | P0309 | Cylinder 9 Misfire Detected |

| OB15 | MB | Description |
| --- | --- | --- |
| 00310 | P0310 | Cylinder 10 Misfire Detected |
| 00311 | P0311 | Cylinder 11 Misfire Detected |
| 00312 | P0312 | Cylinder 12 Misfire Detected |
| 00320 | P0320 | Ignition/Distributor Engine Speed Input Circuit Malfunction |
| 00321 | P0321 | Ignition/Distributor Engine Speed Input Circuit Range/Performance |
| 00322 | P0322 | Ignition/Distributor Engine Speed Input Circuit No Signal |
| 00323 | P0323 | Ignition/Distributor Engine Speed Input Circuit Intermittent |
| 00325 | P0325 | Knock Sensor 1 (Front) Circuit Malfunction (Bank 1 or Single Sensor) |
| 00326 | P0326 | Knock Sensor 1 Circuit Range/Performance (Bank 1 or Single Sensor) |
| 00327 | P0327 | Knock Sensor 1 Circuit low Input (Bank 1 or Single Sensor) |
| 00328 | P0328 | Knock Sensor 1 Circuit High Input (Bank 1 or Single Sensor) |
| 00329 | P0329 | Knock Sensor 1 Circuit Input Intermittent (Bank 1 or Single Sensor) |
| 00330 | P0330 | Knock Sensor 2 (Rear) Circuit Malfunction (Bank 2) |
| 00331 | P0331 | Knock Sensor 2 Circuit Range/Performance (Bank 2) |
| 00332 | P0332 | Knock Sensor 2 Circuit Low Input (Bank 2) |
| 00333 | P0333 | Knock Sensor 2 Circuit High Input (Bank 2) |
| 00334 | P0334 | Knock Sensor 2 Circuit Input Intermittent (Bank 2) |
| 00335 | P0335 | Crankshaft Position Sensor A Circuit Malfunction |
| 00336 | P0336 | Crankshaft Position Sensor A Circuit Range/Performance |
| 00337 | P0337 | Crankshaft Position Sensor A Circuit Low Input |
| 00338 | P0338 | Crankshaft Position Sensor A Circuit High Input |
| 00339 | P0339 | Crankshaft Position Sensor A Circuit Intermittent |
| 00340 | P0340 | Camshaft Position Sensor Circuit Malfunction |
| 00341 | P0341 | Camshaft Position Sensor Circuit Range/Performance |
| 00342 | P0342 | Camshaft Position Sensor Circuit Low Input |
| 00343 | P0343 | Camshaft Position Sensor Circuit High Input |
| 00344 | P0344 | Camshaft Position Sensor Circuit Intermittent |
| 00350 | P0350 | Ignition Coil Primary/Secondary Circuit Malfunction |
| 00351 | P0351 | Ignition Coil A Primary/Secondary Circuit Malfunction |
| 00352 | P0352 | Ignition Coil B Primary/Secondary Circuit Malfunction |
| 00353 | P0353 | Ignition Coil C Primary/Secondary Circuit Malfunction |
| 00354 | P0354 | Ignition Coil D Primary/Secondary Circuit Malfunction |
| 00355 | P0355 | Ignition Coil B Primary/Secondary Circuit Malfunction |
| 00356 | P0356 | Ignition Coil F Primary/Secondary Circuit Malfunction |
| 00357 | P0357 | Ignition Coil G Primary/Secondary Circuit Malfunction |
| 00358 | P0358 | Ignition Coil H Primary/Secondary Circuit Malfunction |
| 00359 | P0359 | Ignition Coil I Primary/Secondary Circuit Malfunction |

| OB15 | MB | Description |
| --- | --- | --- |
| 00360 | P0360 | Ignition Coil I Primary/Secondary Circuit Malfunction |
| 00361 | P0361 | Ignition Coil K Primary/Secondary Circuit Malfunction |
| 00362 | P0362 | Ignition Coil L Primary/Secondary Circuit Malfunction |
| 00370 | P0370 | Timing Reference High Resolution Signal (Camshaft to Crankshaft Angle) A Malfunction |
| 00371 | P0371 | Timing Reference High Resolution Signal (Camshaft to Crankshaft Angle) A Too Many Pulses |
| 00372 | P0372 | Timing Reference High Resolution Signal (Camshaft to Crankshaft Angle) A Too Few Pulses |
| 00373 | P0373 | Timing Reference High Resolution Signal (Camshaft to Crankshaft Angle) A Intermittent/Erratic Pulses |
| 00374 | P0374 | Timing Reference High Resolution Signal (Camshaft to Crankshaft angle) A No Pulses |
| 00375 | P0375 | Timing Reference High Resolution Signal (Camshaft to Crankshaft angle) B Malfunction |
| 00376 | P0376 | Timing Reference High Resolution Signal (Camshaft to Crankshaft angle) B Too Many Pulses |
| 00377 | P0377 | Timing Reference High Resolution Signal (Camshaft to Crankshaft angle) B Too Few Pulses |
| 00378 | P0378 | Timing Reference High Resolution Signal (Camshaft to Crankshaft angle) B Intermittent/Erratic Pulses |
| 00379 | P0379 | Timing Reference High Resolution Signal (Camshaft to Crankshaft angle) B No Pulses |
| 00380 | P0380 | Glow Plug/Heater Circuit "A" Malfunction |
| 00381 | P0381 | Glow Plug/Heater Indicator Circuit Malfunction |
| 00382 | P0382 | Glow Plug/Heater Circuit "B" Malfunction |
| 00385 | P0385 | Crankshaft Position Sensor B Circuit Malfunction |
| 00386 | P0386 | Crankshaft Position Sensor B Circuit Range/Performance |
| 00387 | P0387 | Crankshaft Position Sensor B Circuit Low Input |
| 00388 | P0388 | Crankshaft Position Sensor B Circuit High Input |
| 00389 | P0389 | Crankshaft Position Sensor B Circuit Intermittent |
| 00400 | P0400 | Exhaust Gas Recirculation Flow Malfunction |
| 00401 | P0401 | Exhaust Gas Recirculation Flow Insufficient Detected |
| 00402 | P0402 | Exhaust Gas Recirculation Flow Excessive Detected |
| 00403 | P0403 | Exhaust Gas Recirculation Circuit Malfunction |
| 00404 | P0404 | Exhaust Gas Recirculation Circuit Range/Performance |
| 00405 | P0405 | Exhaust Gas Recirculation Sensor A Circuit Low |
| 00406 | P0406 | Exhaust Gas Recirculation Sensor A Circuit High |
| 00407 | P0407 | Exhaust Gas Recirculation Sensor B Circuit Low |
| 00408 | P0408 | Exhaust Gas Recirculation Sensor B Circuit High |

| OB15 | MB | Description |
| --- | --- | --- |
| 00410 | P0410 | Secondary Air Injection System Malfunction |
| 00411 | P0411 | Secondary Air Injection System Incorrect Flow Detected |
| 00412 | P0412 | Secondary Air Injection System Switching Valve A Circuit Malfunction |
| 00413 | P0413 | Secondary Air Injection System Switching Valve A Circuit Open |
| 00414 | P0414 | Secondary Air Injection System Switching Valve A Circuit Shorted |
| 00415 | P0415 | Secondary Air Injection System Switching Valve B Circuit Malfunction |
| 00416 | P0416 | Secondary Air Injection System Switching Valve B Circuit Open |
| 00417 | P0417 | Secondary Air Injection System Switching Valve B Circuit Shorted |
| 00418 | P0418 | Secondary Air Injection System Relay "A" circuit Malfunction |
| 00419 | P0419 | Secondary Air Injection System Relay "B”” Circuit Malfunction |
| 00420 | P0420 | Catalyst System Efficiency Below Threshold (Bank 1) |
| 00421 | P0421 | Warm Up Catalyst Efficiency Below Threshold (Bank 1) |
| 00422 | P0422 | Main Catalyst Efficiency Below Threshold (Bank 1) |
| 00423 | P0423 | Heated Catalyst Efficiency Below Threshold (Bank l) |
| 00424 | P0424 | Heated Catalyst Temperature Below Threshold (Bank 1) |
| 00430 | P0430 | Catalyst System Efficiency Below Threshold (Bank 2) |
| 00431 | P0431 | Warm Up Catalyst Efficiency Below Threshold (Bank 2) |
| 00432 | P0432 | Main Catalyst Efficiency Below Threshold (Bank 2) |
| 00433 | P0433 | Heated Catalyst Efficiency Below Threshold (Bank 2) |
| 00434 | P0434 | Heated Catalyst Tern--re Below Threshold (Bank 2) |
| 00440 | P0440 | Evaporative Emission Control System Malfunction |
| 00441 | P0441 | Evaporative Emission Control System Incorrect Purge flow |
| 00442 | P0442 | Evaporative Emission Control System leak Detected (small leak) |
| 00443 | P0443 | Evaporative Emission Control System Purge Control Valve Circuit Malfunction |
| 00444 | P0444 | Evaporative Emission Control System Purge Control Valve Circuit Open |
| 00445 | P0445 | Evaporative Emission Control System Purge Control Valve Circuit Shorted |
| 00446 | P0446 | Evaporative Emission Control System Vent Control Circuit Malfunction |
| 00447 | P0447 | Evaporative Emission Control System Vent Control Circuit Open |
| 00448 | P0448 | Evaporative Emission Control System Vent Control Circuit Shorted |
| 00449 | P0449 | Evaporative Emission Control System Vent Valve/Solenoid Circuit Malfunction |
| 00450 | P0450 | Evaporative Emission Control System Pressure Sensor Malfunction |
| 00451 | P0451 | Evaporative Emission Control System Pressure Sensor Range/Performance |
| 00452 | P0452 | Evaporative Emission Control System Pressure Sensor Low Input |
| 00453 | P0453 | Evaporative Emission Control System Pressure Sensor High Input |
| 00454 | P0454 | Evaporative Emission Control System Pressure Sensor Intermittent |
| 00455 | P0455 | Evaporative Emission Control System Tank Leak Detected (large leak) Gas |

| OB15 | MB | Description |
| --- | --- | --- |
|  |  | Cap Off |
| 00460 | P0460 | Fuel Level Sensor Circuit Malfunction |
| 00461 | P0461 | Fuel Level Sensor Circuit Range/Performance |
| 00462 | P0462 | Fuel level Sensor Circuit Low Input |
| 00463 | P0463 | Fuel level Sensor Circuit High Input |
| 00464 | P0464 | Fuel level Sensor Circuit Intermittent |
| 00465 | P0465 | Purge Flow Sensor Circuit Malfunction |
| 00466 | P0466 | Purge flow Sensor Circuit Range/Performance |
| 00467 | P0467 | Purge Flow Sensor Circuit Low Input |
| 00468 | P0468 | Purge flow Sensor Circuit High Input |
| 00469 | P0469 | Purge flow Sensor Circuit Intermittent |
| 00470 | P0470 | Exhaust Pressure Sensor Malfunction |
| 00471 | P0471 | Exhaust Pressure Sensor Range/Performance |
| 00472 | P0472 | Exhaust Pressure Sensor Low |
| 00473 | P0473 | Exhaust Pressure Sensor High |
| 00474 | P0474 | Exhaust Pressure Sensor Intermittent |
| 00475 | P0475 | Exhaust Pressure Control Valve Malfunction |
| 00476 | P0476 | Exhaust Pressure Control Valve Range/Performance |
| 00477 | P0477 | Exhaust Pressure Control Valve Low |
| 00478 | P0478 | Exhaust Pressure Control Valve High |
| 00479 | P0479 | Exhaust Pressure Control Valve Intermittent |
| 00480 | P0480 | Cooling Fan 1 Control Circuit Malfunction |
| 00481 | P0481 | Cooling Fan 2 Control Circuit Malfunction |
| 00482 | P0482 | Cooling Fan 3 Control Circuit Malfunction |
| 00483 | P0483 | Cooling Fan Rationality Check Malfunction |
| 00484 | P0484 | Cooling Fan Circuit Over Current |
| 00485 | P0485 | Cooling Fan Power/Ground Circuit Malfunction |
| 00500 | P0500 | Vehicle Speed Sensor Malfunction |
| 00501 | P0501 | Vehicle Speed Sensor Range/Performance |
| 00502 | P0502 | Vehicle Speed Sensor Circuit Low Input |
| 00503 | P0503 | Vehicle Speed Sensor Intermittent/Erratic/High |
| 00505 | P0505 | Idle Control System Malfunction |
| 00506 | P0506 | Idle Control System RPM Lower Than Expected |
| 00507 | P0507 | Idle Control System RPM Higher Than Expected |
| 00510 | P0510 | Closed Throttle Position Switch Malfunction |
| 00520 | P0520 | Engine Oil Pressure Sensor/Switch Circuit Malfunction |
| 00521 | P0521 | Engine Oil Pressure Sensor/Switch Range/Performance |

| OB15 | MB | Description |
| --- | --- | --- |
| 00522 | P0522 | Engine Oil Pressure Sensor/Switch Low Voltage |
| 00523 | P0523 | Engine Oil Pressure Sensor/Switch High Voltage |
| 00530 | P0530 | A/C Refrigerant Pressure Sensor Circuit Malfunction |
| 00531 | P0531 | A/C Refrigerant Pressure Sensor Circuit Range/Performance |
| 00532 | P0532 | A/C Refrigerant Pressure Sensor Circuit Low Input |
| 00533 | P0533 | A/C Refrigerant pressure Sensor Circuit High Input |
| 00534 | P0534 | Air Conditioner Refrigerant Charge Loss |
| 00550 | P0550 | Power Steering Pressure Sensor Circuit Malfunction |
| 00551 | P0551 | Power Steering Pressure Sensor Circuit Range/Performance |
| 00552 | P0552 | Power Steering Pressure Sensor Circuit Low Input |
| 00553 | P0553 | Power Steering Pressure Sensor Circuit High Input |
| 00554 | P0554 | Power Steering Pressure sensor Circuit Intermittent |
| 00560 | P0560 | System Voltage Malfunction |
| 00561 | P0561 | System Voltage Unstable |
| 00562 | P0562 | System Voltage Low |
| 00563 | P0563 | System Voltage High |
| 00565 | P0565 | Cruise Control On Signal Malfunction |
| 00566 | P0566 | Cruise Control Off Signal Malfunction |
| 00567 | P0567 | Cruise Control Resume Signal Malfunction |
| 00568 | P0568 | Cruise Control Set Signal Malfunction |
| 00569 | P0569 | Cruise Control Coast Signal Malfunction |
| 00570 | P0570 | Cruise Control Accelerator Signal Malfunction |
| 00571 | P0571 | Cruise Control/Brake Switch A Circuit Malfunction |
| 00572 | P0572 | Cruise Control/Brake Switch A Circuit Low |
| 00573 | P0573 | Cruise Control/Brake Switch A Circuit High |
| 00574 | P0574 | through 10580 Reserved for Cruise Codes |
| 00600 | P0600 | CAN Serial Communication Link Malfunction to ESP |
| 00601 | P0601 | Internal Control Module Memory Check Sum Error |
| 00602 | P0602 | Internal Control Module Programming Error |
| 00603 | P0603 | Internal Control Module Keep Alive Memory (KAM) Error |
| 00604 | P0604 | Internal Control Module Random Access Memory (RAM) Error |
| 00605 | P0605 | Internal Control Module Read Only Memory (ROM) Error (Module Identification Defined by SAE J1979) |
| 00606 | P0606 | PCM Processor Fault |
| 00608 | P0608 | Control Module VSS Output "A" Malfunction |
| 00609 | P0609 | Control Module VSS Output "B" Malfunction |
| 00620 | P0620 | Generator Control Circuit Malfunction |

| OB15 | MB | Description |
| --- | --- | --- |
| 00621 | P0621 | Generator Lamp "L" Control Circuit Malfunction |
| 00622 | P0622 | Generator Field "F" Control Circuit Malfunction |
| 00650 | P0650 | Malfunction Indicator Lamp (MIL) Control Circuit Malfunction |
| 00654 | P0654 | Engine RPM Output Circuit Malfunction |
| 00655 | P0655 | Engine Hot Lamp Output Control Circuit Malfunction |
| 00656 | P0656 | Fuel Level Output Circuit Malfunction |
| 00700 | P0700 | Transmission Control System Malfunction |
| 00701 | P0701 | Transmission Control System Range/Performance |
| 00702 | P0702 | Transmission Control System Electrical |
| 00703 | P0703 | Torque Converter/Brake Switch B Circuit Malfunction |
| 00704 | P0704 | Clutch Switch Input Circuit Malfunction |
| 00705 | P0705 | Transmission Range Sensor Circuit Malfunction (PRNDL Input) |
| 00706 | P0706 | Transmission Range Sensor Circuit Range/Performance |
| 00707 | P0707 | Transmission Range Sensor Circuit Low Input |
| 00708 | P0708 | Transmission Range Sensor Circuit High Input |
| 00709 | P0709 | Transmission Range Sensor Circuit Intermittent |
| 00710 | P0710 | Transmission Fluid Temperature Sensor Circuit Malfunction |
| 00711 | P0711 | Transmission Fluid Temperature Sensor Circuit Range/Performance |
| 00712 | P0712 | Transmission Fluid Temperature Sensor Circuit Low Input |
| 00713 | P0713 | Transmission Fluid Temperature Sensor Circuit High Input |
| 00714 | P0714 | Transmission Fluid Temperature Sensor Circuit Intermittent |
| 00715 | P0715 | Input/Turbine Speed Sensor Circuit Malfunction |
| 00716 | P0716 | Input/Turbine Speed Sensor Circuit Range/Performance |
| 00717 | P0717 | Input/Turbine Speed Sensor Circuit No Signal |
| 00718 | P0718 | Input/Turbine Speed Sensor Circuit Intermittent |
| 00719 | P0719 | Torque Converter/Brake Switch B Circuit Low |
| 00720 | P0720 | Output Speed Sensor Circuit Malfunction |
| 00721 | P0721 | Output Speed Sensor Circuit Range/Performance |
| 00722 | P0722 | Output Speed Sensor Circuit No Signal |
| 00723 | P0723 | Output Speed Sensor Circuit Intermittent |
| 00724 | P0724 | Torque Converter/Brake Switch B Circuit High |
| 00725 | P0725 | Engine Speed Input Circuit Malfunction |
| 00726 | P0726 | Engine Speed Input Circuit Range/Performance |
| 00727 | P0727 | Engine Speed Input Circuit No Signal |
| 00728 | P0728 | Engine Speed Input Circuit Intermittent |
| 00730 | P0730 | Incorrect Gear Ratio |
| 00731 | P0731 | Gear 1 Incorrect Ratio |

| OB15 | MB | Description |
| --- | --- | --- |
| 00732 | P0732 | Gear 2 Incorrect Ratio |
| 00733 | P0733 | Gear 3 Incorrect Ratio |
| 00734 | P0734 | Gear 4 Incorrect Ratio |
| 00735 | P0735 | Gear 5 Incorrect Ratio |
| 00736 | P0736 | Reverse Incorrect Ratio |
| 00740 | P0740 | Torque Converter Clutch Circuit Malfunction |
| 00741 | P0741 | Torque Converter Clutch Circuit Performance or Stuck Off |
| 00742 | P0742 | Torque Converter Clutch Circuit Stuck On |
| 00743 | P0743 | Torque Converter Clutch Circuit Electrical |
| 00744 | P0744 | Torque Converter Clutch Circuit Intermittent |
| 00745 | P0745 | Pressure Control Solenoid Malfunction |
| 00746 | P0746 | Pressure Control Solenoid Performance or Stuck Off |
| 00747 | P0747 | Pressure Control Solenoid Stuck On |
| 00748 | P0748 | Pressure Control Solenoid Electrical |
| 00749 | P0749 | Pressure Control Solenoid Intermittent |
| 00750 | P0750 | Shift Solenoid A Malfunction |
| 00751 | P0751 | Shift Solenoid A Performance or Stuck Off |
| 00752 | P0752 | Shift Solenoid A Stuck On |
| 00753 | P0753 | Shift Solenoid A Electrical |
| 00754 | P0754 | Shift Solenoid A Intermittent |
| 00755 | P0755 | Shift Solenoid B Malfunction |
| 00756 | P0756 | Shift Solenoid B Performance or Stuck Off |
| 00757 | P0757 | Shift Solenoid B Stuck On |
| 00758 | P0758 | Shift Solenoid B Electrical |
| 00759 | P0759 | Shift Solenoid B Intermittent |
| 00760 | P0760 | Shift Solenoid C Malfunction |
| 00761 | P0761 | Shift Solenoid C Performance or Stuck Off |
| 00762 | P0762 | Shift Solenoid C Stuck On |
| 00763 | P0763 | Shift Solenoid C Electrical |
| 00764 | P0764 | Shift Solenoid C Intermittent |
| 00765 | P0765 | Shift Solenoid D Malfunction |
| 00766 | P0766 | Shift Solenoid D Performance or Stuck Off |
| 00767 | P0767 | Shift Solenoid D Stuck On |
| 00768 | P0768 | Shift Solenoid D Electrical |
| 00769 | P0769 | Shift Solenoid D Intermittent |
| 00770 | P0770 | Shift Solenoid E Malfunction |
| 00771 | P0771 | Shift Solenoid E Performance or Stuck Off |

| OB15 | MB | Description |
| --- | --- | --- |
| 00772 | P0772 | Shift Solenoid E Stuck On |
| 00773 | P0773 | Shift Solenoid E Electrical |
| 00774 | P0774 | Shift Solenoid E Intermittent |
| 00780 | P0780 | Shift Malfunction |
| 00781 | P0781 | 1-2 Shift Malfunction |
| 00782 | P0782 | 2-3 Shift Malfunction |
| 00783 | P0783 | 3-4 Shift Malfunction |
| 00784 | P0784 | 4-5 Shift Malfunction |
| 00785 | P0785 | Shift/Timing Solenoid Malfunction |
| 00786 | P0786 | Shift/Timing Solenoid Range/Performance |
| 00787 | P0787 | Shift/Timing Solenoid low |
| 00788 | P0788 | Shift/Timing Solenoid High |
| 00789 | P0789 | Shift/Timing Solenoid Intermittent |
| 00790 | P0790 | Normal/Performance Switch Circuit Malfunction |
| 00801 | P0801 | Reverse Inhibit Control Circuit Malfunction |
| 00802 | P0802 | Resonance intake manifold switch valve circuit |
| 00803 | P0803 | 1-4 Upshift (Skip Shift) Solenoid Control Circuit Malfunction |
| 00804 | P0804 | 1-4 Upshift (Skip Shift) Lamp Control Circuit Malfunction |
| 00805 | P0805 | Air-flap recirculation signal output stage incorrect |
| 00806 | P0806 | A/C compressor output stage, magnetic combination |
| 00809 | P0809 | Variation in angle of camshaft to crankshaft incorrect |
| 00811 | P0811 | CAN problem No reception from EZS (Ignition Lock) |
| 00816 | P0816 | Oil pressure sensor open circuit or short circuit, malfunction |
| 01031 | P1031 | O2 sensor (G3/3 and G3/4) connections reversed |
| 01146 | P1146 | Mass air flow circuit malfunction - Bank 2 (left) |
| 01147 | P1147 | ECT circuit malfunction - Bank 2 (left) |
| 01148 | P1148 | IAT circuit malfunction - Bank 2 (left) |
| 01149 | P1149 | MAP circuit malfunction - Bank 2 (left) |
| 01162 | P1162 | Throttle position sensor circuit failure - Bank 2 (left) |
| 01163 | P1163 | Oil level switch. |
| 01176 | P1176 | Oil pressure sensor open circuit or short circuit, malfunction. |
| 01177 | P1177 | Oil sensor, temperature incorrect. |
| 01178 | P1178 | Oil sensor, engine oil level incorrect. |
| 01179 | P1179 | Oil sensor, engine oil quality incorrect. |
| 01180 | P1180 | Oil sensor, engine oil temperature too high |
| 01181 | P1181 | Engine electric-fan /Air conditioning malfunction |
| 01182 | P1182 | Starting system relay in fuse and relay module box |

| OB15 | MB | Description |
| --- | --- | --- |
| 01183 | P1183 | Right cylinders bank cut-off output stage malfunction |
| 01184 | P1184 | Left cylinders bank cut-off output stage malfunction |
| 01185 | P1185 | Water in engine oil, Oil sensor |
| 01186 | P1186 | Fuel safety shut-off recognized. |
| 01225 | P1225 | Resonance intake manifold switchover valve circuit |
| 01235 | P1235 | Air-flap recirculated signal output stage faulty |
| 01236 | P1236 | A/C compressor output stage, magnetic combination incorrect |
| 01300 | P1300 | CKP sensor circuit failure - Bank 2 (left) |
| 01384 | P1384 | Knock sensor circuit malfunction - Left front. |
| 01385 | P1385 | Knock sensor circuit malfunction - Left rear. |
| 01386 | P1386 | Knock sensor control from electronic control module - at limit |
| 01397 | P1397 | CMP sensor circuit range/performance - Bank 2 (left) |
| 01400 | P1400 | EGR (exhaust gas recirculation) output stage faulty |
| 01420 | P1420 | Air-pump switchover valve circuit |
| 01443 | P1443 | EVAP system malfunction - Bank 2 (left) |
| 01453 | P1453 | Air-pump relay, relay module, fuse or circuit |
| 01463 | P1463 | Left AIR system malfunction |
| 01490 | P1490 | EVAP system purge control valve circuit malfunction - Bank 2 (left) |
| 01491 | P1491 | A/C system refrigerant pressure too high |
| 01492 | P1492 | Exhaust-flap faulty |
| 01519 | P1519 | Right or sole adjustable camshaft timing solenoid mechanically faulty. |
| 01522 | P1522 | Left adjustable camshaft timing solenoid mechanically faulty. |
| 01525 | P1525 | Right or sole adjustable camshaft timing solenoid electrically faulty |
| 01533 | P1533 | Left adjustable camshaft timing solenoid electrically faulty |
| 01542 | P1542 | Pedal position sensor signal |
| 01570 | P1570 | CAN bus signal from DAS to the ME-SFI control unit - DAS locked, signal interrupted, mismatched ECMs. |
| 01580 | P1580 | Right or sole EA/CC/ISC Actuator circuit faulty |
| 01581 | P1581 | Left EA/CC/ISC Actuator circuit faulty |
| 01584 | P1584 | Stop lamp switch/Brake switch signal |
| 01587 | P1587 | Left engine control module voltage supply faulty. |
| 01588 | P1588 | CAN bus signal from the RCL controller to the Left engine controller faulty. |
| 01589 | P1589 | Knock sensor control from the left engine controller at limit. |
| 01603 | P1603 | CAN bus problem. No data reception from EIS |
| 01605 | P1605 | CAN fault. ABS speed sensor error vs. VSS (RPM) |
| 01632 | P1632 | Left engine control module faulty. |
| 01641 | P1641 | Right of left CTP signal to the engine control module faulty or CAN bus communication by the left engine control has been interrupted. |

| OB15 | MB | Description |
| --- | --- | --- |
| 01642 | P1642 | Engine control module incorrect coding (MT coded has AT) |
| 01643 | P1643 | Engine control module incorrect coding or CAN signal from Transmission system faulty. |
| 01644 | P1644 | Transmission control module, voltage too low. Transmission control system version cannot be checked. |
| 01747 | P1747 | CAN signal from ETC. CAN signal failure from ETC or instrument cluster faulty. |

Operating the CS1000 - Mercedes Benz

OB15-12 Memory Cartridge - Mercedes Benz Analog & Digital Fault Codes

Setting Up

ATTENTION: DO NOT INSERT CARTRIDGE WITH POWER SUPPLIED TO THE CS1000.

PROPER USE OF THE MERCEDES DIAGNOSTIC SYSTEM

�	Identify vehicle Model and Month/Year of production

�	Confirm specific drivability complaint. If MIL is on, when did it come on and under what conditions?

Insert the OB15-12 memory cartridge into the base of the scanner. Make sure the arrow on the cartridge is facing up as it is inserted. Gently push the cartridge into the CS1000 until the cartridge seats completely.

�   Refer to Diagnostic Cable introduction page 9 and connection table page 10 of this manual to determine vehicle cable requirements. Connect the cable specified to the scanner and to the vehicle Diagnostic Connector.

+	Connect the 25-pin cable connector head firmly to the scanner 25-pin connection port.

+	Connect the Red test lead from the scanner to the power supply socket (B+) on the Diagnostic Connector, where available, or to the vehicle's battery via the extension cable and battery clamp supplied.

+	Connect the Black test lead from the scanner to the ground socket on the Diagnostic Connector. Now the scanner powered up and the power indicator light should be fully illuminated. The screen will display F 1.

Note:

Power indicator light (LED) must light up. If it does not, refer to the list below for detailed test.

Refer to the connection table of this manual; check the Red and Black test lead with the socket number on the Diagnostic Connector, Is there an incorrect or weak connection?

Check the power requirement on the Diagnostic Connector. (Must be performed with the ignition ON when connected with 16-pole diagnostic connector at socket 16)

Connect the Yellow test lead to the system diagnostic socket that you use to extract codes.

Refer to this manual or Mercedes Benz maintenance manual for location of the Diagnostic sockets for the type of Diagnostic Connector fitted to the vehicle and the system capabilities available for code access on the applicable Diagnostic sockets.

Turn Ignition ON (KOEO) or Engine at idle (KOER)

System Selection

F	1	Analog type Transmission Systems (impulse fault code type)

Models 129, 140 with CFI, LH-SFI control systems 1990  - 1993

F	2	Digital type Transmission Systems as follows:

Models 202, 210, 129, 140 with HFM-SFI, ME-SFI control system 1994 - 1997

Press the SYSTEM key to scroll to display from F 1 to F 2 system.

SYSTEM

ANALOG TEST PROCEDURES

Ignition in the KOEO position (Key On Engine Off).

Choose system F1.

Place test probe (yellow) in pin-out for specific analog test.

DIGITAL TEST PROCEDURE

Ignition in the KOEO position (Key On Engine Off)

Choose system F2.

Place test probe (yellow) in pin-out for Digital test.

If any system does not respond, test it using the Analog Test Procedure.

*Some early LH Injection and Diagnostic Module systems may not respond to the digital test.

Read Fault Codes

Press the READ key to begin to read the fault codes for the system selected. The scanner will scan all of the fault codes and keep them in memory.

When reading Digital Fault Codes the scanner will display a U 1 or a U 2 indicating the type of digital system it has discovered. Refer to the U codes displayed on the top of the code pages to identify the system.

READ

Press the NEXT key to scroll through the fault codes C	xx . The display will cycle to the first code after the last code is displayed. When there are no faults in the system, C	0 will be displayed on the screen.

NEXT

Identification/Rectification of Faults

Identify fault  code and related circuit  using this manual  or using the factory  diagnostic manuals

available from Baum Tools Technical Publications 415-566-9229.

Carry out required repair before clearing fault codes.

Clearing Fault Codes

After repairs have been carried out reread the codes. After rereading the codes press the CLEAR key to erase all of the fault codes from the control unit memory. When there are no faults in the system, either C

1 (Impulse or analog systems) or C 2 (digital systems) will be displayed on the screen.

CLEAR

Return to System Select Function

Press the SYSTEM key to scroll through the system selections.

SYSTEM

YMYroe l:Ynr.L CoDE2

YYYYnnnnJJJJoooowwwwsssJJJJ!!!!cccc----ssssuuuuaassaassqq

l:l:l:l:oooonnnnLLLL----MM

l'l'ss

ssssllll

DDDDLLLL!!!!AAAAssss

((((����WWWWYYYY.l.l

llllCC

))))

F	1

| Models | Model Years |
| --- | --- |
| 124.230 124.290 | 1990-93 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 8-pin |
| --- | --- |
| Yellow | Socket 5 |
| Black | Socket 1 |
| Red | Battery (+) |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | 4MATIC control module |
| 3 | Brake light switch |
| 4 | Left front axle vehicle speed sensor |
| 5 | Right front axle vehicle speed sensor |
| 6 | Rear speed sensor signal |
| 7 | All 3 vehicle speed sensors |
| 8 | Over volts protection relay, front axle train valve |
| 9 | Over volts protection relay, central differential lock valve |
| 10 | Over volts protection relay, stop lamp switch, Rear axle differential lock valve |
| 11 | Steering angle sensor signal |

EEEEllll&&&&ccccJJJJLLLLoooouu

!!cccc

YYYYnnnnJJJJoooowwwwssssJJJJ!!!!cccc

.1.1.1.1LLLLssssuuuu2222wwww!!

222222

!!oooouuuu

CCCCoooouuuuJJJJLLLLoooollll

2222----2222bbbb&&&&&&&&qqqq

((((EEEE.L.L.L.LCCCC))))

MMMM!!!! ••••

CCCCl:l:l:l:llll

F	1

| Models | Model Years |
| --- | --- |
| 129 | 1990-93 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 16-pin |
| --- | --- |
| Yellow | Socket 13 |
| Black | Socket 1 |
| Red | Socket 16 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Not used |
| 3 | Engine load signal interrupted |
| 4 | Throttle valve position switch (potentiometer) interrupted |
| 5 | Engine speed signal (RPM) interrupted |
| 6 | Vehicle speed sensor interrupted |
| 7 | Output fault in TCM (N15/1) or fault in the valve block control valve circuit (Y3/1y2) |
| 8 | Transmission control module (TCM) (N15/1) |
| 9 | Valve control valve block (Y3/1y2) |
| 10 | Valve control valve block (Y3/1y2), short circuit |

EEEEllll&&&&ccccJJJJLLLLoooouu

!!cccc

YYYYnnnnJJJJoooowwwwssssJJJJ!!!!cccc

.1.1.1.1LLLLssssuuuu2222wwww!!

222222

!!oooouuuu

CCCCoooouuuuJJJJLLLLoooollll

2222----2222bbbb&&&&&&&&qqqq

((((EEEE.L.L.L.LCCCC))))

MMMM!!!! ••••

rrrrHHHH----22221:1:1:1:1111

F	1

| Models | Model Years |
| --- | --- |
| 129 140 | 1990-93 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 10 |
| Black | Socket 1 |
| Red | Socket 3 |

FAULT CODE TABLE

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Engine control module (N3/4) does not match TCM |
| 3 | Transmission overload protection switch 4th/5th gear defective |
| 4 | CAN data line from EA/CC/ISC control module (N4/1) signal distorted |
| 5 | CAN data line from DI control module (N1/3) or HFM control module signal distorted |
| 6 | CAN data line signal distorted |
| 7 | Valve control valve block (Y3/1y2), open circuit or TCM (N15/1) defective |
| 8 | Automatic Transmission Control Module (TCM) (N15/1) defective |
| 9 | Valve control valve block (Y3/1y2) |
| 10 | Valve control valve block (Y3/1y2), short circuit |

DIGITAL FAULT CODES

EEEEllll&&&&ccccllllLLLLoooouu

!!cccc

YYYYnnnnlllloooowwwwssssllll!!!!cccc

.1.1.1.1LLLLssssuuuu2222wwww!!

222222

!!oooouuuu

CCCCoooouuuullllLLLLoooollll

2222----2222bbbb&&&&&&&&qqqq

((((EEEE.L.L.L.LCCCC))))

MIJIJ ll\E-21:1

F 2

U 1

| Models | Engines | Model Years |
| --- | --- | --- |
| 129 | 140 | 163 | 170 | 202 | 208 | 210 | 104 | 111 | 112 | 113 | 119 | 120 | 606 | 1995-98 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 10 |
| Black | Socket 1 |
| Red | Socket 3 |

Fault Code Table

| DTC Readout | Possible cause of Failure |
| --- | --- |
| 1 | No fault stored |
| 2 | 1-2/4-5 shift solenoid valve circuit fault (Y3/6y3) |
| 3 | 2-3 shift solenoid valve circuit fault (Y3/6y5) |
| 4 | 3-4 shift solenoid valve circuit fault (Y3/6y4) |
| 5 | PWM solenoid valve (torque converter lock-up) circuit fault (Y3/6y6) |
| 6 | Pressure regulating solenoid valve circuit fault (Y3/6y1) |
| 7 | Shift pressure regulating solenoid valve circuit fault (Y3/6y2) |
| 8 | R/P lock solenoid, function defective (Y66/1) |
| 9 | Cable to starter lock-out relay module, function defective (K38/3) |
| 10 | Voltage supply to solenoid valves |
| 11 | Voltage supply to RPM sensors |

| DTC Readout | Possible cause of Failure |
| --- | --- |
| 12 | RPM sensor 2 (Y3/6n2), signal defective |
| 13 | RPM sensor 3 (Y3/6n3), signal defective |
| 16 | Transmission output sensor (B49) defective |
| 17 | Transmission selector lever coding invalid |
| 18 | Selector lever signal incorrect (This code can be ignored.) or between ranges |
| 19 | Transmission fluid temperature sensor (Y3/6b1) signal defective |
| 20 | Starter lock-out contact (Y3/6s1) not functioning |
| 20 | Transmission oil temperature sensor defective/Starter lock-out contact not functioning |
| 21 | Supply voltage (terminal 87) too low or overvoltage. |
| 22 | CAN data: Right rear wheel speed (VSS) from traction system incorrect/implausible |
| 23 | CAN data: Left rear wheel speed (VSS) from traction system incorrect/implausible |
| 24 | CAN data: Pedal value from ME-SFI controller incorrect/implausible |
| 24 | CAN data: Right front wheel speed (VSS) from traction system incorrect/implausible |
| 25 | CAN data: Engine RPM from ME-SFI controller system incorrect/implausible |
| 25 | CAN data: Left front wheel speed (VSS) from traction system incorrect/implausible |
| 26 | CAN data: Right engine torque from ME-SFI controller system incorrect/implausible |
| 26 | CAN data: Pedal value from ME-SFI controller incorrect/implausible |
| 27 | CAN data: Altitude adjustment factor from the ME-SFI controller incorrect/implausible (This fault code can be ignored if no relative faults stored in the ME-SFI |
| 27 | CAN data: Adjusted engine torque incorrect/implausible |
| 28 | CAN data: Left engine torque from ME-SFI controller system incorrect/implausible |
| 28 | CAN data: Engine RPM from ME-SFI controller system incorrect/implausible |
| 29 | CAN data: Right engine torque from ME-SFI controller system incorrect/implausible |
| 30 | CAN data: Communication with traction system faulty |
| 30 | CAN data: Altitude adjustment factor from the ME-SFI controller incorrect/implausible (This fault code can be ignored if no relative faults stored in the ME-SFI |
| 31 | CAN data: Communication to the ME-SFI controller is faulty |
| 31 | CAN data: Maximum induced engine torque from ME-SFI controller incorrect/implausible |
| 32 | CAN data: Communication to/from the ME-SFI controller is faulty |

| DTC Readout | Possible cause of Failure |
| --- | --- |
| 32 | CAN data: Left engine torque from ME-SFI controller system incorrect/implausible |
| 33 | CAN data: Communication to/from the ME-SFI controller is faulty |
| 33 | CAN data: Throttle valve actuator actual value from ME-SFI incorrect/implausible |
| 34 | CAN data: Communication to/from the ME-SFI controller is faulty |
| 35 | CAN data: Communication to/from the ME-SFI controller is faulty |
| 36 | CAN data: Communication to/from the ME-SFI controller is faulty or the engine temperature is implausible. |
| 37 | CAN data: All communications are faulty |
| 38 | CAN data: Communication to/from the Traction system controller is faulty |
| 39 | CAN data: Communication to/from the ME-SFI controller is faulty |
| 40 | CAN data: Communication to/from the Instrument Cluster is faulty |
| 50 | Speed sensor n3 or clutch K1 are faulty |
| 51 | Gear implausible or transmission slips. |
| 52 | Command valve (6, 14, or 25) sticking under pressure. |
| 52 | Unauthorized locking of Torque Converter lock-up clutch. Replace Torque Converter. |
| 53 | Torque converter lock-up clutch, not functioning. Replace Torque Converter. |
| 53 | Torque converter lock-up clutch, input (RPM) too high. Replace Torque Converter. |
| 54 | No feedback signal from transmission overload protection. |
| 55 | Gear comparison incorrect or target gear selection not achieved. |
| 56-65 | Transmission control unit (N15/3) faulty . |
| 98-155 | These codes are intermittent. To establish their meaning, subtract 96 from the code number given and look in the table above for the definition of the intermittent fault. |

E 2

U 2

EEEEllll&&&&ccccllllLLLLoooouu

!!cccc

YYYYnnnnlllloooowwwwssssllll!!!!cccc

.1.1.1.1LLLLssssuuuu2222wwww!!

222222

!!oooouuuu

CCCCoooouuuullllLLLLoooollll

2222----2222bbbb&&&&&&&&qqqq

(E.lC)

| Models | Model Years |
| --- | --- |
| 129 140 | 1993-96 |

Connect wires of Scanner as follows

| Scanner | Data Link Connector 38-pin |
| --- | --- |
| Yellow | Socket 10 |
| Black | Socket 1 |
| Red | Socket 3 |

Fault Code Table

| DTC Readout | Possible Cause of Failure |
| --- | --- |
| 1 | No fault found |
| 2 | Engine control module (N3/4) does not match TCM |
| 3 | Transmission overload protection switch 4th/5th gear defective |
| 4 | CAN data line from EA/CC/ISC control module (N4/1) signal distorted |
| 5 | CAN data line from DI control module (N1/3) or HFM control module signal distorted |
| 6 | CAN data line signal distorted |
| 7 | Valve control valve block (Y3/1y2), open circuit or TCM (N15/1) defective |
| 8 | Automatic Transmission Control Module (TCM) (N15/1) defective |
| 9 | Valve control valve block (Y3/1y2) |
| 10 | Valve control valve block (Y3/1y2), short circuit |

ACRONYM	DESCRIPTION

4MATIC	4 Wheel Drive Transmission Control A/C (Automatic)*	Air Conditioning (Automatic)

A/C (Tempmatic)*	Air Conditioning (Tempmatic)

AB	Supplemental Restraint System (Airbag)

ABS	Anti-lock Brake System

ADM	Automatic Dimming Inside Rearview Mirror

ADS	Automatic Damping System (Suspension)

AIR	Secondary Air Injection

AP	Accelerator Pedal

AS	Antenna System

ASD	Automatic Locking Differential

ASR	Acceleration Slip Regulation

AT	Automatic Transmission

ATA*	Anti-theft Alarm System

BA	Backup Assist

BARO	Barometric Pressure

BCAPC	Barometric Pressure-charge Air Pressure Compensation

BM*	Base Module (Master ECU Controller)

BPC	Barometric Pressure Compensation

CA	Closing Assist

CAN	Controller Area Network

CC*	Cruise Control (Tempomat)

CDC	Cd Changer

CF	Convenience Feature

CFI	Continuous Fuel Injection

CKA	Crank Angle

CKP	Crankshaft Position

CL	Central Locking

CLUS	Instrument Cluster

CMP	Camshaft Position

CST*	Cabriolet Soft Top

CTEL	Cellular Telephone

CTP	Closed Throttle Position (Idle)

DFI*	Electronic Distributor-type Fuel Injection

DI*	Distributor Ignition System

DM (USA)	Diagnostic Module (Emissions)

DTC	Diagnostic Trouble Code

EA*	Electronic Accelerator

EAG	Electronic Automatic Transmission Control

EATC*	Electronic Automatic Transmission Control

ECL	Engine Coolant Level

ECT	Engine Coolant Temperature

EDC	Electronic Diesel Control

EDR	Electronic Diesel Regulation

EDS	Electronic Diesel System

EDW*	Anti-theft Alarm System

EFP*	Electronic Accelerator

EGR	Exhaust Gas Recirculation

EGS	Electronic Transmission Control

EIFI	Electronic In-line Fuel Injection

EMSC	Electric Mirror, Steering Column Adjustment, Heated Mirrors

ERE*	Electronic In-line Fuel System

ESA	Electric Seat Adjustment

ESC	Electric Steering Column Adjustment

ESCM	Engine System Control Module

ESP	Electronic Stability Program

ETC	Electronic Transmission Control

ETR	Emergency Tensioning Retractor

ETS	Electronic Traction System

EVAP	Evaporative Emission Control System

EVE	Electronic Distributor-type Fuel Injection

EZL	Distributor Ignition System

FAN	Fanfare Horns

FFS	Frame Floor System

FP	Fuel Pump

GM	Base Module (Master ECU Controller)

HAU	Automatic Heater

HCS	Headlamp Cleaning System

HEAT	Automatic Heater

HFM	Hot Film Engine Management

HFS	Hands Free System

HHT	Hand Held Tester

HORN	Horn Signal System

HS	Heated Seats

IAT	Intake Air Temperature

IC	Instrument Cluster

IDC	In Dash Controller

IFI*	Electronic In-line Fuel System(diesel)

IFZ	Infrared Remote Central Locking (IRCL)

IRCL*	Infrared Remote Central Locking

ISC*	Idle Speed Control

KE	Continuous Injection System (CIS)

KFB	Convenience Feature

KI	Instrument Cluster

KLA	Air Conditioning

KS	Knock Sensor

KSS	Knock Sensor System

LH-SFI	LH Sequential Fuel Management Bank 1 (1-6 Cylinders)

LH2-SFI	LH Sequential Fuel Management Bank 2 (7-12 Cylinders)

LLR	Cruise Control

LS	Loudspeaker System

MAF	Mass Air Flow

MAP	Manifold Absolute Pressure

ME	Motor Electronics

MIL	Malfunction Indicator Lamp (Check Engine)

MT	Manual Transmission

MVA	Manifold Vacuum Assist

O2S	Oxygen (O2) Sensor

OBD	On-board Diagnostics

OC	Oxidation Catalytic Convertor

OSB	Orthopedic Seat Backrest

PL	Power Lock

PML	Speed-sensitive Power Steering

PMP	Partial Intake Manifold Preheater

PNP	Park/neutral Position

PS	Power Steering

PSE	Pneumatic System Equipment

PTS	Parktronic System

RB*	Roll Bar Control

RD	Radio

REST	Residual Engine Heat Utilization

RHR	Retractable Rear Head Restraints

RHS	Rear Heated Seats

RPM	Revolutions per Minute (Engine Speed)

RST*	Roadster Soft Top

RTG	Retractable Trunk Lid Grip

RV	Roadster Soft Top

SBE	Seat Belt Extender

SLO	Starter Lock-out

SMS	Service Microfiche System

SPS	Speed-sensitive Power Steering

SRS	Supplemental Restraint System (Airbag)

STH	Stationary Heater

TB	Throttle Body

TC	Turbo Charger

TCM	Transmission Control Module

TD	Speed Signal (Time Division) (EZL)

TDC	Top Dead Center

TIC	Transistorized Ignition Control

TN	Speed Signal (EZL/AKR)

TRAP	Trap Oxidizer

TS	Towing Sensor

TVV	Tank Ventilation Valve

TWC	Three Way Catalytic Convertor

ÜRB	Roll Bar Control

VAF	Volume Air Flow

VSS	Vehicle Speed Signal

WOT	Wide Open Throttle (Full Load)

* USA Acronym only.

ll\EHCEDE2 BEMS - n2w ll\ODEr IDEM.lIl:IEH

| MODEL | YEARS | CHASSIS | ENGINE | TRANSMISSION | STEERING |
| --- | --- | --- | --- | --- | --- |
| 190C | 1961-65 | 110 | 121.924 | GA190C | LO 1 |
| 190D 2.2 | 1984-85 | 201.122 | 601.921 | 717.4/722.4 | LO75Z/68 |
| 190D 2.5 | 1986-89 | 201.126 | 602.911 | 717.4/722.4 | LS68 |
| 190D 2.5 TURBO | 1987- | 201.128 | 602.961 | 722.4 | LS68 |
| 190DC | 1961-65 | 110 | 621.912 | GA190DC | LO 1 |
| 190E 2.3 | 1982-86 | 201.024 | 102.961 K | 717.4/722.4 | LS68 |
| 190E 2.3 | 1982-86 | 201.024 | 102.985 KE | 717.4/722.4 | LS68 |
| 190E 2.3 | 1987-93 | 201.028 | 102.985 KE | 717.413/722.408 | 765.903 |
| 190E 2.3-16v | 1984-87 | 201.034 | 102.983 KE | 717.4/722.4 | 765.9 |
| 190E 2.5-16v | 1988-93 | 201E25 | 102.983 KE | 717.4/722.4 | 765.9 |
| 190E 2.6 | 1986-93 | 201.029 | 103.942 KE | 717.432/722.409 | 765.903 |
| 200 | 1965-68 | 110 | 121.940 | GA190C | LO 1 |
| 200CE | 1990-93 | 124.021 | 102 KE | 717.4/722.400 | 765.905 |
| 200D | 1965-68 | 110 | 621.918 | GA190DC | LO 1 |
| 200E | 1993 | 124.021 | 102.963 KE | 717.4/722.400 | 765.905 |
| 200TE | 1988-92 | 124.021 | 102. KE | 717.4/722.400 | 765.905 |
| 220 | 1967-72 | 115.010 | 115.920 | 722.1 | L1Z/LS75/765.706 |
| 220B | 1959-65 | 111 | 180.940 | GA220B | LO 1 |
| 220D | 1967-72 | 115.110 | 615.912 | 722.2 | L1Z/LS75/765.706 |
| 220SB | 1959-65 | 111 | 180.941 | GA220SB | LO 1 |
| 220SE Cabriolet | 1951-65 | 111.023 | 127.984 | GA220SEB | LO 1 |
| 220SE Coupe | 1959-65 | 111.021 | 127.984 | GA220SEB | LO 1 |
| 220SEB | 1959-65 | 111 | 127.982 | GA220SEB | LO 1 |
| 220SEB/C | 1951-65 | 111 | 127.984 | GA220SEB | LO 1 |
| 230 |  | 123.023 | 115.954 | 722.1 | 765.706 |
| 230 | 1965-66 | 110 | 180.945 | GA230 | LO 1 |
| 230 | 1967-72 | 114.015 | 180.954 | 722.2 | L1Z/LS75/765.706 |
| 230 | 1973-78 | 115.017 | 115.951 | 716/722.1 | L1Z/765.706 |
| 230S | 1965-68 | 111 | 180.945 | GA220B,SB | LO 1 |

| MODEL | YEARS | CHASSIS | ENGINE | TRANSMISSION | STEERING |
| --- | --- | --- | --- | --- | --- |
| 230SL | 1963-68 | 113.042 | 127.981 | GA230SL | LO 1 |
| 240D | 1973-75 | 115.117 | 616.916 | 716/722.1 | L1Z |
| 240D | 1976-85 | 123.123 | 616.912 | 716.0,.2/722.1 | L1Z/765.706 |
| 250 | 1967-69 | 114.010 | 114.920 | 722.2 | L1Z/LS75/765.706 |
| 250 | 1970-75 | 114.011 | 130.923 | 722.2 | L1Z/LS75/765.706 |
| 250C | 1969-75 | 114.023 | 130.923 | 722.2 | L1Z/LS75/765.706 |
| 250D | 1986-93 | 124.125 | 602.912 | 722.414 | 765.904 |
| 250S | 1963-68 | 108 | 108.920 | GA230SL | LO 1 |
| 250SE | 1965-68 | 108 | 129.980 | GA230SL | LO 1 |
| 250SE Cabriolet | 1965-68 | 111.023 | 129.980 | GA230SL | LO 1 |
| 250SE Coupe | 1965-68 | 111.021 | 129.980 | GA230SL | LO 1 |
| 250SL |  | 113.043 | 129.982 |  | LO 1 |
| 260E | 1985-88 | 124.026 | 103.940 KE | 717.4/722.4 | LSC068/O068 |
| 280 | 1972-76 | 114.060 | 110.921 | 722.1 | L1Z/LS75/765.706 |
| 280C | 1972-76 | 114.073 | 110.921 | 716/717/722.1 | L1Z/LS75/765.706 |
| 280CE | 1977-85 | 123.053 | 110.984 K | 716.0/722.1 | 765.706 |
| 280E | 1976-85 | 123.033 | 110.984 K | 716.0/722.1 | 765.706 |
| 280S | 1967-72 | 108.016 | 130.920 | 722.2 | L1K/LS75 |
| 280S | 1972-80 | 116.020 | 110.922 | 716/722.1 | 765.706 |
| 280SE | 1967-72 | 108.018 | 130.980 | 722.2 | L1K/LS75 |
| 280SE | 1972-80 | 116.024 | 110.985 | 716.0/722.1 | 765.706 |
| 280SE 3.5 Cabriolet |  | 111.025 | 116.980 |  | LO 1 |
| 280SE 3.5 Coupe |  | 111.024 | 116.980 |  | LO 1 |
| 280SE 4.5 | 1971-72 | 108.067 | 117.984 | 722.0 | LS75 |
| 280SE Cabriolet |  | 111.025 | 130.980 |  | LO 1 |
| 280SE Coupe |  | 111.024 | 130.980 |  | LO 1 |
| 280SEL |  | 108.019 | 130.980 | 722.2 | L1K/LS75 |
| 280SEL 4.5 | 1971-72 | 108.068 | 117.984 | 722.0 | LS75 |
| 280SL |  | 113.044 | 130.983 |  | LO 1 |
| 300CD | 1977-80 | 123.150 | 617.912 | 722.1 | 765.706 |
| 300CD Turbo | 1982-85 | 123.153 | 617.952 | 722.3/.4 | 765.706 |
| 300CE | 1987-89 | 124.050 | 103.983 KE | 717.4/722.3 | LS68 |
| 300CE | 1990-92 | 124.051 | 104.980 KE | 717.4/722.3 | LSH068/C068 |
| 300CE | 1993-96 | 124.052 | 104.992 HFM | 717.4/722.369 | 765.908 |
| 300CE Cabriolet | 1993-96 | 124.066 | 104.992 HFM | 717.4/722.369 | 765.904 |
| 300D | 1975 | 115.114 | 617.910 | 716/722.1 | L1Z |
| 300D | 1976-85 | 123.130 | 617.912 | 716.0/722.1 | 765.706 |

| MODEL | YEARS | CHASSIS | ENGINE | TRANSMISSION | STEERING |
| --- | --- | --- | --- | --- | --- |
| 300D 2.5Turbo | 1988-93 | 124.128 | 602.962 | 717.4/722.4 | 765 |
| 300D Turbo | 1982-85 | 123.130 | 617.952 | 722.3/.4 | 765.706 |
| 300D Turbo | 1985- | 124.133 | 603.960 | 722.3 | LS68 |
| 300E | 1985-92 | 124.030 | 103.983 KE | 717.4/722.3 | 765 |
| 300E | 1993-96 | 124.032 | 104.992 HFM | 722.369 | 765.904 |
| 300E 2.6 | 1985-92 | 124.026 | 103.940 KE | 717.4/722.4 | 765 |
| 300E 2.8 | 1985-93 | 124.028 | 103.942 KE | 717.4/722.4 | 765.904 |
| 300E 4MATIC | 1987-93 | 124.230 | 103.985 KE | 717.4/722.342 | 765.906 |
| 300SD Turbo | 1978-80 | 116.120 | 617.950 | 722.1 | 765.706 |
| 300SD Turbo | 1981-85 | 126.120 | 617.951 | 722.3 | 765.706 |
| 300SD Turbo | 1992-93 | 140.134 | 603.971 | 722.367 | 765.940 |
| 300SDL Turbo | 1985-88 | 126.125 | 603.961 | 722.3 | 765.706 |
| 300SE | 1961-65 | 112 | 189 | GA300SE,-E,-EH | DB |
| 300SE | 1985-92 | 126.024 | 103.981 KE | 717.4/722.351 | 765.706 |
| 300SE | 1992-93 | 140.032 | 104.990 KE | 722.502 | 765.940 |
| 300SE/C | 1961-67 | 112 | 189 | GA300SE,-E,-EH | DB |
| 300SEB | 1965-72 | 108 | 189 | GA300SE-EH | DB |
| 300SEL |  | 109.016 | 130.981 |  |  |
| 300SEL | 1966-68 | 109 | 189 | GA300SE-EH | DB |
| 300SEL | 1985-92 | 126.025 | 103.981 KE | 717.431/722.319 | 765.706 |
| 300SEL 3.5 | 1969-72 | 109.056 | 116.981 | 722.2 | LS75 |
| 300SEL 4.5 | 1971-72 | 109.057 | 117.981 | 722.0 | LS75 |
| 300SEL 6.3 | 1967-72 | 109.018 | 100.981 | K4A050 | LS75 |
| 300SL | 1988-93 | 129.061 | 103 KE | 722.500 | 765.907 |
| 300SL-24 | 1990-92 | 129.061 | 104.981 KE | 722.500 | 765.907 |
| 300TD | 1978-85 | 123.190 | 617.912 | 716.0/722.1 | 765.706 |
| 300TD Turbo | 1981-84 | 123.193 | 617.952 | 722.3/.4 | 765.706 |
| 300TD Turbo | 1985- | 124.193 | 603.960 | 722.3 | LS68 |
| 300TE | 1985-93 | 124.090/.092 | 103.983 KE | 717.4/722.369 | 765.904 |
| 300TE 4MATIC | 1987-93 | 124.290 | 103.985 KE | 717.4/722.342 | 765.906 |
| 350SD Turbo | 1989-6/91 | 126.134 | 603.970 | 722.361 | 765.706 |
| 350SDL Turbo | 1989-6/91 | 126.135 | 603.970 | 722.361 | 765.706 |
| 380SE | 1985-89 | 126.032 | 116.963 | 722.3 | 765.706 |
| 380SEC | 1985- | 126.043 | 116.983 | 722.3 | 765.706 |
| 380SEL | 1980-84 | 126.033 | 116.961 | 722.3 | 765.706 |
| 380SEL | 1985-89 | 126.033 | 116.963 | 722.3 | 765.706 |
| 380SL | 1980-89 | 107.045 | 116.960 | 722.3 | 765.706 |

| MODEL | YEARS | CHASSIS | ENGINE | TRANSMISSION | STEERING |
| --- | --- | --- | --- | --- | --- |
| 380SLC | 1980-89 | 107.025 | 116.960 | 722.3 | 765.706 |
| 400E | 1990-93 | 124.034 | 119.975 LH | 722.354 | 765.921 |
| 400SE | 7/91- | 140.042 | 119.971 LH | 722.3 |  |
| 400SEL | 1992-93 | 140.043 | 119.971 LH | 722.366 | 765.940 |
| 420SEL | 1985-6/91 | 126.035 | 116.965 KE | 722.351 | 765.706 |
| 450SE | 1972-73 | 116.032 | 117.983 | 722.0 | 765.706 |
| 450SE | 1974-80 | 116.032 | 117.986 | 722.0 | 765.706 |
| 450SEL | 1972-73 | 116.033 | 117.983 | 722.0 | 765.706 |
| 450SEL | 1974-80 | 116.033 | 117.986 | 722.0 | 765.706 |
| 450SL | 1971-74 | 107.044 | 117.982 | 722.0 | 765.706 |
| 450SL | 1975-80 | 107.044 | 117.985 | 722.0 | 765.706 |
| 450SLC | 1971-74 | 107.024 | 117.982 | 722.0 | 765.706 |
| 450SLC | 1975-80 | 107.024 | 117.985 | 722.0 | 765.706 |
| 500E | 1993 | 124.036 | 119.974 LH | 722.365 | 765.921 |
| 500SEC | -1992 | 126.044 | 117.965 KE | 722.356 | 765.706 |
| 500SEC | 1992-93 | 140.070 | 119.970 LH | 722.370 | 765.940 |
| 500SEL | 1985-6/91 | 126.037 | 117.963 KA | 722.311 | 765.706 |
| 500SEL | 1992-93 | 140.051 | 119.970 LH | 722.370 | 765.940 |
| 500SL | 1990-92 | 129.066 | 119.960 KE | 722.3 | LSG068 |
| 500SL | 1992-93 | 129.067 | 119.972 LH | 722.364 | 765.907 |
| 560SEC | 1985- | 126.045 | 117.968 KE | 722.350 | 765.706 |
| 560SEL | 1985- | 126.039 | 117.968 KE | 722.350 | 765.706 |
| 6.9 | 1975 | 116.036 | 100.985 | 722.0 | 765.706 |
| 600 | 1964- | 100.012 | 100.980 | K4A050 | LS75 |
| 600 | 1964- | 100 | 100 | GA600 | DB |
| 600 | 1990-93 | 129.076 | 120.981 LH | 722.3 | LSG068 |
| 600 Long 4 Door | 1964- | 100.014 | 100.980 | K4A050 | LS75 |
| 600 Long 6 Door | 1964- | 100.016 | 100.980 | K4A050 | LS75 |
| 600SEC | 1992-93 | 140.076 | 120.980 LH | 722.362 | 765.940 |
| 600SEL | 1992-93 | 140.057 | 120.980 LH | 722.362 | 765.940 |
| 600SL | 1990-93 | 129.076 | 120.981 LH | 722.362 | 765.907 |
| C180 | 1994- | 202.018 | 111.920 PMS | 717.416/722.421 | 765.950 |
| C200D | 1994- | 202.120 | 601.913 | 717.416/722.425 | 765.950 |
| C220 | 1994-96 | 202.022 | 111.961 HFM | 722.423 | 765.950 |
| C220D | 1994 | 202.121 | 604.910 EVE | 717.416/722.426 | 765.950 |
| C230K | 1997-99 | 202.023 | 111.974 ME 2.1 | 722.600 | 765.950 |
| C250D | 1994 | 202.125 | 605.910 ERE | 717.417/722.427 | 765.950 |

| MODEL | YEARS | CHASSIS | ENGINE | TRANSMISSION | STEERING |
| --- | --- | --- | --- | --- | --- |
| C280 | 1994-96 | 202.028 | 104.941 HFM | 722.424 | 765.950 |
| C280 | 1997- | 202.028 | 104.941 HFM | 722.604 | 765.950/765.922 |
| C280 | 1998-99 | 202.029 | 112.920 ME-2.0 | 722.606 | 765.950 |
| C36AMG | 1996-97 | 202.028 | 104.941 HFM | 722.604 | 765.922 |
| C36AMG | 1996-96 | 202.028 | 104.941 HFM | 722.424 | 765.922 |
| C43 AMG | 1998-99 | 202.033 | 113.944 ME 2.0 | 722.631 | 765. |
| CL500 (Coupe) | 1996-97 | 140.070 | 119.980 ME 1.0 | 722.620 | 765.940 |
| CL500 S500 (Coupe) | 1996-97 | 140.070 | 119.970 ME 1.0 | 722.620 | 765.940 |
| CL600 S600 | 1996-98 | 140.076 | 120.982 ME | 722.621 | 765.940 |
| CLK320 (COUPE) | 1998 | 208.365 | 112.940 ME 2.0 | 722.607 | 765.952 |
| E250D | 1992-94 | 124D25 | 602 |  |  |
| E250D Turbo | 1988-95 | 124D25 | 602 |  |  |
| E280 | 1994-95 | 124.028 | 104.942 HFM | 722.433/722.504 | 765.904 |
| E300 | 1994-95 | 124.230 | 103.985 KE | 722.342 | 765.906 |
| E300 TURBO DIESEL | 1998 | 210.025 | 606.982 | 722.608 | 768.002 |
| E300D | 1994-95 | 124.131 | 606.910 | 722.4/722.435 | 765.904 |
| E300D TURBO | 1994-95 | 124.133 | 603.960 | 722.4/722.317 | 765.904 |
| E300D | 1997-99 | 210.020 | 606.912 | 722.600 | 768.003 |
| E300TD TURBO | 1994-95 | 124.193 | 603.960 | 722.4/722.317 | 765.904 |
| E320 | 1994-95 | 124.032/052 | 104.992 HFM | 722.369 | 765.904 |
| E320 | 1996-97 | 210.055 | 104.995 HFM | 722.605 | 768.903 |
| E320 | 1998-99 | 210.065/082/265/282 | 112.941 ME 2.0 | 722.607/664 | 768.002/006 |
| E420 | 1994-95 | 124.034 | 119.975 LH | 722.366 | 765.921 |
| E420 | 1996-97 | 210.072 | 119.985 ME 1.0 | 722.625 | 768.003 |
| E430 | 1998-99 | 210.070 | 113.940 ME 2.0 | 722.623 | 768.002 |
| E500 | 1994-95 | 124.036 | 119.974 LH | 722.370 | 765.921 |
| E55 AMG | 1999 | 210 | 113? ME 2.0 | 722.6 |  |
| ML320 | 1998-99 | 163.154 | 112.942 | 722.662 | ZF.970.402 |
| ML430 | 1999 | 163.1 | 113. ME 2.0 | 722.6 | ZF.970.402 |
| S320 | 1997-98 | 140.033 (Long) | 104.994 HFM | 722.605 | 765.940 |
| S320 | 1997-98 | 140.032 | 104.994 HFM | 722.605 | 765.940 |
| S320 | 1994-96 | 140.032 | 104.994 HFM | 722.508 | 765.940 |
| S320 | 1996 | 140.033 (Long) | 104.994 HFM | 722.508 | 765.940 |
| S350 Turbo Diesel | 1994-95 | 140.134 | 603.971 | 722.367 | 765.940 |
| S420 | 1994-95 | 140.043 | 119.971 LH | 722.366 | 765.940 |
| S420 | 1996-97 | 140.043 | 119.981 ME 1.0 | 722.622 | 765.940 |
| S430 | 1998 | 208. | 113. ME 2.0 | 722.6 |  |

| MODEL | YEARS | CHASSIS | ENGINE | TRANSMISSION | STEERING |
| --- | --- | --- | --- | --- | --- |
| S500 (Coupe) | 1994-95 | 140.070 | 119.970 LH | 722.3 | 765.940 |
| S500 | 1994-95 | 140.051 | 119.970 LH | 722.370 | 765.940 |
| S500 | 1996-98 | 140.051 | 119.980 ME 1.0 | 722.620 | 765.940 |
| S600 | 1996-97 | 140.057 | 120.982 ME 1.0 | 722.621 | 765.940 |
| S600 | 1994-95 | 140.057 | 120.980 LH | 722.362 | 765.940 |
| SL320 | 1994-96 | 129.063 | 104.991 HFM | 722.507 | 765.907 |
| SL320 | 1997 | 129.063 | 104.991 HFM | 722.605 | 765.907 |
| SL500 | 1994-95 | 129.067 | 119.972 LH | 722.364 | 765.907 |
| SL500 | 1996-99 | 129.067 | 119.982 ME 1.0 | 722.620 | 765.907 |
| SL600 | 1994-95 | 129.076 | 120.981 LH | 722.362 | 765.907 |
| SL600 | 1996-98 | 129.076 | 120.983 ME 1.0 | 722.621 | 765.907 |
| SLK230 | 1998-99 | 170.447 | 111.973 ME 2.1 | 722.605 | 765.951 |
| SLK430 | 1999 | 170.4 | 113. ME 2.0 | 722.6 |  |

Mercedes production is generally from July to June. This means that the 1994 model year has production dates 7/93-6/94.

A catalog of tools for all models is available by calling

Baum Tools Unlimited Inc. 800-848-6657 USA/Canada

941-927-1414 International

941-927-1612 Fax

Manuals for most models are available from our Technical Publications division. To order or request a listing call

or visit our website.

or email us at

Baum Tools Unlimited - West 415-566-9229 Voice

415-566-0694 Fax

http://www.baumtools.com

tech@baumtools.com